## Slide 1: WF on UE feature list for RRM and modulation order
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #86 draft R4-1803552
Athens, Greece, 26 February – 2 March 2018
Agenda item: 7.1

## Slide 2: Capabilities for modulation order

## Slide 3: Background
Agreements
  64QAM for PDSCH is mandatory without capability at least for all FR2 bands defined within Rel.15 timeframe
  Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced
  64QAM for PUSCH is mandatory without capability at least for all bands defined within Rel.15 timeframe
  Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced
  256QAM for PDSCH for FR1 is mandatory with Type 4 capability signalling. It can be revisited in the future whether the 256QAM is mandated in all UE types or cateogories.
  If capability signalling is introduced for FR2 256QAM PDSCH and PUSCH (pending on the feasibility study), it shall be type 1 signalling. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers.
  256QAM for PUSCH for FR1 is optional with type 1 capability signalling. RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release.
  pi/2-BPSK for PUSCH is optional
  Type 4 (per UE) with FR1/2 differentiation
  RAN4 will define the same minimum requirements for pulse-shaped pi/2 BPSK and non pulse-shaped pi/2 BPSK for FR2.
  pi/2-BPSK for PUCCH format 3/4 is optional
  Type is same as pi/2-BPSK for PUSCH, i.e. Type 4 (per UE) with FR1/2 differentiation

## Slide 4: Background
Current RAN4 feature list for modulation order part
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
64QAM modulation for FR2 PDSCH | 1) 64QAM modulation for FR2 PDSCH |  | Yes | 64QAM for PUSCH is not possible |  | No need | Applicable only to FR2 |  | Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced | RAN4 | Mandatory without capability | 
64QAM for PUSCH | 1) 64QAM for PUSCH |  | Yes | 64QAM for PUSCH is not possible |  | No need | No need |  | Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced | RAN4 | Mandatory without capability | 
256QAM for PDSCH | 1) 256QAM for PDSCH |  | Yes | 256QAM for PDSCH is not possible | Type4 for FR1 [Type1] if needed for FR2 | No need | Yes |  | For FR1, it can be revisited in the future whether the 256QAM is mandated in all UE types or categories For FR2, FFS on whether type 1 is sufficient considering the number of supporting MIMO layers. | RAN4 | Mandatory with capability for FR1 TBD for FR2 | 
256QAM for PUSCH | 1) 256QAM for PUSCH |  | Yes | 256QAM for PUSCH is not possible | Type1 for FR1 [Type1] if needed for FR2 | No need | Yes |  | For FR1, RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release. For FR2, FFS on whether type 1 is sufficient considering the number of supporting MIMO layers. | RAN4 | Optional for FR1 TBD for FR2 | 
pi/2-BPSK for PUSCH | 1) pi/2-BPSK for PUSCH |  | Yes | pi/2-BPSK for PUSCH is not possible | Type 4 | No need | Yes |  | RAN4 will define the same minimum requirements for pulse-shaped pi/2 BPSK and non pulse-shaped pi/2 BPSK for FR2. | RAN4 | Optional | 
pi/2-BPSK for PUCCH format 3/4 | 1) pi/2-BPSK for PUCCH format 3/4 |  | Yes | pi/2-BPSK for PUCCH format 3/4 is not possible | Type 4 | No need | Yes |  |  | RAN4 | Optional | 

## Slide 5: 256QAM for FR1/FR2 PDSCH
Agreement on Monday
  256QAM for PDSCH for FR1 is mandatory with Type 4 capability signalling. It can be revisited in the future whether the 256QAM is mandated in all UE types or cateogories.
  If capability signalling is introduced for FR2 256QAM PDSCH and PUSCH (pending on the feasibility study), it shall be type 1 signalling. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers.
Agreement on Thursday
  For 256QAM in FR2, the capability signaling type is Type 1. RAN4 will continue to discuss whether to introduce the requirements.
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
256QAM for PDSCH | 1) 256QAM for PDSCH |  | Yes | 256QAM for PDSCH is not possible | Type 4 for FR1 [Type1] if needed Type 1 for FR2 | No need | Yes |  | For FR1, it can be revisited in the future whether the 256QAM is mandated in all UE types or categories For FR2, RAN4 will continue to discuss whether to introduce the requirements. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers. | RAN4 | Mandatory with capability for FR1 TBD for FR2 | 

## Slide 6: 256QAM for FR1/FR2 PUSCH
Agreement on Monday
  If capability signalling is introduced for FR2 256QAM PDSCH and PUSCH (pending on the feasibility study), it shall be type 1 signalling. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers.
  256QAM for PUSCH for FR1 is optional with type 1 capability signalling. RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release.
Agreement on Thursday
  For 256QAM in FR2, the capability signaling type is Type 1. RAN4 will continue to discuss whether to introduce the requirements.
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
256QAM for PUSCH | 1) 256QAM for PUSCH |  | Yes | 256QAM for PUSCH is not possible | Type1 for FR1 [Type1] if needed Type 1 for FR2 | No need | Yes |  | For FR1, RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release. For FR2, RAN4 will continue to discuss whether to introduce the requirements. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers. | RAN4 | Optional for FR1 TBD for FR2 | 

## Slide 7: pi/2-BPSK for PUSCH
Agreement on Monday
  pi/2-BPSK for PUSCH is optional
  Type 4 (per UE) with FR1/2 differentiation
  RAN4 will define the same minimum requirements for pulse-shaped pi/2 BPSK and non pulse-shaped pi/2 BPSK for FR2.
RAN4 also agreed that this feature is optional for FR1, but TBD for FR2 on Friday
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
pi/2-BPSK for PUSCH | 1) pi/2-BPSK for PUSCH |  | Yes | pi/2-BPSK for PUSCH is not possible | Type 4 | No need | Yes |  | RAN4 will define the same minimum requirements for pulse-shaped pi/2 BPSK and non pulse-shaped pi/2 BPSK for FR2. | RAN4 | Optional for FR1 TBD for FR2 | 

## Slide 8: pi/2-BPSK for PUCCH format 3/4
Agreement on Monday
  pi/2-BPSK for PUCCH format 3/4 is optional
  Type is same as pi/2-BPSK for PUSCH, i.e. Type 4 (per UE) with FR1/2 differentiation
RAN4 also agreed that this feature is optional for FR1, but TBD for FR2 on Friday
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
pi/2-BPSK for PUCCH format 3/4 | 1) pi/2-BPSK for PUCCH format 3/4 |  | Yes | pi/2-BPSK for PUCCH format 3/4 is not possible | Type 4 | No need | Yes |  |  | RAN4 | Optional for FR1 TBD for FR2 | 

## Slide 9: Other capabilities

## Slide 10: Background
Current RAN4 feature list for BWP switching delay, 1 symbol GP in unpaired spectrum and Number of Tx antenna port
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
BWP switching delay | 1) Support BWP switching delay specified in TS38.xxx, candidate values set: {type1, type2} |  | Yes | UE does not support BWP switching delay | Type 4 if needed | No need | TBD |  | Network cannot configure the shorter delay for certain UE type RAN4 may remove the capability signaling if RAN4 can agree single minimum delay for each scenario. | RAN4 | TBD | 
1-symbol GP for 120kHz SCS in unpaired spectrum | 1) Slot formats with 1-symbol GP(s) for 120KHz SCS in unpaired spectrum in FR2 2) Slot formats with 1-symbol GP(s) for 60KHz SCS in unpaired spectrum in FR1 |  | Yes | UE does not support 1 symbol GP in unpaired spectrum | Type 4 if needed | Applicable only to TDD | Yes |  | RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15. | RAN4 | TBD | 
[Number of UE TX ports] |  |  |  |  |  |  |  |  | No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week. | RAN4 |  | [Number of UE TX ports]

## Slide 11: BWP switching delay
Agreement on Monday
  Introduce the type 4 capability signaling to differential the type 1 and type 2 for each scenario if the capability signaling is agreed to be introduced. We may remove the capability signaling if RAN4 can agree single minimum delay for each scenario.
Agreement on Thursday
  FR1 and FR2 differential is not needed for BWP switching delay
For this feature, RAN4 approved another LS (R4-1803283) on Friday
Proposed description (Green is agreed part, Red is non agreed part):
Frequency Range | Scenario | Delay (us)(Note) | Comment
1 | 1 | Type 1: 600us Type 2: 2ms | 
 | 2 | Type 1: 600us Type 2: 2ms | 
 | 3 | Type 1: 600us Type 2: 2ms | 
 | 4 | Type 1: 350us Type 2: 950us | No delay required from the RF perspective
2 | 1 | Type 1: 600us Type 2: FFSms | 
 | 2 | Type 1: 600us Type 2: FFSms | 
 | 3 | Type 1: 600us Type 2: FFSms | 
 | 4 | Type 1: 350us Type 2: FFSus | No delay required from the RF perspective
  Note: Network cannot configure the shorter delay for certain UE type
Feature group | Components | Prerequisite feature groups | Need for gNB to know… | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
BWP switching delay | 1) Support BWP switching delay specified in TS38.xxx, candidate values set: {type1, type2} |  | Yes | UE does not support BWP switching delay | Type 4 if needed | No need | No need TBD |  | For this feature, RAN4 also sent another LS (R4-1803283) Network cannot configure the shorter delay for certain UE type RAN4 may remove the capability signaling if RAN4 can agree single minimum delay for each scenario. | RAN4 | TBD | 

## Slide 12: 1-symbol GP in unpaired spectrum
Agreement on Monday
  Capability signaling type for 1-symbol GP for 120KHz SCS in unpaired spectrum will be type 4 for FR2. RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15.
  Capability signaling type for 1-symbol GP for 60KHz SCS in unpaired spectrum will be type 4 for FR1. RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15.
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know… | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-symbol GP in unpaired spectrum | 1) Slot formats with 1-symbol GP(s) for 120KHz SCS in unpaired spectrum in FR2 2) Slot formats with 1-symbol GP(s) for 60KHz SCS in unpaired spectrum in FR1 |  | Yes | UE does not support 1 symbol GP in unpaired spectrum | Type 4 if needed | Applicable only to TDD | Yes |  | RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15. | RAN4 | TBD | 

## Slide 13: Number of Tx ports
Agreement on Monday
  No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week.
Agreement on Thursday
  Feature “Number of Tx ports” is removed
Proposed description (remove this row):
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
Number of UE TX ports |  |  |  |  |  |  |  |  | No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week. | RAN4 |  | 

## Slide 14: Capabilities for RRM

## Slide 15: Background
Current RAN4 feature list for RRM part
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
Independent measurement gap configurations for FR1 and FR2 | 1) measurement gaps for FR1 and FR2 are configured independently |  | Yes | UE does not support independent gap configuration between FR1 and FR2 | Type 4 | No Need | No Need |  |  | RAN4 | Optional | 
Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement | 1) Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement |  | Yes | UE does not support simultaneous reception of data and SS block with different numerologies | Type 4 | No Need | Applicable only to FR1 |  | FFS: inter-band CA case | RAN4 | Optional | 

## Slide 16: Simultaneous reception of data and SS block with different numerologies
Agreements on Monday
  Renamed to “Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement with SSB within the active BWP”
    FFS: inter-band CA case
  Type 4 (per UE) and applicable only to FR1
Agreements on Thursday
  We need FR1 and FR2 differential for the capability of feature “Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement”.
Proposed description (Green is agreed part, Red is non agreed part):
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement with SSB within the active BWP | 1) Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement with SSB within the active BWP |  | Yes | UE does not support simultaneous reception of data and SS block with different numerologies | Type 4 | No Need | Yes Applicable only to FR1 |  | FFS: inter-band CA case | RAN4 | Optional |