## Slide 1: Way forward on higher velocity UE under CEmodeA
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 6.18.4.1
R4-1804727

## Slide 2: Background
We have reached the following agreements in RAN4 #86:
  On gap sharing and higher-velocity operation
    Introduce a new measurement gap sharing table for eFeMTC UEs operating under higher velocity, and the values of the table are FFS.
    Inter-frequency requirements under higher-velocity operation are FFS.
    If higher-velocity indication is received by the efeMTC UE, the UE shall use the measurement gap sharing table associated with higher-velocity.

## Slide 3: Way forward
This way forward is to capture agreements on
  Method for intra-frequency measurement requirement with DRX
DRX cycle length (s) | Tidentify_intra (s) (DRX cycles) | Tmeasure_intra (s) (DRX cycles)
≤0.04 | [0.8] (Note1) | [0.2] (Note1)
[0.04<DRX-cycle≤0.08] | Note2([TBD]) | Note2 ([TBD])
[0.08<DRX-cycle≤1.28] | Note2([TBD]) | Note2 ([TBD])
[1.28<DRX-cycle≤2.56] | Note2([TBD]) | Note2 ([TBD])
Note1: Number of DRX cycle depends upon the DRX cycle in use. Note2: Time depends upon the DRX cycle in use. |  | 

## Slide 4: Way forward
  Define inter-frequency measurement requirement
    Method for inter-frequency measurement requirement with or without DRX
      Reuse R14 inter-frequency cell identification and measurement requirement without DRX
      FFS the inter-frequency measurement requirement with DRX
  An optional UE capability to support higher velocity under eFeMTC CEmodeA is introduced in R15
  Higher velocity UE under eFeMTC CEmodeA is able to report its speed status to the network so that the network can apply proper requirement for the UE.