## Slide 1: Way forward on eFeMTC PUSCH demodulation performance requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20 – 24 August, 2018
R4-1811373

## Slide 2: Way forward on subPRB transmission
RAN4 will specify the demodulation requirements with 2 of 3 sub-carriers pi/2 BPSK
  Companies are encouraged to provide the simulation results in RAN4#88bis according to the simulation assumption given in the next page.

## Slide 3: Simulation assumption for PUSCH with subPRB transmission
Parameter | Value
Number of Tx antennas | 1
Number of Rx antennas | 2
Propagation condition | EPA5
Cyclic prefix | Normal
Fraction of maximum throughput | 70 %
RV sequences | 0,2,3,1,0,2,3,1
Maximum number of HARQ transmissions | 4
Reference receiver | MRC
Channel bandwidth | 3 MHz, 5 MHz, 10 MHz, 15 MHz, 20 MHz
RU size and repetition number | CE Mode A: 1RU without repetitions, TBS=[32]bits CE Mode B: 2RU x 16, TBS=[88]bits
DMRS | Fixed one
Frequency hopping | On

## Slide 4: Information
TBS table for subPRB PUSCH