## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #93
Reno, USA, 18th – 22nd November, 2019 Agenda Item: 9.18.1.1
R4-1915861

## Slide 2: SCS and Channel bandwidth
      Define requirements for FR1 TDD 15 kHz
      CA scenario for testing of FR1 TDD 15kHz
  FR1 inter-band CA with TDD 15 kHz + TDD 30 kHz
  FR1 inter-band CA with TDD 15 kHz + FDD 15 kHz
    TDD 15 kHz + FDD 15kHz CA will be tested only in case UE does not support different SCS on different CCs for TDD-FDD CA scenario (i.e. scenario TDD 30 kHz + FDD 15 kHz).
      Single carrier channel bandwidth for FR1 TDD 15 kHz
  All configurable channel bandwidths
      TDD UL-DL pattern for FR1 TDD 15kHz
  3D1S1U with S=10:2:2

## Slide 3: Test parameters
      Rank and MCS for FR2
  Option 1: rank 2 and MCS 10
  Option 2: rank 1 and MCS 13
  Down-select to one option
      PUCCH group
  one PUCCH group, i.e., A/N feedback on Pcell with no UL CA
      PUCCH format for A/N feedback
  use PUCCH format 1 for no more than 2 DL CCs, and use PUCCH format 3 for more than 2 DL CCs.
      No PUCCH capacity issue

## Slide 4: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
FDD 15 kHz + TDD 30 kHz CA and FDD 15 kHz + TDD 15 kHz CA
  FFS whether requirements will be defined for FDD PCell and TDD Pcell
    If Pcell in both carriers are supported, the performance for FDD Pcell and FDD Scell is similar and the performance for TDD Pcell and TDD Scell is similar, FFS which one is used for the tests.
  HARQ process number for FDD 15 kHz + TDD 30 kHz CA
    Pcell: 4 for FDD and [8 or 10] for TDD
    Scell: FFS
  HARQ process number for FDD 15 kHz + TDD 15 kHz CA: FFS
TDD 15 kHz + TDD 30 kHz CA
  FFS whether requirements will be defined for 15 kHz PCell and 30 kHz Pcell
    If Pcell in both carriers are supported, the performance for 15kHz Pcell and 15 kHz Scell is similar and the performance for 30 kHz Pcell and 30 kHz Scell is similar, FFS which one is used for the tests.
  HARQ process number: FFS

## Slide 5: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
Performance requirements:
  Further discuss whether single carrier requirements from FDD and TDD CA with the same SCS can be reused.
  Companies are encouraged to bring performance analysis in the next meeting

## Slide 6: Test applicability rule
      Test applicability for different CA duplex mode
  Test all the supported CA duplex mode
      Categorizing of CA capabilities
  Option 1: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.
  Option 2: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA
  Other options are not precluded.
  Companies to bring proposals on the demod spec structure for CA, with the motivation to minimize future maintenance.

## Slide 7: Test applicability rule
      Test of different CA capabilities
  Option 1: Test intra-band contiguous CA, Intra-band non-contiguous CA and Inter-band CA with the largest number of bands
  Option 2: Test intra-band contiguous CA, Intra-band non-contiguous CA and Inter-band CA with the largest aggregated CBW
  Option 3: Test all the supported CA capabilities, including intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands
  Option 4: Any one of the supported CA capabilities
  Other options are not precluded.
      Selection of CA configuration(s) and CBW combination
  Further discuss by taking into account:
    The supportedSubCarrierSpacingDL, maxNumberMIMO-LayersPDSCH and supportedModulationOrderDL are reported for each CC and scalingFactor are reported per band for FR1 and FR2.
    The testable SNR for FR2.