## Slide 1: WF on A-MPR requirements for simultaneous PSFCH transmission
Agenda item: 6.4.1
Source: Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #95-e R4-2008440
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background
In RAN4#94e, in order to be aligned with each other, the simulation assumption and parameters for PSFCH are proposed in a WF [1].
In RAN4#94bis-e, MPR for PSFCH was approved based on WF [5]. AMPR will be decided in this meeting.
  Qualcomm and Huawei provided AMPR simulations results for simultaneous PSFCH transmission in RAN4#94bis-e. [2~4]
This WF is proposed to derive the AMPR requirements for simultaneous PSFCH transmission, with 1 PSFCH transmission per RB, considering the worst AMPR values.

## Slide 3: Reference
[1] R4-2002758 WF on MPR/A-MPR simulation assumptions and parameters for simultaneous PSFCH transmission, Huawei
[2] R4-2004201 MPR\AMPR simulation results and discussion for PC3 PSFCH NR V2X in band n47, Huawei, HiSilicon
[3] R4-2003437 A-MPR for 40MHz V2X PSFCH transmission TP, Qualcomm Incorporated
[4] R4-2003439 A-MPR for 10MHz V2X PSFCH transmission TP, Qualcomm Incorporated
[5] R4-2005224 WF on MPR AMPR requirements for simultaneous PSFCH transmission, Huawei, HiSilicon
[6] R4-2007881 TP to TR38.886 A-MPR for 10 and 40MHz V2X PSFCH

## Slide 4: WF on ESTI NS_33 AMPR for PSFCH
Channel Bandwidth, MHz | Carrier Frequency (MHz) | PSFCH A-MPRbase (dB) |  |  | A-MPRstep (dB) | Number of RBs
 |  | 0 ≤ NGap / NRB < 0.15 | 0.15≤ NGap / NRB < 0.3 | 0.3≤ NGap / NRB ≤ 1 |  | 
10 MHz | 5860 | 19 |  |  | 1 | 1
 |  | 22 |  |  | 1 | >1
 | 5870, 5880, 5890, 5900, 5910, 5920 | 5 |  |  | 0.8 | 1
 |  | 14 | 7 | 18.5 | 0.8 | >1
Note 1: NGap is the gap (in units of RBs) between RBstart and RBend for simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation. (NGap = RBend - RBstart) |  |  |  |  |  | 
The additional maximum output power reduction specified as
A-MPR = CEIL {MA, 0.5}
Where MA is defined as follows
MA = A-MPRBase + Gpost_connector * A-MPRStep

## Slide 5: WF on FCC NS_52 AMPR for PSFCH
Channel Bandwidth, MHz | Carrier Frequency (MHz) | PSFCH A-MPR (dB)
40 MHz | 5885 | 23.5

## Slide 6: WF on ESTI NS_New AMPR for PSFCH
Channel Bandwidth, MHz | Carrier Frequency (MHz) | PSFCH A-MPR (dB) |  |  | Number of RBs
 |  | 0 ≤ NGap / NRB < 0.15 | 0.15≤ NGap / NRB < 0.3 | 0.3≤ NGap / NRB ≤ 1 | 
10 MHz | 5860, 5870, 5880, 5890, 5900, 5910, 5920 | 5 |  |  | 1
 |  | 14 | 7 | 18.5 | >1
Note 1: NGap is the gap (in units of RBs) between RBstart and RBend for simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation. (NGap = RBend - RBstart) |  |  |  |  | 
It can be foreseen that only conducted requirements will be specified in the future ETSI regulations. Anyway, RAN4 can further discuss the ESTI NS_New AMPR after ETSI release the updated regulations.
Thus, the additional maximum output power reduction for expected ETSI regulations specified as