## Slide 1: WF on Enabling Transparent TxD in Rel-16
Qualcomm
3GPP TSG-RAN WG4 Meeting # 95-e
Electronic Meeting, 25 May – 5 June, 2020
R4-2008465

## Slide 2: Issue 3-3-1: Summing the power and emissions
Motivation is to define requirements so that power is measured correctly for all implementations
  Option 1: Use “requirements apply to a sum of both connectors”.
    Leaves the testing aspect to RAN5.
  Option 2: Use“measured as sum of each antenna connector”.
    Forces ran5 to implement variable phaseshifter in to the test setups or forces UE to implement S-CDD

## Slide 3: Issue 3-3-2: Unwanted emissions for Transparent TxD: MPR study
Possible WF:
  Simulation/measurement assumptions for MPR study for 2Tx UE’s
    Using Follow 29 dBm WI assumptions in R4-2005190 as baseline
      Two 20dBm Tx chains are not precluded
      Two 23dBm Tx chains are not precluded
      Two 26dBm Tx chains are precluded
MPRs are defined for each power class separately
  PC3 = 2x20dBm
  PC2 = 2x23dBm

## Slide 4: Issue 3-3-2: Unwanted emissions for Transparent TxD: how to write emission requirements
Motivation is to ensure correct requiremen setting for unwated emissions
  Option 1: Define “requirements apply to a sum of both connectors”. Issue 3-3-1 option 1
  Option 2: Define “measured as the sum of the emissions from all antenna connectors”. Same as issue 3-3-1 Option 2
  Option 3: Measured per antenna connector against a 3 dB tighter emissions requirement per connector (for two antenna connectors).
Note for discussion: why not measure the output power in issues 3-3-1 against 3 dB lower than power class per connector?

## Slide 5: Issue 3-3-3: ACLR for Transparent TxD
ACLR is defined as follows
ACLRUE = (PADJ, TX1 + PADJ, TX2) / (POWN, TX1 + POWN, TX2)
  Where
    PADJ, TX1 = power of the adjacent channel on TX port 1
    POWN, TX1 = power of own channel on TX port 1
    And TX2 similarly.
Note for discussion: this covers non equal power split but is neutral if it is allowed or not

## Slide 6: Issue 3-3-4: EVM for Transparent TxD
Agree EVM defined as
Needed changes into the TS are TBD
  Annex F
  6.4D

## Slide 7: Issue 3-3-5: Declaration for default TX connector
Motivation is to clarify what is UE behavior and TE assumptions in RX and BB tests
Narrow down to one of the following in next meeting
  Option 1a: TE needs to detect all antenna connectors for ACK and NACK and any other expected response from UE
  Option 1b: TE needs to detect all declared TX antenna connectors for ACK and NACK and any other expected response from UE
  Option 2: UE declares which connector is primary TX connector from which ACK and NACK and any other expected response from UE is transmitted in aall cases
And send LS to RAN5 about RAN4 conclusion

## Slide 8: Issue 3-3-6: UE behavior under conformance testing
Motivation is to guide how to test requirements that require power changes such as relative power control
  Option 1a: UE will keep the tx diversity status unchanged in conformance testing.
  Option 1b: Test mode signalling is implemented to instruct UE to keep TX div status unchanged
  Option 2: TE will detect and sum for every power step and change in condition from all connector (according to the issue 3-3-5 outcome)

## Slide 9: Issue 3-3-7: Power splitting behavior
Motivation is to discuss and agree what implementations are excuded
  Option 1: Only allow equal power split between connectors
    Excludes 17+17+20 dBm implementations
    Excludes power control optimizations
  Option 2: Allow any power split between connectors
Note for discussion
  RAN1 language mandates UE to split power equally between logical antenna ports. This allows 17+17 dBm = port 1 and 20 dBm = port 2 case
  What is the motivation for RAN4 to disallow this? Or power optimization for example for 24 dBm output power realization 23 + 17 dBm for maximized efficiency?