## Slide 1: WF on Applicability of DL interruption for Tx switching
3GPP TSG-RAN WG4 Meeting #95e
Electronic Meeting, 25 May - 5 June, 2020
Agenda: 6.13.1.5
R4-200xxxx
China Telecom

## Slide 2: Background
Approved WFs on RF requirements for Tx switching in the previous meetings
  R4-1913041, RAN4 #92bis
  R4-1916084, RAN4 #93
  R4-2002815, RAN4 #94e
  R4-2005664, RAN4 #94e-bis

## Slide 3: Background on Applicability of DL interruption
  RAN4 #94e-bis Agreement in RF session(R4-2005664):
  Define different capabilities for UEs with and without DL interruption
    Whether to allow DL interruption for each band combination can be discussed later after the signaling for DL interruption is defined.
  RAN4 #94e-bis Agreement in RRM session (R4-2005416):
  If the DL interruptions are allowed and the DL interruption applicability is agreed to be captured in RF specification, RRM can directly refer to RF spec. Otherwise, the DL interruption applicability is captured in RRM spec.

## Slide 4: Background: companies’ positions at RAN4 #95e
For EN-DC:
  Option 1: DL interruptions due to UL Tx switching are not allowed for any EN-DC band combinations. (Nokia)
  Option 2: DL interruptions are only allowed for band combinations where it is difficult to avoid DL interruptions in practical UE implementations. (Huawei, MTK, CTC, KDDI, OPPO, ZTE)
  Option 3: DL interruptions on any band combinations with UE capability indication should be allowed (Apple, OPPO, ZTE, vivo, MTK)
For UL CA:
  Option 1: DL interruptions are only allowed for band combinations where it is difficult to avoid DL interruptions in practical UE implementations. (Nokia, MTK, CTC, HW, KDDI, OPPO, ZTE)
  Option 2: DL interruptions on any band combinations with UE capability indication should be allowed (HW, Apple, OPPO, ZTE, vivo, MTK)

## Slide 5: WF on Applicability of DL interruption for different band combinations
For EN-DC: continue discussing the following options at RAN4 #96e
  Option 1: DL interruptions due to UL Tx switching are not allowed for any EN-DC band combinations.
  Option 2: DL interruptions are only allowed for band combinations where it is difficult to avoid DL interruptions in practical UE implementations.
    Encouarge chipset and UE vendors to feedback if DL interruption can be aovided for the band pairs for in slide #7.
  Option 3: DL interruptions on any band combinations with UE capability indication should be allowed
For UL CA: continue discussing the following options at RAN4 #96e
  Option 1: DL interruptions are only allowed for band combinations where it is difficult to avoid DL interruptions in practical UE implementations.
    Encouarge chipset and UE vendors to feedback if DL interruption can be avoided for the band pairs for in slide #7.
  Option 2: DL interruptions on any band combinations with UE capability indication should be allowed

## Slide 6: Capture of the applicability on DL interruption
Option 1: Specify in RRM spec for which band combinations DL interruptions are allowed.
Option 2: Capture to TS38.101-1 and TS38.101-3

## Slide 7: Interested band pairs from operators for FDD+TDD CA and FDD+TDD EN-DC (for information)
  Band (n)1 + Band n78 (CTC, CU, KDDI, CHTTL)
  Band (n)3 + Band n78 (CTC, CU, KDDI, CHTTL)
  Band (n)1 + Band n77 (KDDI)
  Band (n)3 + Band n77 (KDDI)
  Band (n)18 + Band n77 or n78 (KDDI)
  Band (n)28 + Band n77 or n78 (KDDI)
  Band (n)3 + Band n41 (CMCC)
  Band (n)3 + Band n79 (CMCC, docomo)
  Band (n)8 + Band n41 or n79 (CMCC)
  Band (n)8 + Band n77 or n78 (SoftBank)
  Band 11 + Band n77 or n78 (SoftBank)
  Band (n)5 + Band n78 or n79 (docomo)
  Band 19 + Band n78 or n79 (docomo)
  Band 21 + Band n78 or n79 (docomo)
  Band (n)1 + Band n79 (docomo)

## Slide 8
Thanks!