## Slide 1: WF on BC based on SSB
Huawei, HiSilicon, [ ]…
R4-200XXXX
3GPP TSG-RAN WG4 #95-e
May 25th – June 5th, 2020
Electronic meeting

## Slide 2
WF1: Beam correspondence requirement based on SSB-only
Whether and how much performance relaxation, ∆p, relative to the condition which assumes both SSB and CSI-RS are present, is necessary
  Alt 1: ∆p = 0 dB
    Will have impact on SSB searching efficiency
  Alt 2: 0 < ∆p ≤ 3 dB
Note for discussion：A common understanding has emerged that it is up to UE implementation how to refine the UE beam based on SSB, with one company providing an example algorithm of hierarchical beam refinement. Other companies have argued that this implementation choice is not required by the specification.

## Slide 3
WF2: Applicability rule for peak direction
Applicability rule for peak direction:
  Alt 1: Applicable for both ∆p = 0 dB and ∆p > 0
  restrict the side condition applicability only to the Rel-16 beam correspondence enhancement, and all of the remaining FR2 RF requirements in Rel-16 shall continue to be defined based on the Rel-15 side conditions (i.e. both SSB and CSI-RS signals are present during beam peak search and spherical coverage measurements).
  Alt 2: Applicable for both ∆p = 0 dB and ∆p > 0
    If a UE meets beam correspondence requirements either based on SSB or based on CSI-RS, it is considered to have met the beam correspondence requirements based on SSB and CSI-RS.
    If a UE meets beam correspondence requirements based on SSB, it is considered to have met the beam correspondence requirements based on CSI-RS.
    The single beam peak direction for other UL tests shall be determined by the single Rel-16 BC which is to be tested according to applicability rule
  Alt 3: Applicable for both ∆p = 0 dB
  If UE support eBC in Rel-16 and passes the requirements, then the BC requirement in Rel-15 will be skipped
  Alt 4: Applicable for both ∆p = 0 dB and ∆p > 0
  Tx requirements other than BC only need to be tested once, regardless whether Rel-16 BC is same to Rel-15 BC or not. For UEs supporting Rel-16 BC, all other Tx requirements is tested with beam peak or TRP derived by Rel-16 BC and skip Rel-15 tests if beam correspondence requirements are same for Rel-16 and Rel-15, otherwise, only test with beam peak or TRP derived by Rel-15 BC.
  Note for discussion: Alt3 and Alt4 are in the same principle, Alt4 provide how to handle with ∆p > 0

## Slide 4: WF 3: Test case applicability
Further refinement of the agreement “Rel-15 BC test is declared automatically passed if a UE passes Rel-16 BC test using the same SSB configuration and SNR as in Rel-15” in WF R4-2005735
  Alt 1
  If RAN4 agrees to introduce beam correspondence based on SSB with relaxation, Rel-15 tests cannot be skipped since the performance is different between Rel-15 and Rel-16.
  If no relaxation is defined, Rel-16 BC can only be declared by UE with bit 1 in Rel-15, otherwise, Rel-16 BC and Rel-15 BC are independent capability can be declared by both bit 0 and bit 1 UE.
  Alt 2
  If a UE meets beam correspondence requirements either based on SSB or based on CSI-RS, it is considered to have met the beam correspondence requirements based on SSB and CSI-RS.
  If a UE meets beam correspondence requirements based on SSB, it is considered to have met the beam correspondence requirements based on CSI-RS.

## Slide 5
WF 4: SSB periodicity
SSB periodicity
Alt 1: RAN4 revisits the SSB periodicity =20ms for SSB based BC. Suggest SSB periodicity = 5ms to reduce the test time in RRC connected mode
Keep SSB periodicity =20ms for SSB based BC, which reflects the real network configuration

## Slide 6
Reference
[1] R4-2008952, “email discussion summary on NR FR2 UE RF part 2”, Apple