## Slide 1: Remaining Issues in 6.14.1.3
[95e][123] NR_RF_FR2_req_enh_Part_3
Intra-band non-cont DL CA for BW larger than 1400 MHz
3GPP TSG-RAN WG4 Meeting # 95-e R4-200XXXX
Electronic Meeting, 25 May – 5 June 2020 2 June 2020

## Slide 2: Major remaining differences in Cat B CRs
 | R4-2006634 (revised to R4-2008485) | R4-2008483 | Moderator Comment | Resolution
Items from other agenda items |  | Phrase containing [ and inter-band with bands in the same band group] | This phrase can be entered through Cat B CR of DL inter-band CA if agreed in that agenda | Go with 6634
Capability reporting | UE reports Fsd parameter only if it relies on DL-only spectrum for eDLCA | UE reports something new whether or not it relies on DL-only spectrum for eDLCA | Majority view is captured in 6634 | In 6634, the current form is ok, while in the LS to mention besides Fsd, there could be some other info that UE may need to report such as whether or not it relies on DL-only spectrum
New frequency separation classes, relative to smallest Rel-15 (800 MHz) | None smaller | Introduces 400 MHz, 600 MHz classes |  | Go with 6634

## Slide 3: Relaxation in REFSENS for intra eDLCA
If time allows, discuss relaxation value for 2400 MHz
  One opposing company, no value proposed in this meeting by them
Cumulative Aggregated Channel BW (MHz) | ΔRIB (dB)
≤ 800 | 0.0
> 800 and ≤ 1400 | 0.5
…. | …
<? and ≤ 2400 | 1.0