## Slide 1: WF on NR Mobility Enhancements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #95-e R4-2008585
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2009020 Email discussion summary for [95e][208] NR_Mob_enh_RRM
Agreements in the last RAN4#94-e-bis meeting can be found in:
  R4-2005392 Email discussion summary for [94e Bis][108] NR_Mob_enh_RRM
  R4-2005305 WF on NR Mobility enhancement RRM requirements

## Slide 3: DAPS handover: Agreement in 1st round
Issue 1-4 Definition of asynchronous DAPS HO for intra-frequency or intra-band scenarios shall be based on:
Agreement: If side condition for sync is not met, async DAPS HO is assumed. (agreement in RNA4#94-e-bis)
Issue 1-5 Additional note for sync condition:
Agreement: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot. (agreement in RNA4#94-e-bis)
Issue 1-6 Response to RAN1 LS (R1-2003058):
Agreement: RAN4 doesn’t need to reply RAN1 LS
Issue 1-7 LS to RAN2 on misalignment between RAN2 and RAN4 on the following capabilities:
Agreement: Since RAN2 is already aware of this, it is not necessary to send this LS.

## Slide 4: DAPS handover: way forward for 2nd round
Issue 1-1: interruption requirements for async intra-frequency DAPS HO.
Agreement: one more slot of interruption is allowed compared to sync scenario
Issue 1-2: interruption requirements for async intra-band inter-frequency DAPS HO.
Agreement: one more slot of interruption is allowed compared to sync scenario

## Slide 5: DAPS handover: way forward for 2nd round
Issue 1-3: definition of synchronous DAPS HO for intra-frequency or intra-band scenarios shall be based on:
Option 1: 3 us MRTD and 5.21 us MTTD between source and target cells.
    Note: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
Option 2: 6 us MRTD and 7.6 us MTTD between source and target cells.
    Note 1: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
    Note 2: A UE is not expected to transmit in the uplink earlier than after the end of the last received downlink symbol in the same cell where is given by Table below.
    Note 3: A UE is not expected to receive in the downlink earlier than after the end of the last transmitted uplink symbol in the same cell where is given by Table below.
Transition time | FR1 | FR2
 | 25600 | 13792
 | 25600 | 13792
Transition time | FR1 | FR2
 | 25600 | 13792
 | 25600 | 13792

## Slide 6: Test case list for DAPS HO and CHO
Applicability rule: the UE only supporting sync DAPS HO is not required to test async cases.
Whether additional test cases are needed can be further discussed and decided in RAN4#96-e
Test case number | Test purpose | Description | Responsible company
1 | Intrafrequency DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Qualcomm
2 | Interfrequency DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Intel
3 | Conditional intrafrequency handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Ericsson
4 | Conditional interfrequency handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Ericsson
5 | Interfrequency DAPS handover test in SA for FR1-FR2 | See table in section 4.5 in R4-2009020 | 
6 | Conditional intrafrequency handover test in SA for FR2 | See table in section 4.5 in R4-2009020 | Ericsson
7 | Conditional interfrequency handover test in SA for FR2 | See table in section 4.5 in R4-2009020 | Ericsson