## Slide 1: WF on CSI-RS based L3 measurement capability and requirements
OPPO, [ CATT ]
3GPP TSG-RAN4 Meeting #95e
Electronic Meeting, 25 May– 5 June, 2020
R4-2009009

## Slide 2: Background
Agreement in last meeting (R4-2005357)
  Requirements shall be defined when CSI-RS is configured with an associated SSB.
    No requirements in Rel-16 for the case associatedSSB is not configured for CSI-RS
  The total number of carrier UE shall be capable of monitoring at least 13 effective carrier frequency layers
  Introduce restrictions about time-domain scheduling for CSI-RS resources
  CSI-RS based cell identification can consider
    1) Cell search via SSB, 2) PBCH decoding and 3) CSI-RS measurement.
    If configured SSB fails to be detected, requirement should not be defined.
  If the CSI-RS is QCL-ed to the associated SSB, no Rx sweeping is needed only after SSB has been detected.
  If CSI-RS configured with associated SSB but not QCL-ed to the associated SSB, Rx sweeping is needed.
    FFS on the scaling factor N =8.
  For FR2, if the RX beam sweeping for QCL-ed associatedSSB is not finished, requirement should not be applied.
  No UE requirement is defined for the CSI-RS resources that are not within DRX on-duration or measurement gap

## Slide 3: Agreement
    Scope of Requirements
Define requirements only for intra-f without gap and inter-f with gap in Rel-16.
No requirements shall be defined in Rel-16 for CSI-RS L3 measurement, when
      associated SSB is not configured
      associated SSB is not detected even if associated SSB is configured
      associated SSB is not included in ssb-ToMeasure in SSB-ConfigMobility in the same MO.
    UE is not required to perform CSI-RS based L3 measurement when associated SSB is not QCLed with CSI-RS
      No RX beam sweeping is needed when CSI-RS is QCL-ed to the associated SSB
    UE capability of CSI-RS resource to be monitored per slot
The total number of CSI resources that UE can monitor per slot is indicated by existing capability maxNumberCSI-RS-RRM-RS-SINR.
  No requirements when number of configured CSI-RS resources per slot exceeds the indicated UE capability.
  UE capability of simultaneous reception of CSI-RS of neighbour cell and SSB of serving cell
  Introduce new UE capability to indicate the simultaneous reception of CSI-RS of neighbour cell and SSB of serving cell

## Slide 4: Agreement on topic#1: measurement capability
CSI-RS measurement capability requirements are defined based on per frequency layer
  one MO with CSI-RS is identical to 1 CSI-RS frequency layer. Different MOs are different frequency layers.
  CSI-RS and SSB for mobility configured in the same MO are counted as [2] layers
  When associatedSSB is configured, the UE is supposed to monitor not only the frequency layer of the CSI-RS resource, but also the frequency layer of the associatedSSB which is indicated via ssbFrequency.
UE shall be able to measure at least
  1 SSB intra-frequency layer and [1] CSI-RS intra-frequency layer per serving cell
  7 SSB inter-frequency layers and 7 CSI-RS inter-frequency layers
  [8] NR inter-frequency layers including SSB and CSI-RS in total, and 13 NR inter-frequency and inter-RAT layers in total
The number of SSB frequency layers is the total number of “carrier frequencies” including
  Ssbfrequency when ssb-ConfigMobility is configured
  Ssbfrequency when CSI-RS-ResourceConfigmobility is configured with associatedSSB
  the ssbfrequency is counted only once if the ssbfrequency in above bullets are the same, or ssbfrequency in multiple MOs are the same.
During each layer 1 measurement period, the UE shall be capable of performing SS-RSRP, SS-RSRQ, SS-SINR, CSI-RSRP, CSI-RSRQ and CSI-SINR measurements for at least:
  8 identified cells for FR1, and 6 identified cells for FR2 , for each intra-frequency layer
  4 identified cells for FR1, and 4 identified cells for FR2, for each inter-frequency layer
The number of CSI-RS resource/beams to be monitored for UE shall be at least
  [32] CSI-RS resources for intra frequency measurements in FR1, [32] CSI-RS resources for intra frequency measurements in FR2,
  [7] CSI-RS resources for inter frequency measurements in FR1, [10] CSI-RS resources for inter frequency measurements in FR2.
Per FR2 band, intra-frequenct CSI-RS measurement for neighbour cells is only required for PCell/PSCell or one of SCell if there is no PCell/PSCell on that band. UE shall also be capable of at least 2 SSBs and 2 CSI-RS resources on serving cell per CC in the same band.

## Slide 5: Agreement on topic#2: measurement requirements
    Cell identification and measurement period
    For both CSI-RS intra and inter-frequency measurement, CSI-RS based cell identification comprises SSB-based cell identification and CSI-RS based measurements period, where SSB-based cell identification is the same as the cell identification for SSB-based measurement.
      TPSS/SSS_sync_intra and TSSB_time_index_intra can be reused for the case that cell search via SSB and PBCH decoding are needed.
    If UE already detects the SSB of the target cell and deriveSSB-IndexFromCell is indicated, UE can skip PBCH decoding.
    FFS: whether to introduce 2 different requirements for with index and without index.
    For CSI-RS intra-frequency measurement,
    T CSI-RS_identify_intra_with_index = (TPSS/SSS_sync_intra + T CSI-RS_measurement_period_intra + TSSB_time_index_intra) ms
      Reuse [5] samples for intra-frequency measurement period.
    For inter-frequency CSI-RS measurement,
    T CSI-RS_identify_inter_with_index = (TPSS/SSS_sync_inter + T CSI-RS_measurement_period_inter + TSSB_time_index_inter) ms
      Reuse the values of SSB samples for inter-frequency measurement period.
      The tuning time of inter-frequency GAP of CSI-RS measurement shall be equal to the gap switch time for measuring the inter-frequency SSBs.
    Scheduling restriction
    When UE is not able to support mixed numerology of data and CSI-RS L3 mobility, or when UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit or receive on 2 data OFDM symbols impacted by CSI-RS resource symbols to be measured
    when UE performs RX beam sweeping, UE is not expected to transmit or receive 1 data symbol before and after CSI-RS symbol to be measured due to Rx beam sweeping.
    Do not define CSI-RS measurement requirements for the collision case between L1 measurement of serving cell and CSI-RS L3 measurement of neighbour cell

## Slide 6: WF on issue 1-5-3 and 1-6-1
Issue 1-6-1: Whether and how to introduce time-domain restriction on CSI-RS resources configuration
  Option 1: introduce restriction when defining requirements in RAN4 other than introducing new signaling due to time limit.
  Option 2: introduce CMTC
  Option 3: Limit CSI-RS resources to be confined in the SMTC duration of the same MO.
  Option 3a: send LS to RAN1/2 whether and how CSI-RS time domain can be restricted by SMTC of the same MO
Issue 1-5-3: Whether or not to introduce new UE capability for minimum separation between two slots with CSI-RS resources
  Option 1(No): CSI-RS resources in any two consecutive slots are separated by at least 7 symbols.
  Option 2(YES): Introduce a UE capability on the minimum separation between two consecutive slots with CSI-RS resources in the unit of [n]*125us. (multiples of FR2 slot duration, where n=1,2,4,8,16)
  Option 3(FFS): Clarify how it is related to time domain limitation
  Time domain restriction of CSI-RS resource configuration
  Confine CSI-RS resources within SMTC of the associatedSSB and the corresponding periodicity of SMTC should no more than 40ms In R16. FFS introduce CMTC in R17.
  Time domain restriction on CSI-RS resources configuration is introduced:
      CSI-RS resources are configured in 5ms window
      CSI-RS periodicities for L3 measurement : [10,20,40] ms
      Up to [2] CSI-RS periodicities can be configured per CSI-RS intra-frequency layer
      Up to [1] CSI-RS periodicity can be configured per CSI-RS inter-frequency layer
  Tentative agreement：

## Slide 7: WF on CSSF
Option 1:
  All CSI-RS in the same MO should follow the same time-domain relation with gap, e.g., either fully overlapped with gap, partially overlapped with gap or fully non-overlapped with gap
Option 2:
  If additional dedicated searcher is assumed for CSI-RS measurement, no impact on existing CSSF defined for SSB based measurement specified in 38.133.
  Otherwise, the CSSFs for FR1/FR2 SCC shall be updated by considering the CSI-RS based intra-frequency and inter-frequency measurement without gap and within gap respectively.
Option 3:
  If a UE is configured with both CSI-RS-Resource-Mobility and ssb-ConfigMobility in one MO, the CSSF calculation shall consider SSB MO and CSI-RS MO.

## Slide 8: Reference
R4-2005357, WF on CSI-RS based L3 measurement capability and requirements, OPPO
R4-2008515, Email discussion summary for [95e][226] NR_CSIRS_L3meas_RRM_2, OPPO
R4-2009038, Email discussion summary for [95e][226] NR_CSIRS_L3meas_RRM_2, OPPO