## Slide 1: 3GPP TSG-RAN WG4 Meeting #95-e Electronic Meeting, May 25th – June 5th 2020
Huawei, HiSilicon
WF on RRM requirements for R16 enhancement for NB-IoT
R4-2009242

## Slide 2: Filtering and combination of NRSRP samples between anchor carrier and non-anchor carriers
There is no prerequisite or condition for UE in enhanced coverage when filtering the measurement between anchor and non-anchor carriers.
NRSRP measurements on non-anchor carrier can be filtered or combined with NRSRP measurement on anchor carrier after translating the non-anchor carrier measurement with parameter nrs-PowerOffsetNonAnchor, provided that
  SINR ≥ -6 dB on the non-anchor carrier
  the comparison of NRSRP samples between anchor and non-anchor carrier accounting for the signal power offset, yields a difference within a margin M dB

## Slide 3: Filtering and combination of NRSRP samples between anchor carrier and non-anchor carriers
If the measurement samples for comparison satisfy the inequality, UE is allowed to perform RRM measurements on the non-anchor carrier until the next comparison takes place or until the relaxed monitoring criteria is no longer met
| NRSRPanchor – (NRSRPnon-anchor + nrs-PowerOffsetNonAnchor) | < M dB
The value of the margin M = 10 dB
The periodicity of NRSRP comparison is at least once every one hour
For comparison the number of samples for non-anchor carrier is same as number of samples for anchor carrier