## Slide 1: WF on UE demodulation and CSI reporting requirements for FR2 DL 256QAM
China Telecom
3GPP TSG-RAN4 Meeting #95e
Electronic Meeting, 25 May - 5 June, 2020
Agenda item: 6.12.4
R4-2008817
Document for: Approval

## Slide 2: Background: WF in previous meeting
RAN4 #94e-Bis
  WF: R4-2005531

## Slide 3: PDSCH Demodulation: Main Parameters
  Tx EVM
  3% (CTC, Intel, Huawei, QC, DCM, Ericsson)
  Rx impairment modelling and band agnostic requirements
  The following scenarios can be considered for band agnostic requirements definition; and FFS for other scenarios
    Static channel mode: MCS 20-23, rank 1
    TDL-D channel mode: MCS 20-21, rank 1
    TDL-A channel mode: MCS 20-21, rank 1
  FFS on whether to explicitly model Rx impairment until the next meeting
  Rank
  Option 1: Rank 1 (Huawei, QC, Ericsson, CTC, Intel)
  Option 2: Define requirements for Rank 1, FFS on whether to define requirements for rank 2 (CTC, DCM)
  Option 3: Define requirements for single Rank configuration, i.e., either rank1 or rank 2 (Intel)

## Slide 4: PDSCH Demodulation: Main Parameters cont’d
  Channel bandwidth and PRB allocation
  Option 1: 100MHz CBW with full PRB allocation (Ericsson)
  Option 2: 100MHz CBW with partial PRB allocation
  Option 3: 50MHz CBW with full PRB allocation (Intel, Huawei, CTC, DCM)
  Propagation condition
  Option 1: Fading channel (QC, CTC, DCM, Ericsson)
    Option 1A: TDLA30-300
    Option 1B: TDLD30-75
    Option 1C: TDLD30-35
  Option 2: Static channel (Intel)
  TBD in the next meeting based on more companies’ simulation results.

## Slide 5: PDSCH Demodulation: Main Parameters cont’d
  MCS
  MCS 20 for rank 1, if requirements for rank 1 are to be defined.
  FFS for rank 2
  MIMO configuration
  Option 1: 2Tx 2Rx ULA low (Ericsson)
  Option 2: 1Tx 2Rx
  Option 3: Depend on the agreement on propagation condition. Use 2Tx 2Rx ULA low if it is agreed to use fading channel, and use 1Tx 2Rx if it is agreed to use static channel. (Intel, QC, CTC, DCM, Huawei)

## Slide 6: PDSCH Demodulation: Other Parameters
  DM-RS configuration
  Type 1 single symbol front loaded, 1 additional DMRS (CTC, Intel, Huawei, QC, Ericsson)
PRB bundling size and Precoding model
  Option 1:
    PRB bundling size: 2
    Precoding model: Random Precoding, per slot , WB granularity
  Depend on the agreement on propagation condition. Use option 1 if it is agreed to use fading channel; and TBD if it is agreed to use static channel (QC, CTC, Huawei, [E///])
  HARQ process number
  8 (Huawei, QC, CTC, DCM, Ericsson)

## Slide 7: Agreed simulation parameters in previous meeting
Parameter | Unit | Value
SCS | kHz | 120
PT-RS configuration |  | per 2PRB in frequency domain per symbol in time domain
Overhead for TBS determination |  | 6
PDSCH mapping type |  | Type A
TDD Configuration: |  | DDDSU, S=10D:2G:2U
PDCCH duration |  | Symbol #0 in each slot
PDSCH configuration |  | Full DL slots: Start symbol 1, Duration 13 Special slots: Start symbol 1, Duration 9
SSB configuration |  | Periodicity 20 ms, Allocated in first slot within 20ms
TRS configuration |  | 20 ms periodicity, 2 slots, Offset 10 ms
HARQ RV sequence |  | {0, 2, 3, 1}
Receiver assumption |  | MMSE-IRC
Test metric |  | 70% of max TP

## Slide 8: SDR Requirements
In the next meeting, decide whether to define SDR requirements for FR2 256QAM, based on more simulation results and analysis for testable SNR
  If it is agreed to define SDR requirements, consider the following test parameters:
  MCS and rank
    Option 1: Add MCS indexes 26, 21, 20 and 11 in MCS table 2 for both 1 and 2 MIMO layers. Run simulations for MCS 20 to MCS 26 in MCS table 2 to derive the required SNR achieving 85% of peak throughput under AWGN conditions. (China Telecom)
    Other options are not precluded.

## Slide 9: CQI reporting Requirements
In the next meeting, decide whether to define FR2 CQI reporting requirements for CQI table 2
If it is agreed to define FR2 CQI reporting, consider the following test parameters:
  Propagation condition
    Option 1: Cover both AWGN and fading conditions
    Other options are not precluded
  SNR testing point
    Option 1: Cover higher SNR testing point compared to that in Rel-15 FR2 CQI tests
    Other options are not precluded
  Other parameters
    Option 1: Reuse the assumptions in Rel-15 FR2 CQI tests
    Other options are not precluded