## Slide 1: WF on NR-U RRM Requirements (Part 2) (All agreements in RAN4#94e in email thread #205)
MediaTek inc.
3GPP TSG-RAN WG4 Meeting #94e R4-2008567
Electronic Meeting, May 25 - June 5, 2020
Agenda Items: 6.1.5.2, 6.1.5.8, 6.1.5.9, 6.1.5.10, 6.1.5.13

## Slide 2
Agreements from the 1st round
Agreement from GTW session
Agreements from the 2nd round

## Slide 3: Topic #1: Cell re-selection (AI 6.1.5.2)
Definition of unavailable SMTC/SSB
  Wait for RAN1 feedback
Definition of Ms
  Wait for RAN1 feedback
Max number of unavailable SMTC occasions during measurement before UE detects the cell again
  For a cell that is already identified, after N unsuccessful measurement attempts due to exceeding the max number of unavailable SMTC occasions, UE needs to detect the cell again.
    N = 2 or 3
Whether to consider LBT failure in Ttarget_cell_SMTC_period in the paging interruption requirements
  Ttarget_cell_SMTC_period dose not consider LBT failure

## Slide 4: Topic #3: Active BWP switching (AI 6.1.5.9)
The ending point of UL BWP switching delay upon detection of consistent UL LBT failure
  Option 1: UE is ready to transmit RACH
  Option 2: UE transmits RACH
  Option 3: The UE shall be able to transmit PRACH on the new UL BWP of the SpCell on the first available UL slot occurs right after slot n+TBWPswitchDelay +1, where TBWPswitchDelay is defined in Table 8.6.2-1
Whether to introduce any non-overlapping condition for the old and new UL BWPs
  No condition to be added on the relative frequency location of new UL BWP when UE is performing UL BWP switching upon detection of consistent UL LBT failure.

## Slide 5: Topic #4: RLM and link recovery procedures (AI 6.1.5.10)
The set of SSBs that UE is required to monitor
  Wait for RAN1 feedback
Whether UE is able to distinguish the unavailable RLM-RS in low SNR in NR-U
  Option 1: UE is not able to distinguish the unavailable RLM-RS for Es/Iot ≤ -7dB in NR-U
  Option 2: UE is not able to distinguish the unavailable RLM-RS for Es/Iot ≤ -XdB in NR-U. X is FFS based on simulation results.
Availability of Q factor
  Except for initial access, Q factor is always known to UE.
CSI-RS based CBD requirement
  RAN4 start to discuss CSI-RS based BFD requirement after RAN1 conclude on CSI-RS validation

## Slide 6: Topic #4: RLM and link recovery procedures (AI 6.1.5.10)
SSB-based OOS evaluation period
  For SINREST ≤ X dB the OOS evaluation period
    Option 1: Keep unchanged
    Option 2: Fixed extension of number of samples as follows:
      L = TBD for max(TSSB, TDRX) ≤ 40,
      L = TBD for 40 <Max(TDRX, TSSB)≤320
      L = TBD for TDRX >320
  For SINREST > X dB the OOS evaluation period is FFS
  X = [-7dB]
  SINREST is the estimated SINR at the UE side
    Option 1: Filtered SINR estimate over evaluation period
    Option 2: Current SSB SINR estimate
    Option 3: last available SSB SINR
    Other options are not precluded

## Slide 7: Topic #4: RLM and link recovery procedures (AI 6.1.5.10)
CSI-RS based RLM requirement
  Continue discussion in #96e meeting
SSB based BFD requirement
  Wait for the conclusion of SSB based OOS requirement
CSI-RS based BFD requirement
  RAN4 start to discuss CSI-RS based BFD requirement after RAN1 conclude on CSI-RS validation.
CSI-RS based CBD requirement
  RAN4 start to discuss CSI-RS based BFD requirement after RAN1 conclude on CSI-RS validation.

## Slide 8: Topic #4: RLM and link recovery procedures (AI 6.1.5.10)
SSB based CBD requirement
  Set the SSB based CBD evaluation period for NR-U as follows
  If LCBD > LCBD,max, UE behavior is same as the case UE cannot find any candidates.
Configuration | TEvaluate_CBD_CBD (ms)
non-DRX, DRX cycle ≤ 320ms | Max(25, ceil((3+LCBD)*P) * TSSB)
DRX cycle > 320ms | ceil((3+LCBD) *P) * TDRX
Note 1: TDRS is the periodicity of DRS in the set . TDRX is the DRX cycle length. Note 2: LCBD is the number of SSBs not available at the UE during TEvaluate_CBD_SSB where LCBD ≤ LCBD_max. Note 3: LCBD,max=7 for Max(TDRX,TSSB) ≤ 40ms where TDRX=0 for non-DRX, LCBD_max=5 for 40ms < Max(TDRX, TSSB) ≤ 320ms, and LCBD_max=3 for TDRX > 320ms. | 
Configuration | TEvaluate_CBD_CBD (ms)
non-DRX, DRX cycle ≤ 320ms | Max(25, ceil((3+LCBD)*P) * TSSB)
DRX cycle > 320ms | ceil((3+LCBD) *P) * TDRX

## Slide 9: Topic #5: Timing (AI 6.1.5.13)
Definition of “reference cell is available”
  Wait for RAN1 feedback
If a reference cell on a carrier frequency belonging to the PTAG/STAG, which is subject to CCA, is unavailable at the UE for more than 160 ms then the UE is allowed to use any of available activated SCell(s) at the UE in PTAG/STAG as a new reference cell