## Slide 1: WF on R16 NR RRM enhancements – CGI reading
ZTE
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May. 20th – Jun. 5th 2020
R4-2008685

## Slide 2: Agreements in the meeting
MIB decoding delay for FR2
  Option 1: 3 * N * TSMTC, where N = 8 and TSMTC is SMTC periodicity of target cell.
  Option 2: 5 * TSMTC + N * TSMTC, where N = 8 and TSMTC is SMTC periodicity of target cell.
SIB1 decoding delay requirements
  Option 1: -3 dB SNR and 6 samples
  Option 2: -4 dB SNR and 6 samples
Margin for interruptions during each autonomous gap for SIB1 decoding
  2* 2ms + 1 slot (victim cell SCS)
Known Cell condition for FR1 and FR2
  During the last X seconds before the reception of the report CGI command
    the UE has sent a valid L3-RSRP measurement report with SSB index for the target cell
  During MIB decoding at least reported SSBs remains detectable according to the cell identification conditions specified in clauses 9.2 or 9.3 of TS 38.133, and
  During SIB1 decoding the SSB used for MIB decoding remains detectable according to the cell identification conditions specified in clauses 9.2 or 9.3 of TS 38.133, and
  During MIB decoding and SIB1 decoding, the SSB for MIB decoding and PDSCH for SIB1 decoding remain detectable with SNR ≥ -3dB.
  X=5 for FR1 and X=3 for FR2
Value for timer T321
  Option 1: 2 seconds for FR1 and 5 seconds for FR2
  Option 1: 2 seconds for FR1 and 3 seconds for FR2