## Slide 1: Way forward on UE power imbalance requirements for FR1 CA and EN-DC
NTT DOCOMO
3GPP TSG-RAN4 Meeting #95e Electronic Meeting, 25 May - 5 June, 2020 Agenda item: 6.18.1.4
R4-2008848

## Slide 2: Wayforward
For FR1 intra-band contiguous CA
Channel bandwidth combination for defining performance requirements
  Option 2: Define requirements for 5+5 MHz bandwidth for FDD+FDD CA, 10+10 MHz bandwidth for TDD+TDD CA, with the following test applicability
    Option 2a
      The test is done for any one of the supported bandwidth combination, by using performance requirement for 5+5 MHz FDD+FDD CA or 10+10 MHz TDD+TDD CA.
      The tested PRBs shall be placed in the lowest part for the CC with lower carrier frequency, and placed in the highest part for the CC with higher carrier frequency.
    Option 2b
      The test is done for any one of the supported bandwidth combination, by using performance requirement for 5+5 MHz FDD+FDD CA or 10+10 MHz TDD+TDD CA.
      The tested PRBs shall be placed in the highest part for the CC with lower carrier frequency, and placed in the lowest part for the CC with higher carrier frequency.
      Select the CA combination with largest bandwidth, and select the CA configuration with the same BWs in each carrier for power imbalance test
      If there is no supported CA configuration with the same BWs, additional power imbalance test can be considered if necessary.
      Note that from 38.101-1, we can observe that most of the CA combinations have the configuration with same BWs, except CA_n71B and CA_n78B.
  Option 3: Define generic methodology for selection of CBW combination among all CBW combinations in supported CA configurations
  RAN4 uses option 3 if it is feasible to define bandwidth agnostic requirements for option 3.

## Slide 3: Wayforward
For FR1 intra-band contiguous CA
Channel bandwidth combination for testing
  As baseline, use the following approach
    Step 1: First select the CBW combinations with the same BWs in each carrier
      If there is no such CBW combination, select the CBW combinations with smallest CBW difference between the two carriers, and the carrier with [larger or smaller] CBW will be used for test.
    Step 2: Among the CBW combinations selected from step 1, select the CA combination with largest aggregated CBW
  Following topic will be discussed further
    In step 1, if there is no CBW combinations with the same BWs in each carrier, whether the carrier with larger or smaller CBW will be used for test?

## Slide 4: Wayforward
For FR1 intra-band contiguous CA
PDSCH RB allocation
  To be decided after the channel bandwidth combination is agreed
MIMO configuration
  1x2 and 1x4
MCS
  FFS whether to use 64QAM or 256QAM based on more simulation results for 1x2 and 1x4
  Assumptions related to the target SNR point for simulation
    Power difference between two CCs
      6dB
    Impairment margin + extra margin
      Option 1: 3dB
      Option 2: lower than 3dB
PRB bundling size
  WB

## Slide 5: Wayforward
For intra-band contiguous EN-DC
Duplex mode
  FDD and TDD
SCS
  FDD: 15kHz
  TDD:
    Option 1: 30kHz
    Option 2: 15kHz and 30kHz
      Test #2a: LTE TDD + NR TDD 15 kHz, in case UE supports it, otherwise LTE TDD + NR TDD 30 kHz
      Test #2b: LTE TDD + NR TDD 30 kHz, in case UE supports it, otherwise LTE TDD + NR TDD 15 kHz
TDD pattern for 30kHz SCS
  7D1S2U
TDD pattern for 15kHz SCS (if needed)
  Option 1: DSU+DD
  Other options are not precluded.

## Slide 6: Wayforward
For intra-band non-contiguous EN-DC
The possibility of using single RF chain to receive two non-continuous carriers in co-located scenario cannot be precluded.
RAN4 agree to introduce test cases for power imbalance requirement for FR1 intra-band non-contiguous EN-DC with test applicable rules
Test applicability rules
  Option 1
    UE supports only intra-band contiguous EN-DC, i,e., if UE does not indicate “intraBandENDC-Support”,
      power imbalance requirement for intra-band contiguous EN-DC is applied
    UE supports only intra-band non-contiguous EN-DC, i.e., if UE indicates “non-contiguous” in “intraBandENDC-Support” or UE does not indicate “interBandContiguousMRDC”,
      power imbalance requirement for intra-band non-contiguous EN-DC is applied
    UE supports both intra-band contiguous and non-contiguous EN-DC, i.e., if UE indicates “both” in “intraBandENDC-Support” or UE indicates “interBandContiguousMRDC”,
      power imbalance requirement for FR1 intra-band contiguous EN-DC
  Option 2
    UE supports only intra-band contiguous EN-DC, i,e., if UE does not indicate “intraBandENDC-Support”,
      power imbalance requirement for intra-band contiguous EN-DC is applied
    UE supports only intra-band non-contiguous EN-DC, i.e., if UE indicates “non-contiguous” in “intraBandENDC-Support”
      power imbalance requirement for intra-band non-contiguous EN-DC is applied
    UE supports both intra-band contiguous and non-contiguous EN-DC, i.e., if UE indicates “both” in “intraBandENDC-Support”
      power imbalance requirement for FR1 intra-band contiguous EN-DC
  Other options are not precluded.
Test design
  FFS