## Slide 1: WF on the inter-band CA within FR2 objective
Anritsu
R4-2012715
3GPP TSG-RAN WG4 Meeting #96-e
Online, 17th – 28th Aug 2020
Agenda: 13.1.3
E-mail title: [96e][330] FR2_enhTestMethods
Sub-topic: 3-1
WI: FR2_enhTestMethods

## Slide 2: Outcome of the 1st round discussion
Two contributions on the test methodology for DL inter-band CA in FR2 were submitted and a necessity of the offset feed antennas for FR2 test system were discussed in the 1st round.
4 companies out of 5 were supportive to the further study of the influence by the offset antenna to determine a feasibility of this test method.
T-doc number | Company | Proposals / Observations
R4-2009962 | Apple Inc. | Views on test methodology for inter-band CA within FR2 Proposal 1: Further study is needed to determine whether non-colocated test antennas for DL inter-band CA verification is feasible from the perspective of ∆PSD at the UE after spatial filtering.
R4-2010802 | Rohde & Schwarz | Discussion on open issues of inter-band CA testability Observation 1: Providing DL signals from the same AoA inter-band CA in FR2 with 2 bands is feasible for the Rel-16 frequency bands, without exceeding the MU for single carrier/intra-band CA. Observation []: Imbalance can be larger for a single antenna test system, than estimated in [7]. Proposal 1: RAN4 agrees that the testing of Rel-16 inter-band CA using a single antenna from 1AoA is feasible. Proposal 2: RAN4 discusses above questions to clarify the testing implications for inter-band CA with power imbalance.

## Slide 3: Way forward
- RAN4 agrees that the testing of Rel-16 inter-band CA using a single antenna from 1AoA is feasible. (Proposal 1 from [3])
- Further study is needed to determine whether non co-located test antennas for FR2 DL inter-band CA verification is feasible from the perspective of ∆PSD at the UE after spatial filtering.
Companies are encouraged to bring analysis of influences to the UE and the TE dynamic range by the offset antenna method especially with the independent beam management (IBM) UE which supports 28GHz + 39 GHz ranges.
Angular offset from the focal point is in a range from 2.5 to 105 degrees.
Other conditions such as common beam management, CA combination of 28GHz + 28GHz or 39GHz + 39GHz are not precluded.
- Whether the offset feed antenna method is necessary to address band n262 testability is FFS.

## Slide 4: Expected angular offset between 2 antennae
Considered antenna offset in distance is within the range from 50 mm to 100 mm from the current antenna arrangement including the spurious measurement antenna.
 |  | Antenna offset in distance / angle | 
 |  | 50 mm | 100 mm
Range length | 1200 mm | 2.4 deg | 4.8 deg
 | 1000 mm | 2.9 deg | 5.7 deg
 | 800 mm | 3.6 deg | 7.1 deg
Radiation pattern of 2x8 antenna. Extract from [6]
Expected angular offset between 2 antennae
Including a slightly extreme case, 2.5 to 510 degrees are expected as a baseline angular offset to study.

## Slide 5: Reference
[1] R4-2012561, “Email discussion summary for [96e][330] FR2_enhTestMethods”, Moderator (Apple Inc.), RAN4 #96-e, Online
[2] R4-2009962, “Views on test methodology for inter-band CA within FR2”, Apple Inc., RAN4 #96-e, Online
[3] R4-2010802, “Discussion on open issues of inter-band CA testability”, Rohde & Schwarz, RAN4 #96-e, Online
[4] R4-2000445, “Consideration on capability of multi signal transmission from single AoA in FR2 OTA test system”, Anritsu, RAN4 #94-e, Online
[5] R4-2003332, “Consideration on FR2 OTA test system with multi signal transmission”, Anritsu, RAN4 #94-e-bis, Online
[6] R4-1911338, “FR2 blocker signal from offset antenna”, Anritsu, RAN4 #92-bis, Chongqing, China