## Slide 1: WF on replacement of measCycleSCell in core requirements for Direct SCell activation
Apple
3GPP TSG-RAN WG4 Meeting #98-e R4-2103552
Electronic Meeting, 25th Jan. – 5th Feb. 2021

## Slide 2: Background
In existing direct SCell activation requirement, Tactivation_time refers to that defined in legacy SCell activation requirement.
In legacy SCell activation requirement, measCycleSCell is used to differentiate whether the target cell has been measured recently:
  If the SCell is known and belongs to FR1, Tactivation_time is:
    TFirstSSB+ 5ms, if the SCell measurement cycle is equal to or smaller than 160ms.
    TFirstSSB_MAX + Trs + 5ms, if the SCell measurement cycle is larger than 160ms.
It was identified in R4-2100227 that measCycleSCell is no longer a suitable condition to differentiate activation delay requirements for direct SCell activation in FR1.

## Slide 3: Agreement
In direct SCell activation requirements, if SCell is known and belongs to FR1, Tactivation_time does NOT depend on whether measCycleSCell is larger than 160ms or not.
RAN4 will further how to replace measCycleSCell in corresponding conditions.
The issue can be addressed in core requirements maintenance without any impact on test case design.

## Slide 4: Agreement
Candidate options to move forward:
  Option 1 (Apple): Replace condition on measCycleSCell with Tsample_interval defined as follows:
    If no DRX is configured or DRX cycle>320ms, Tsample_interval = Max(MGRP, SMTC period, DRX cycle)  CSSFinter
    Otherwise, Tsample_interval = 1.5  Max(MGRP, SMTC period, DRX cycle)  CSSFinter
  Option 2 (MediaTek): Replace condition on measCycleSCell with Tsample_interval defined as follows:
    If no DRX is configured or DRX cycle>320ms, Tsample_interval = Max(MGRP, SMTC period, DRX cycle)
    Otherwise, Tsample_interval = 1.5  Max(MGRP, SMTC period, DRX cycle)
  Option 3 (Nokia, vivo, Huawei, Ericsson): Replace condition on measCycleSCell, but discuss further on with what to replace it.
  Option 4 (Apple):
    TFirstSSB+ 5ms, if the SCell has been measured within measurement gap before activation and TSSB_measurement_period_inter, as specified in Table 9.3.5-1, is equal to or smaller than 1280ms; or if the SCell has been measured without measurement gap before activation and T SSB_measurement_period_intra, as specified in Table 9.3.9-1, is equal to or smaller than 800ms.
    TFirstSSB_MAX + Trs + 5ms, if the SCell has been measured within measurement gap before activation and TSSB_measurement_period_inter, as specified in Table 9.3.5-1, is larger than 1280ms; or if the SCell has been measured without measurement gap before activation and T SSB_measurement_period_intra, as specified in Table 9.3.9-1, is larger than 800ms.