## Slide 1: Way forward on introduction of NR intra-band UL CA as UL configuration in an inter-band combination
Skyworks Solutions Inc.
R4-2103097
3GPP TSG-RAN WG4 Meeting #98-e
Electronic meeting, 25 Jan. – 5 Feb. 2021

## Slide 2: Scope
Capture guidelines on how to introduce an UL configuration that contains an NR intra-band UL CA part in an inter-band:
  Inter-band NR CA, inter-band EN-DC and inter-band NR DC are in scope
Unlike the introduction of an intra-band configuration in DL that can be introduced with a simple CR as it does not create new UL related MSD issue, the change of UL configuration may have impact on MSD and potentially to band protections and emissions
The new MSD issues must be assessed to clarify if RAN4 need to introduce new requirements or put constraints on how these are introduced
These guidelines will be used to evaluate potential revision of CRs that are introducing n7B UL CA configuration [1-4] for next meeting

## Slide 3: Background on intra-band UL CA types in an inter-band combination:
There are three types of intra-band UL CA cases that can be introduced in an inter-band combination:
  Type 1: The intra-band part is the only UL part, for example UL configurations like CA_nXB, CA_nXC, CA_nX(2A): 2 UL CC are involved
  Type 2: The intra-band part is part of an inter-band UL configuration, for example UL configurations like CA_nYA-nXB, CA_nYA-nXC, CA_nYA-nX(2A), DC_nYA_nXB, DC_nYA_nXC, DC_nYA_nX(2A), : 3 UL CC are involved but in some cases there are 3 separate sub-blocks
  Type 3: there is intra-band UL CA in both UL bands: 4 UL CCs are involved more triple beat tones are generated but it is an extension of type 2 and there could be up to 4 separate sub-blocks
In all cases new IMD products are generated compared to the initial case:
  Two tone IMDs of the 1RB+1RB worst case allocation for type 1
  Triple beat IMDs of the 1RB+1RB with the second band UL for type 2
  Even more Triple beat IMDs of the 1RB+1RB in both bands for type 3
  These issues exist only for simultaneous TX/RX case
  There has been no real discussion in RAN4 about these types of cases
  Potential MSD issues have not been assessed
  Are >2 separate sub-blocs valid?

## Slide 4: Background: Illustration of issues for type 1 and type 2/3 cases
Band 1 UL
Band 1 DL
Band 2 w intra UL CA
Delta F
Delta F
Delta F
UL CC2-1
UL CC2-2
DL CC1-1
IMD3
IMD5
IMD5 of the 1RB+1RB case from the UL CA configuration of band 2 fall in the DL of band 1
IMD3 of the 1RB+1RB case from the UL CA configuration of band 2 fall in the DL of band 1
=> This issue can apply to two band or three band inter-band combinations
Type 1
2 UL
Delta F
IMD3
Band 3 DL
DL CC3-1
Band 1 UL
Band 1 DL
Band 2 w intra UL CA
Delta F
Delta F
Delta F
UL CC2-1
UL CC2-2
DL CC1-1
IMD3
IMD5 + triple beat tone
Same IMD products than type 1 but with additional triple beat tones here FUL_CC1 + FUL_CC2-2 – FUL_CC2-1
=> This issue can be very severe if the UL intra-band distance between the two allocation is close to the duplex distance but also is it is equal to the distance between the single UL and another band
This issue can apply to two band or three band inter-band combinations
Type 3 has two time type 2 cases
Type 2/3
3/4 UL
Delta F
IMD3
Band 3 DL
DL CC3-1
UL CC1-1
Delta F

## Slide 5: Background: current LTE cases
CA_1A-1A-7C CA_7C
CA_1A-3C CA_1A-3A\_3C
CA_1A-1A-3C CA_3C
CA_1A-7C CA_1A-7A\_7C
CA_1A-41C CA_1A-41A/C
CA_1A-42C CA_1A-42A/C\_42C
CA_2A-48C CA_2A-48A, CA_48C
CA_3A-7C CA_3A-7A\_7C
CA_3C-7A CA_3A-7A\_3C
CA_3C-7C CA_3A-7A\_3C\_7C
CA_3C-8A CA_3A-8A\_3C
CA_3C-20A\_3C-28A\_3C-38A CA_3C
CA_3A-41C CA_3A-41A/C\_41C
CA_3A-41D CA_3A-41A\_41C
CA_3A-42C CA_3A-42A/C\_42C
CA_3A-42A-42C\ _3A-42C-42C CA_3A-42A\_42C
CA_4A-5B CA_5B
CA_4A-4A-5B CA_4A-5A\_5B
CA_5A-5A-66A-66B\_5A-5A-66B CA_5A-66A\_66B
CA_5A-66B\_5A-66A-66B CA_66B
CA_5B-66A CA_5B
CA_5B-66B CA_5B\_66B
CA_7C-28A CA_7A-28A\_7C
CA_18C-41C CA_18C-41C
CA_18A-41C CA_18A-41A/C
CA_28A-42C CA_28A-42A\_42C
CA_28A-42A/C-42C CA_42C
CA_39A-41C CA_41C\_39A-41A/C
CA_39A-41D CA_41C\_39A-41A
CA_39C-41A CA_39C\_39A/C-41A
CA_39C-41C CA_39C\_41C\_39A-41A
CA_41A-42C CA_41A-42A/C\_42C
CA_41A-42A/C-42C\CA_41C-42A/C-42C CA_42C
CA_41C-42A CA_41A/C-42A\_41C
CA_41C-42C CA_41A/C-42A/C\_41C\_42C
CA_41C-48A/C/D\_41D-48A/C CA_41C
CA_46A/C-48C\_46A-48D/E\_46C-48D/E CA_48C
CA_46A/C/D/E-48B CA_48B
UL configurations including intra-band UL CA
2 UL CC intra-band UL CA: class B 20MHz IMD5 OOB range, class C 40MHz OOB range
=> no cross band isolation issue
3UL CC intra-band UL CA + 1 UL: class B 20MHz TB range, class C 40MHz TB range
=> < duplex distance in most cases => no issue for FDD band de-sense (or only exceptionally)
4UL CC intra-band + intra-band UL CA: 1 TDD-TDD case and
> 700MHz distance no cross-band isolation issue
In all cases no more than two contiguous sub-blocks
In LTE there is only contiguous intra-band UL configurations within inter-band combinations => intra-band IMDs have limited spread beyond their band (40MHz IMD5 offset), and Intra-band CA maximum aggregation BW is small compared to FDD duplex distance. Given the above, the cases where additional MSD needs to be studied is limited.

## Slide 6: Background: current NR CA and ENDC cases
CA_n2A-n48 CA_n2A-n48A\_n48C
CA_n3A-n77(2A) CA_n77(2A)\_n3A-n77A
CA_n3A-n78(2A) CA_n78(2A)
CA_n25A-n41C CA_n25A-n41A\_n41C
CA_n28A-n77(2A) CA_n77(2A)\_n28A-n77A
CA_n28A-n78(2A) CA_n78(2A)\_n28A-n78A
Already in 38.101-3
DC_1A/C_n3A DC_1A/C_n3A
DC_2A_n41A/C\_2C_n41A DC_2A/C_n41A
DC_2A_n71A/B\_2C_n71A DC_2A/C_n71A
DC_3A/C_n1A DC_3A/C_n1A
DC_3A/C_n5A DC_3A/C_n5A
DC_3A_n7A/B\_3C_n7A/B DC_3A_n7A/B\_3C_n7A
DC_3A/C_n28A DC_3A/C_n28A
DC_3A/C_n41A DC_3A/C_n41A
DC_3A_n77A/C\_3C_n77A\_3A/C_n77(2A) DC_3A/C_n77A
DC_3A_n78A/C\_3C_n78A DC_3A/C_n78A
DC_3A_n77A/C\_3C_n77A DC_3A/C_n77A
DC_3A_n79A/C\_3C_n79A DC_3A/C_n79A
DC_7A/C_n1A DC_7A/C_n1A
DC_7A/C_n3A DC_7A/C_n3A
DC_7A/C_n5A DC_7A/C_n5A
DC_7A/C_n28A DC_7A/C_n28A
DC_7A/C_n78A\_7A_n78C DC_7A/C_n78A
DC_7A/C_n78(2A) DC_7A/C_n78A
DC_8A_n79A/C DC_8A_n79A/C
DC_28A_n7A/B DC_28A_n7A/B
DC_39A/C_n41A DC_39A/C_n41A
DC_40A/C_n78A DC_40A/C_n78A
DC_41A/C_n3A DC_41A/C_n3A
DC_41A/C_n28A DC_41A/C_n28A
DC_41A/C_n77A DC_41A/C_n77A
DC_41A/C_n77(2A) DC_41A/C_n77A
DC_41A/C/D_n78A DC_41A/C_n78A
DC_41A/C_n78(2A) DC_41A/C_n78A
DC_41A_n79A/C\_41C_n79A DC_41A/C_n79A
DC_42A/C_n3A DC_42A/C_n3A
DC_42A/C_n28A DC_42A/C_n28A
DC_48A/B/C/D/E_n46A\_48A/B/C/D_n46B\_48A/B/C/D/E_n46C\_48A/B/C/D/E_n46D\_48A/B/C/D/E_n46E DC_48A/B_n46A
NC CA UL configurations including intra-band UL CA
Only 2 UL CC intra-band UL CA: IMD5 OOB range class B 200MHz/C 400MHz/2A 800MHz for n78, 1200MHz for n77
Potential cross-band isolation issue
CA_n40A-n41C CA_n41C\_n40A-n41A
CA_n41C-n66A CA_n41C\_n41A-n66A
CA_n41C-n71A CA_n41C\_n41A-n71A
CA_n41C-n77A CA_n41A-n77A\_n41C
CA_n41C-n79A CA_n41A-n79A\_n41C
CA_n66A-n77(2A) CA_n66A-n77A\_n77(2A)
ENDC added in [1] DC_1A_n7A/B\_1A-1A_n7A DC_1A_n7A/B
DC_3A_n7A/B\_3C_n7A/B\_3A-3A_n7A/B DC_3A_n7A/B\_3C_n7A/B
ENDC UL configurations including intra-band UL CA
3UL CC LTE intra-band UL CA + 1 NR UL: TB range class B 20MHz, 40MHz TB range
< duplex distance => no issue for FDD band de-sense
3UL CC NR intra-band UL CA + 1 LTE UL : TB range Class B 100MHz, class C 200MHz, 400MHz for n78(2A), 600MHz n77(2A), some already in 38.101-3, more added in [1]
> most duplex distance => potential FDD band de-sense but also of neighbour DL band in >2 DL band combinations
[1] adds 4UL CC NR intra-band UL CA + LTE intra-band UL : TB range Class B+C = 40+100MHz in this particular case TB range 3C+n7B=40+50=90MHz, 180MHz IMD5 range
Need to check potential issue with band 3 duplex distance of 95MHz
In all cases no more than two contiguous sub-blocks
With a much larger total TX bandwidth, non-contiguous and contiguous NR UL CA can generate new MSD issues

## Slide 7: Background: LTE versus NR, what’s new
In LTE the few cases containing UL CA configuration are only contiguous UL CA thus 40MHz allocation span max
In NR we have type 1, 2, 3 and:
  Contiguous UL CA allocation span is 100MHz for type B and 200MHz for type C
  Non-contiguous UL CA with at up to 600MHz allocation span for n77(2A)
In the later case the IMD3/5 range can cover up to 3GHz BW!
The triple beat with FDD UL can cover all known duplex distances
It is necessary to study these IMD products for:
  Cross band isolation MSD due to IMDs for 2UL CC intra-band only
  New triple beat IMD MSD test points for 2UL CC intra-band + second band UL (1 or 2 CC)
  Potential band protection issues in the two cases
The n7B case in this meeting CRs with 50MHz max BW is reasonable but there are critical cases

## Slide 8: Background: some “realistic” examples
band protection issue:
  For type 1 MPR guaranties -30dBm/MHz beyond ACLR1 but only -13dBm/MHz in ACLR1
  Filter rejection needs to be >20dB beyond ACLR1 region and >37dB in ACLR 1
  !!! For NS04 it is only -25dBm/MHz and A-MPR is waived beyond filter pass-band: A-MPR may not help
  No MPR help for triple beat: depends on allocation
Cross-band isolation issue for type 1 and type 2:
  For type 1 even with 50dB filter isolation we potentially have a -63dBm/MHz or -80dBm/MHz interference issue to DL channels => large MSD can exist
    In many case the filter rejection between band s is << 50dB
  For triple beat product cases, the levels needs to be estimated but depends on how much reverse IMD may be generated or which level of the 3UL gets in the receiver => complex analysis
  New IMD test points related to triple beat products at duplex distance is similar but FDD filter assumption are known

## Slide 9: WF: Options on how to introduce intra-band UL CA configuration in an inter-band combination
MSD issues are specified and tested and network performance is known and UL configurations can be chosen properly
A TR must be used to introduce such cases, CR are not allowed. If a combinations does not meet the restriction of only up two non-contiguous sub-blocks, a discussion paper should be provided
RAN4 companies are welcomed to provide their views on the following options in RAN4#98bis-e
  Restrict cases to only up to two non-contiguous sub-blocks:
    Only contiguous NR intra-band UL can be added to a second UL band
    Non-contiguous NR intra-band UL cannot be added to a second UL band
      All cases already in the specification and submitted in this meeting are compliant
      Triple beat issues are limited to 200MHz range for class C
  Provided all of the above is agreed:
    Band protection should be guaranteed if distance to DL bands is > intra-band total BW
    Only cross band issue related to ACLR1/2 of contiguous intra-band and IMDs of non-contiguous intra-band part should be verified
    A TR must be used to introduce such cases, could be part of UL CA basket
  Check if restrictions for contiguous intra-band cases allocation can reduce the extend of the problem

## Slide 10: WF: MSD calculations for intra-band UL CA configuration in an inter-band combination
Can be used as guidelines for related TRs in next meeting and depending on agreements from previous page may result in a specific template.
For IMDs of 2CC intra-band UL CA:
  Take the maximum total TX BW for the intra-band UL CA
    Maximum aggregated bandwidth for contiguous UL CA
    Maximum separation class for non-contiguous UL bonded to the band BW
  If distance between the UL band and the DL band is < 2xTX_BW then DL band is subject to IMD3 and/or IMD5 of the 2CC 1RB+1RB allocation and MSD should be analyzed.
  For contiguous allocation only in contiguous intra-band case lower MSD should be feasible
Triple beat of 2CC contiguous intra-band UL CA + second UL band:
  Take the Maximum aggregated bandwidth for contiguous UL CA = TXBW
  If TX BW > separation between second UL band and DL band (for FDD DL or third DL band) then DL band subject of 3rd order triple beat
  MSD should be analyzed but with contiguous and non-contiguous allocations
Without restrictions from previous page band protection need to be checked for bands at small distance from UL CA band when compared to TXBW.

## Slide 11: References of related CRs introducing such cases:
[1] R4-2102045 draft CR 38.101-3 adding CA_n7B UL configurations for 1 LTE + 1 NR, Ericsson R4#98e
[2] R4-2102046 draft CR 38.101-3 adding CA_n7B UL configurations for 2 LTE + 1 NR, Ericsson R4#98e
[3] R4-2102047 draft CR 38.101-3 adding CA_n7B UL configurations for 3 LTE + 1 NR, Ericsson R4#98e
[4] R4-2102048 draft CR 38.101-3 adding CA_n7B UL configurations for x LTE + 2 NR, Ericsson R4#98e