## Slide 1: WF on additional emission requirements for CA/DC
SoftBank
3GPP TSG-RAN WG4 Meeting #98-e R4-2103120
Electronic meeting, 25 Jan – 5 Feb, 2021

## Slide 2: Background
Applicability of additional emission requirements(NS) to 2 band UL CA/DC is left unsettled for some time.
Thus far, it was clarified that additional requirements should not be specified in general requirement tables and these are removed.
This WF is intended to capture agreements in this meeting and next steps for coming meetings.

## Slide 3: Agreement in RAN4#98-e
The following is to be agreed in RAN4#98-e
[Agreement-1] If an NS value is indicated in a band, the additional requirement shall be met regardless if the UE has uplinks configured in the other bands.
Contributions are invited if the agreement should also be captured in the relevant specifications, i.e. 36.101/38.101-X.

## Slide 4: Next steps (1)
For 2 bands UL CA/DC, the following issue is identified to be studied.
[Issue-1] Whether or not 2 band specific issues(IMDs) could violate an additional emission requirement, with an aid of a single band NS (if applicable).
  Note that so far, we have assumed that IMDs won’t violate the tightest protection requirement (-50dBm/MHz in the general requirement) then IMDs have not been checked against a protection requirement.
  This sounds like it is better to consider the general requirement also.
Focus is on 2 band (inter-band) UL CA/DC
  In case of 3 ULs where one of the bands has intra-band cont/non-cont UL CA, an emission requirement within the band is assumed to be addressed properly, i.e. with NS_XX or CA_NS_YY if necessary.

## Slide 5: Next steps (2)
To address the issue, the following approach is proposed.
As a first step, identify safe or risky scenarios against (additional) emission requirements
  Note: Since IMDs could also violate a general emission requirement for UE co-ex (e.g. Table 6.5A.3.2.3-1 of 38.101-1), consideration for the general emission requirement is not precluded
Further actions will be determined based upon the findings above:
  Methods to identify the problematic combos
  Systematic approach possible or case-by-case?
  Problematic combos to be identified during standardisation process with practical work load?

## Slide 6: EOF