## Slide 1: WF on intra-band UL CA PCMAX
Huawei, HiSilicon, []
R4-2103146
3GPP TSG-RAN WG4 #98-e
Jan 25 – Feb 05, 2021
Electronic meeting

## Slide 2: Background
In RAN1 #93 meeting, following is agreed: “for CA, when calculating the PHR of a cell based on a real transmission, transmissions whose DCI come after the first DCI after PHR trigger are ignored”.
In TS 38.214, PUSCH preparation time for PUSCH timing capability is divided into capability 1 and capability 2:
N2(PUSCH preparation time) processing time can be different across CC

## Slide 3: WF1
For intra-band UL CA, if DCI for transmission of one CC(CC1) come after the PHR trigger of DCI for the other CC(CC2), in which the UL transmissions for CC1 and CC2 are overlapped in time, CC1’s PHR will ignore the transmission on CC2.
FFS how to define Pcmax,c for each CC in intra-band UL CA , following aspects can be considered:
  MPR and AMPR of Pcmax,c for each CC in intra-band UL CA
  Whether Ppowerclass,CA and PEMAX,CA need to be considered in Pcmax,c calculation

## Slide 4
WF2: TAG
Agreement: there is only one TAG for intra-band UL contiguous CA
  FFS for intra-band UL non-contiguous CA