## Slide 1: Way forward on the introduction of 25 MHz in band n5
AT&T
­­­3GPP TSG-RAN WG4 Meeting # 98-e R4-2103185
Electronic Meeting, 25th Jan. – 5th Feb., 2021

## Slide 2: Background
Ericsson provided contribution concerning A-MPR for 25MHz channel bandwidth for n5 suggesting the following:
  Coexistence with adjacent Public Safety service in DL (851-859MHz) might need to be further checked
  Also, coexistence with band n26 might need further consideration
Ericsson provided contribution with REFSENS proposals for 25MHz channel bandwidth for n5
No agreement can be reached on REFSENS proposal

## Slide 3: WF on A-MPR
Issue 5-1: A-MPR for 25MHz channel BW
Observations:
  Concerns raised on the following:
    Impact of 25MHz TX BW
    Coexistence with B26 (possibly others based on regional deployment situation)
    Coexistence with adjacent Public Safety service in DL (851-859MHz)
    Need to check A-MPR
WF
  Companies encouraged to evaluate TX/RX 20MHz/25MHz and 25MHz/25MHz options at next meeting
  Companies encouraged to evaluate coexistence with B26 and adjacent Public Safety service in DL (851-859MHz) at next meeting
  Companies encouraged to check A-MPR and provide results at next meeting

## Slide 4: Way Forward on REFSENS
Issue 5-2: UE REFSENS
  Option 1: Specify following REFSENS limits and corresponding RB allocation (Ericsson)
Observations:
  No agreement to use scaling of existing values for REFSENS for 25 MHz
  Concerns raised on the following:
    Impact of 25MHz TX BW
WF
  Companies encouraged to bring UL config proposals for REFSENS at next meeting
  Companies encouraged to bring analysis/measurements for REFSENS at next meeting for 25MHz
  Companies encouraged to evaluate TX/RX 20MHz/25MHz and 25MHz/25MHz options at next meeting
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | Duplex Mode
n5 | 15 | -98.0 | -94.8 | -93.0 | -86.8 | -85.8 | FDD
 | 30 |  | -95.1 | -93.1 | -88.6 | -87.5 | 
 | 60 |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | Duplex Mode
n5 | 15 | 25 | 251 | 201 | 201 | 201 | FDD
 | 30 |  | 121 | 101 | 101 | 101 | 
 | 60 |  |  |  |  |  | 

## Slide 5: References
R4-2102166, “Additional channel bandwidths in bands n2, n5 and n48 – A-MPR impacts”, Ericsson, 3GPP TSG-RAN WG4 Meeting # 98-e
R4-2102167, “Additional channel bandwidths in bands n2, n5 and n48 – REFSENS”, Ericsson, 3GPP TSG-RAN WG4 #98-e