## Slide 1: Way forward on simulation assumptions for PC2 NR V2X
Huawei, HiSilicon, ...
3GPP TSG-RAN WG4#98e R4-2003250
Electronic Meeting, Jan 25 – Feb 5, 2021

## Slide 2: Background
In this meeting, RAN4 discussed the MPR/A-MPR simulation assumptions for NR V2X PC2 UE [1] [2] [3].

## Slide 3: General MPR Assumption
parameter | Assumption
center frequency | 5.9GHz
Bandwidth | 10/20/30/40MHz
Maximum output power | 26dBm
numerology | 15 kHz/30kHz/60kHz
Modulation | QPSK/16QAM/64QAM/256QAM
Waveform | CP-OFDM
Carrier leakage | 25dBc
IQ image | 25dBc
CIM3 | 45dBc or 60dBc
PA calibration | PA calibrated to deliver [31dBc] ACLR for a fully allocated RBs in 20MHz QPSK DFT- S-OFDM waveform at 1 dB MPR. This is based to share PA between LTE V2X and NR V2X at 5.9GHz as worst case.
Note: RAN4 will further evaluate and check the ACLR value for PC2 UE based on the co-existence simulation.

## Slide 4: Assumption for PSCCH/PSSCH
Items | Assumption
Allowed sub-channel sizes | • Support {10, 12, 15, 20, 25, 50, 75, 100} PRBs for possible sub-channel size.
Allowed LCRB allocation | 10,12,15,20, 24, 25,30,36, 40,45,48,50,60,70,72, 75,80,84, 90,96,100,105,108,110,120,130,132,135,140,144,150,156,160,165,168,170,175,180,190,192,195,200,204,210, 216
Regarding PSCCH / PSSCH multiplexing | 
PSCCH size | 10RB*3 Symbols
PSD offset of X dB between PSCCH and PSSCH | 0dB

## Slide 5: Assumption for PSFCH
Items | Assumption
Modulation for PSSCH | QPSK
PSFCH | ZC sequence
Structure of Slot | Baseline is follow RAN1 agreements
RB allocation | 1 RB per user All users have the same power per RB Total power of all users equals 26dBm for PC2 Both Non-contiguous PSFCH RB allocation and contiguous PSFCH allocation are allowed MPR will be derived by non-contiguous PSFCH RB allocation (N>1) At least, the worst cases with possible RBstart and Ngap need to be checked. ( Ngap = RBend – RBstart ) For example: The worst case N gap is (106-1 =105*15kHz*12=) 18.9MHz for 20MHz, 15kHz SCS IMD problem by dual PSFCH in SEM/SE region shall be considered to derive MPR level according to all supporting CBW and SCS. N (Number of users) is up to 5 and RBs except for RBstart and RBend can be inserted between RBstart and RBend randomly. Assumption of N in RAN4 is only for MPR simulation purpose, the final number is up to RAN1 decision.

## Slide 6: Assumption for S-SSB
Items | Assumption
Modulation for PSBCH | QPSK
S-PSS | M-sequence
S-SSS | Golden-sequence
S-SSB structure | 
RB allocation | RBstart: All the possible cases LCRB: 11 RB

## Slide 7: Additional SE/SEM requirements for NS_33/NS_52
The additional SE/SEM requirements for NS_33 and NS_52 specified in sub-clause 6.2E from TS 38.101-1 should be met, before any updates from ETSI and FCC.
For the ETSI future updating the additional SE, RAN4 also study and capture the A-MPR requirement with NS_xx in TR38.xxx in Rel-17.

## Slide 8: References
# | TDoc | Title | Source
1 | R4-2100284 | PC2 MPR/A-MPR simulation assumptions for SL enhancement in Rel-17 | LG Electronics Inc.
2 | R4-2101937 | Discussion on n47 PC2 MPR simulation of Rel-17 SL enhancement | Huawei, HiSilicon
3 | R4-2100420 | Discussion on PC2 for SL enhancement | CATT