## Slide 1
WF on FR2 UEs that support inter-band DL CA with CBM
3GPP TSG-RAN WG4 Meeting #98-e R4-2103399
Electronic Meeting, Jan.21st – Feb.05th, 2021
Agenda Item: 11.3.2.1.3
Samsung

## Slide 2: Background
UE requirements for CBM UEs within same frequency group have been mainly discussed in email thread [139], and also involved in [138] as well.
Network deployment for CBM UEs have been discussed in email thread [138].
This WF captures the agreement for CBM UEs from above two threads.

## Slide 3: Definition of CBM
CBM: (Common Beam Management) A UE that supports inter-band CA with CBM selects its DL Rx beam(s) for all CCs in all configured bands based on DL measurements made in the only CC configured with the reference signal for beam management.
  Note the above definition is based on the agreement on next page “Beam management reference signal location for FR2 CA test”

## Slide 4: Beam management reference signal location for FR2 CA test
In FR2 CA cases, requirements apply when the BM RS is provided in a CC with a configured UL BWP

## Slide 5: WF on UE Requirements for inter-band DL CA within the same frequency group based on CBM
Define UE requirements for inter-band CA within the same freq. group (e.g. 28GHz + 28GHz) for common beam management (CBM) based on requested band combinations.
Requirement framework for inter-band DL CA within the same frequency group based on CBM:
  REFSENS relaxations
    FFS: for CBM between overlapping or touching bands, REFSENS relaxations structure shall follow intra-band CA
    REFSENS relaxations values are band combination dependent
    REFSENS relaxation shall be a function of frequency span between the configured DL CCs.
  FFS whether EIS spherical coverage requirements shall not be specified
  Specify same requirements for maximum input level, ACS and in-band blocking as that for intra-band CA scenarios

## Slide 6: WF on network deployment for inter-band DL CA based on CBM
network deployment restriction for CBM
  There are no deployment restrictions (Non-co-located/co-located) for network to configure inter-band DL CA for CBM UEs.
  UE RF requirements for CBM shall be derived based on co-located deployment scenario only.

## Slide 7: WF on Fs_inter_CBM for inter-band DL CA within same frequency group based on CBM
Fs_inter_CBM
  RAN4 needs to further discuss whether or not introduce ‘Fs_inter_CBM’ as UE capability to indicate the maximum frequency span between lower edge of lowest CC and upper edge of highest CC in FR2 inter-band CA based on CBM which UE can support (as Fs in 5.3A.4 of TS38.101-2)

## Slide 8: Reference
R4-2102986 Email discussion summary for [98e][138] NR_RF_FR2_req_enh2_Part_1, Moderator (Nokia)
R4-2102987 Email discussion summary for [98e][139] NR_RF_FR2_req_enh2_Part_2, Moderator (Qualcomm)