## Slide 1: WF on test cases for IAB-MTs
ZTE Corporation
3GPP TSG-RAN WG4 #98-e
Electronic Meeting, Jan. 25-Feb. 5, 2021
R4-2103540

## Slide 2: Way Forward - Core Maintenance
Remove gap patterns for IAB-MTs completely from TS 38.174 RRM requirements.

## Slide 3: Way Forward - Test configurations
Test configurations for IAB-MTs shall take TS 38.133 Annex as baseline. IAB-MTs are to be tested under specific and simplified test configurations which are specified in TS 38.133 Annex.

## Slide 4: Way Forward - Test configurations
Tests can be done for any TDD configuration. TDD pattern and related configurations shall be configurable and left for implementation including
  DL/UL scheduling related configuration
  PRACH and SRS configuration
  SSB/CSI-RS configuration

## Slide 5: Way Forward - Test configurations
In IAB-MT RRM tests only one serving cell shall be considered. However, there can be more than one cell in some tests to account for a target cell e.g. RRC re-establishment and RRC release with redirection.

## Slide 6: Way Forward - Test configurations
In IAB-MT RRM test requirements are derived using the corresponding configuration parameters as example. The actual IAB-MT RRM test can be conducted by any set of configuration parameters and corresponding test requirements shall be based on the actual configuration parameters used in the test.

## Slide 7: Way Forward - Test configurations
AoA related configurations are based on declaration. Only indicate the number of AoAs in the test cases.
No test cases and configurations defined with DRX, CA or DC.

## Slide 8: Way Forward - Test cases
As agreed in previous meeting that no conformance testing will be defined for IAB-MT, the corresponding reference to conformance tests shall be removed to avoid ambiguities when specifying requirements and test cases in TS 38.174.

## Slide 9: Way Forward - Test cases
Not to have separate test cases for timing advance for both WA IAB-MT and LA IAB-MT.

## Slide 10: Way Forward - Test cases
Only define performance test cases for LA IAB-MT.

## Slide 11: Way Forward - Test cases
Following test cases are defined to verify RRC re-establishment requirements in clause 12.1.1.1, TS 38.174:
  TC1: Inter-frequency RRC Re-establishment in FR1 for LA IAB-MT and IAB type 1-H
  TC2: Intra-frequency RRC Re-establishment in FR1 without serving cell timing for LA IAB-MT and IAB type 1-H
  TC3: Inter-frequency RRC Re-establishment in FR2 for LA IAB-MT and IAB type 1-O
  TC4: Intra-frequency RRC Re-establishment in FR2 without serving cell timing for LA IAB-MT and IAB type 1-O

## Slide 12: Work split
RRM Test cases | Related RRM Requirements | Applicability | Company
RRC Re-establishment in FR1 | 12.1.1.1 SA: RRC Re-establishment | 1-H LA | 
RRC Re-establishment in FR2 |  | 2-O LA | 
RRC Connection Release with Redirection to NR in FR1 | 12.1.1.3 SA: RRC Connection Release with Redirection to NR | 1-H LA | Huawei
RRC Connection Release with Redirection to NR in FR2 |  | 2-O LA | 
IAB-MT transmit timing in FR1 | 12.2.1 IAB-MT transmit timing | 1-H LA | ZTE
IAB-MT transmit timing in FR2 |  | 2-O LA | 
RLM OOS with SSB in FR1 | 12.3.1.2 Requirements for SSB based radio link monitoring | 1-H LA | 
RLM OOS with SSB in FR2 |  | 2-O LA | 
RLM IS with SSB in FR1 |  | 1-H LA | 
RLM IS with SSB in FR2 |  | 2-O LA | 
RLM OOS with CSI-RS in FR1 | 12.3.1.3 Requirements for CSI-RS based radio link monitoring | 1-H LA | 
RLM OOS with CSI-RS in FR2 |  | 2-O LA | 
RLM IS with CSI-RS in FR1 |  | 1-H LA | 
RLM IS with CSI-RS in FR2 |  | 2-O LA | 
Beam Failure Detection and Link Recovery with SSB in FR1 | 12.3.2.2 Requirements for SSB based beam failure detection12.3.2.5 Requirements for SSB based candidate beam detection | 1-H LA | 
Beam Failure Detection and Link Recovery with CSI-RS in FR1 | 12.3.2.3 Requirements for CSI-RS based beam failure detection12.3.2.6 Requirements for CSI-RS based candidate beam detection | 1-H LA | 
Beam Failure Detection and Link Recovery with SSB in FR2 | 12.3.2.2 Requirements for SSB based beam failure detection12.3.2.5 Requirements for SSB based candidate beam detection | 2-O LA | 
Beam Failure Detection and Link Recovery with CSI-RS in FR2 | 12.3.2.3 Requirements for CSI-RS based beam failure detection12.3.2.6 Requirements for CSI-RS based candidate beam detection | 2-O LA |