## Slide 1: WF on core part maintenance of CSI-RS based L3 measurement requirements
Apple, …
3GPP TSG-RAN WG4#98-e Meeting R4-2103629
Electronic Meeting, 25th Jan – 5th Feb., 2021

## Slide 2: WF on CSI-RS based L3 measurement
On CSI-RS resources in the same MO with different offset
  Option 1: All CSI-RS resources in the same MO are configured in the same 5ms window.
  Option 2: Different CSI-RS resources in the same MO may fall in different 5ms window.
No clarification on refFreqCSI-RS is needed in RAN4.
Starting point of 5ms L CSI-RS window is to be specified in R16 with details FFS
  Option 1: Define the starting point of the 5ms window as the slot boundary of the first configured L3 CSI-RS resource is located.
  Option 2: Define the starting point of the 5ms window based on the resource with smallest offset which may not be the first resource.
  Other options are not precluded.MG sharing mechanism between SSB based and CSI-RS based L3 measurement
Gap sharing mechanism defined in 9.1.2 should be applicable to inter-frequency CSI-RS measurement
    CSI-RS L3 and SSB L3 are considered as different frequency layers regardless they are configured in the same or different MO
    CSI-RS and SSB based L3 measurements are subject to the same value of parameter X corresponding to measGapSharingScheme

## Slide 3: WF on CSI-RS based L3 measurement
On Scheduling restriction
  On intra-frequency measurement scheduling restriction for TDD band
    Option 1: When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit on data OFDM symbols overlapped by CSI-RS resource symbols to be measured, and 1 OFDM symbols before and after each consecutive CSI-RS symbols, where the serving cell is taken as the symbol level timing reference.
    Option 2: When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit PUCCH/PUSCH/SRS on CSI-RS resource symbols to be measured, and on 1 OFDM symbol before and after each consecutive CSI-RS symbols to be measured.
  For intra-band carrier aggregation, the scheduling restriction due to a given serving cell should also apply to all other serving cells in the same band.
  For inter-band carrier aggregation in FR2, there are no scheduling restrictions on the serving cells in the bands due to CSI-RS based measurement in different bands, provided that UE is capable of independent beam management on this FR2 band pair.
  No more clarification on applicability of the scheduling restriction is needed.