## Slide 1: WF on further RRM enhancement for NR and MR-DC – Handover with PSCell
Apple, …
R4-2103673
3GPP TSG-RAN4 Meeting #98-e
Online, 25 Jan. – 5 Feb., 2021
Agenda item: 11.4
Document for: Approval
Agreement in 1st round
Agreement in GTW (Jan. 29th)
Agreement in 2nd round

## Slide 2: Sub-topic 2-1 Scenarios for RRM requirement of HO with PSCell (1/2)
Issue 2-1-1: Scenarios for RRM requirement of HO with PSCell
  Agreements
    Define RRM requirement for HO with PSCell for following scenarios:
      from NR SA to EN-DC
      from EN-DC to EN-DC
      from NE-DC to NE-DC
      from NR-DC to NR-DC
      FFS on other scenarios

## Slide 3: Sub-topic 2-1 Scenarios for RRM requirement of HO with PSCell (2/2)
Issue 2-1-2: NR-DC and NE-DC mode in HO with PSCell
  FFS:
    Option 1(Apple, CATT, QC, MTK): In R17 RAN4 only considers legacy FR1+FR2 NR-DC for HO with PSCell from NR-DC to NR-DC, and only considers FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
    Option 2(Huawei, Ericsson): In R17 RAN4 considers FR1+FR2 NR-DC and FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC, and only considers FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
    Option 3(tentative compromise)(Apple):
      For HO with PSCell from NR-DC to NR-DC, following scenario(s) are considered in RAN4,
        FR1+FR2 NR-DC
        FFS: FR1+FR1 NR-DC
      For HO with PSCell from NE-DC to NE-DC, following scenario(s) are considered in RAN4,
        FR1+LTE NE-DC
        FFS: FR2+LTE NE-DC
    Option 4(Nokia):
      For HO with PSCell from NR-DC to NR-DC, following scenario(s) are considered in RAN4,
        FR1+FR2 NR-DC
        FR1+FR1 NR-DC
      For HO with PSCell from NE-DC to NE-DC, following scenario(s) are considered in RAN4,
        FR1+LTE NE-DC
        FFS: FR2+LTE NE-DC
Issue 2-1-3: known/unknown cell condition in HO with PSCell
  Agreement:
    Option 1(Apple, NEC, HW, OPPO, Xiaomi, CMCC, Intel, QC, Ericsson, DCM, MTK, Nokia): Known and unknown cell condition in legacy HO and PSCell addition requirement could be reused in the requirement of HO with PSCell. The requirement of HO with PSCell covers following combinations:
      Known target Pcell + Known target PSCell
      Known target Pcell + Unknown target PSCell
      Unknown target Pcell + Known target PSCell
      Unknown target Pcell + Unknown target PSCell

## Slide 4: Sub-topic 2-2 Delay requirement design of HO with PSCell (1/6)
Issue 2-2-1: starting point and ending point of the delay requirement for HO with PSCell
  FFS:
    Option 1 (Apple, Xiaomi, OPPO, NEC): For delay requirement of HO with PSCell, reuse the starting point definition from legacy HO and reuse the ending point definition from legacy PSCell addition, i.e., when the UE receives a RRC message implying handover with PSCell the UE shall be capable to transmit PRACH preamble towards target PSCell within Thandover_with_PSCell from the end of the last TTI containing the RRC command. (Thandover_with_PSCell is the delay requirement of HO with PSCell).
    Option 2 (Qualcomm, MTK): during HO with PSCell, the same starting point is assumed for PCell and PScell, i.e. when the UE receives a RRC message implying handover with PSCell; the ending points should be separately defined as PCell PRACH and PSCell PRACH and the overall ending point can be whichever leg finishes the PRACH preamble at last.
    Option 3 (tentative compromise, Nokia, Apple, Intel, NEC, Ericsson, CATT): For delay requirement of HO with PSCell,
      reuse the starting point definition from legacy HO, i.e., the end of the last TTI containing the RRC command implying handover with PSCell.
      FFS: the ending point
Issue 2-2-2: old PSCell/Scell release during HO with PSCell
  Agreement: RAN4 does not need to consider the old PSCell/SCell release time in the HO with PSCell delay requirement design

## Slide 5: Sub-topic 2-2 Delay requirement design of HO with PSCell (2/6)
Issue 2-2-3: timeline for HO with PSCell
  Agreement
    Identify the detailed components of “HO with PSCell” procedure
      Further discuss whether the procedures could be performed in parallel or sequentially based on the existing requirements.
Issue 2-2-4: optimisation for the case when PSCell is not changed during HO with PSCell
  FFS:
    Option 1 (Intel): For HO with PSCell from NR-DC to NR-DC, if PSCell is not changed, no timing tracking for PSCell is needed. If PSCell is changed, timing tracking for PSCell is needed, scaling factor may be considered.
    Option 2 (Ericsson, Nokia): T∆ reduction when source and target PSCell is the same cell.
    Option 3 (Huawei, Apple, Xiaomi, Intel, QC, MTK, OPPO): For UE which is already configured with DC, the UE’s behaviour is same when the configured PSCell is same as the original one or not.
    Option 4 (CATT): When PSCell is not changed, the requirements for HO with PSCell should be the legacy HO requirement. The PSCell can still work but with interruption caused by PCell HO.
    FFS on other optimizations if any (Qualcomm, OPPO , NEC)

## Slide 6: Sub-topic 2-2 Delay requirement design of HO with PSCell (3/6)
Issue 2-2-5: RRC processing delay for HO with PSCell
  FFS:
    Option 1 (Apple, Huawei): use the max{RRC procedure delay of legacy HO, RRC procedure delay of legacy PSCell addition} for the corresponding RRC procedure delay in the requirement of HO with PSCell. The RRC procedure delays in following table are used for the requirements of HO with PSCell.
    Option 2 (NEC): 16ms
    Option 3 (Xiaomi, CATT, Ericsson, MTK, Nokia, Qualcomm, OPPO): shall be determined by RAN2.
    Agreement: sending LS to RAN2
Scenario | Source PCell | Target PCell | Target PSCell | RRC procedure delay for HO with PSCell
NR SA to EN-DC | NR (incl. FR1 and FR2) | LTE | NR (incl. FR1 and FR2) | 50ms
EN-DC to EN-DC | LTE | LTE | NR (incl. FR1 and FR2) | 20ms
NE-DC to NE-DC | NR FR1 | NR FR1 | LTE | 20ms
NR-DC to NR-DC | NR FR1 | NR FR1 | NR FR2 | 16ms

## Slide 7: Sub-topic 2-2 Delay requirement design of HO with PSCell (4/6)
Issue 2-2-6: UE SW processing and RF warm-up(if needed) time for HO with PSCell
  FFS:
    Option 1 (Apple): Sum of the UE processing time from legacy HO and from legacy PSCell addition for HO with PSCell.
    Option 2 (NEC): Tprocessing is the UE processing time. It can be 20ms or 40 ms depending on same FR or inter FR NR PSCell addition.
    Option 3 (Intel):
      For HO with PSCell from NR-DC to NR-DC, Tprocessing can be split into software processing (Tprocessing_SW) and RF warm up time(Tprocessing_RF). Tprocessing_SW=[20]ms needs further discussion if some extension is needed. Tprocessing_RF will be dependent on different scenarios, i.e. whether Pcell or PSCell change across FRs.
      For HO with PSCell from NR SA to EN-DC, Tprocessing only includes software processing time (Tprocessing_SW). Tprocessing_SW=[20]ms needs further discussion if some extension is needed.
    Option 4 (Ericsson): Tprocessing reduction when source and target PSCell are in same FR
    Option 5 (Nokia, Qualcomm, OPPO): more discussion is needed, waiting for the conclusion from issue 2-2-3

## Slide 8: Sub-topic 2-2 Delay requirement design of HO with PSCell (5/6)
Issue 2-2-7: Delay requirement design if option 1 in issue 2-2-3 is adopted
  FFS:
    Option 1 (Apple , Xiaomi):
      For requirement of HO with PSCell, RAN4 assumes that UE performs target PSCell addition after receiving RAR (msg 2) from target Pcell.
      The cell detection time, AGC settling time, T/F tracking time and RACH uncertainty time in legacy HO and legacy PSCell addition requirement could be reused for HO with PSCell.
    Option 2 (ZTE):
      Take core requirements for handover and PSCell addition as baseline and identify if there is any new issue in the new procedure.
    Option 3 (Xiaomi):
      The additional interruption delay for target PSCell should be considered based on the legacy HO delay requirement for the HO with PSCell delay requirement. And the interruption delay contains the following procedures:
        Cell search time
        Fine timing tracking time
        UE processing time
        Time for interruption uncertainty in acquiring the first available PRACH occasion in the new cell
        Time for SSB post-processing
    Option 4 (Nokia): more discussion is needed, waiting for the conclusion from issue 2-2-3

## Slide 9: Sub-topic 2-2 Delay requirement design of HO with PSCell (6/6)
Issue 2-2-8: Delay requirement design if option 2 in issue 2-2-3 is adopted
  FFS:
    Option 1 (CMCC):
      the delay requirement for handover with PSCell is suggested as following:
        TRRC_delay + Tprocessing + Tsearch + fine time tracking + delay uncertainty in acquiring the first available PRACH occasion + Tmargin
    Option 2 (NEC):
      RAN4 to agree that Tsearch should consider all the four combination of Pcell and PSCell known and unknown conditions; Actual Tsearch is FFS.
      RAN4 to agree that components that contribute to TIU delay are the TA acquisition delay in LTE Pcell, delay uncertainty in acquiring resources for RRC connection Reconfiguration Complete message on LTE Pcell and PRACH acquisition uncertainty delay in NR PSCell.
      T∆ is time for fine time tracking and acquiring full timing information of the NR PSCell. Where T∆ = Trs.
    Option 3 (Intel):
      For HO with PSCell from NR-DC to NR-DC, if target Pcell and PSCell are in different FR, cell search can be performed independently as different searcher for FR1 and FR2 are assumed. If target Pcell and PSCell are in the same FR, scaling factor may be considered.
      For HO with PSCell from NR-DC to NR-DC, the uncertainty in acquiring the first available PRACH occasion in the Pcell and PSCell will be max(TIU, TPSCell_ DU ).
      For HO with PSCell from NR SA to EN-DC, Tsearch and T∆ for PSCell can be skipped.
    Option 4 (Huawei):
      The SMTC for AGC may be jointly considered when the target Pcell and the target PSCell are within the same band.
    Option 5 (Qualcomm):
      Joint/concurrent PCell HO with PSCell change/add takes [TFFS]ms longer in the timelines of both PCell and Pscell than performing standalone PCell HO task or standalone PSCell add/change.
      As a starting point for discussion, TFFS may be chosen as 10ms. RAN4 can further discuss if TFFS shall be adjusted differently in various scenarios.
    Option 4 (Nokia): more discussion is needed, waiting for the conclusion from issue 2-2-3

## Slide 10: Sub-topic 2-3 Interruption requirement design of HO with PSCell
Issue 2-3: Interruption requirement for HO with PSCell
  FFS:
    Option 1 (ZTE): For interruption requirements, consider the following options:
      Specify a total interruption for handover and PSCell addition
      Specify separate interruptions for handover and PSCell addition.
    Option 2 (Xiaomi): when UE is ready to be scheduled on the new PCell during the interruption time for PSCell, the following options can be considered for the UE behavior.
      Option 2-1: UE is not expected to be scheduled on the new PCell during the HO with PSCell procedure;
      Option 2-2: UE can be scheduled on the new PCell but define interruption requirement between the time PCell is ready for scheduling and the time UE starts the transmission of the new PRACH on the new PSCell.
    Option 3 (Nokia, Qualcomm, OPPO): more discussion is needed, Waiting for the conclusion from issue 2-2-3

## Slide 11: Sub-topic 2-4 Generic RACH assumption for HO with PSCell
Issue 2-4-1: 2 step and 4 step RACH for HO with PSCell
  FFS:
    Option 1 (ZTE, Ericsson, Nokia): Include both 2-step RA and 4-step RA into the new requirements made for handover with PSCell.
    Option 2 (Apple, Xiaomi, CATT, MTK, OPPO): start the discussion with 4 step RACH first and FFS on 2 step RACH.
    Option 3 (QC): wait conclusion of issue 2-2-3
Issue 2-4-2: RACH occasion collision between Pcell and PSCell
  FFS:
    Option 1 (Huawei, Apple, Xiaomi, Ericsson, MTK, CATT): There is no need to further consider the RO collision issue from RAN4’s perspective.
    Option 2 (Huawei, Intel, Qualcomm): wait conclusion of issue 2-2-3.
    Option 3 (Nokia): need more discussion

## Slide 12: Sub-topic 2-5 Others
Issue 2-5: Failure case definition for HO with PSCell
  FFS:
    Option 1 (NTT DCM): Regarding HO with PSCell, the scenario that UE fails to synchronize to the expected SCG is possible. If such failure scenario occurs, one of the two solutions described as below should be taken.
      a. UE performs conventional Rel-15 HO procedure and SCG addition separately.
      b. UE tries to synchronize another SCG which is the most likely to connect successfully. (b. assumes that the target PCell configures multiple SCGs.)
    Option 2 (DCM, CATT, Ericsson, Nokia, Qualcomm, OPPO): Need to be clarified by RAN2
    Option 3 (Apple, OPPO): in HO with PSCell if UE completed PCell HO but failed the PSCell addition, the whole event of HO with PSCell shall be considered as “failed”, and no RRC complete signaling would be sent to network.
  Agreement: sending LS to RAN2.