## Slide 1: WF on high DL power and low UL power test cases (objective1) and band n262 testability (objective7)
Apple
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 January – 5 February, 2021
Agenda Item: 12.1
R4-2103918

## Slide 2: High DL power / low UL power test cases (1)
Related to the CFFNF system
  Techniques for CFFNF with transform + black box
    Three radii approach (i.e. local search on radius r1 and very localized searches at r2 and r3) based on the asymptotic expansion transform can be used.
    Other methods are not precluded
  Techniques for CFFNF with transform + black&white box
    Two radii approach (without local searches) based on the asymptotic expansion transform can be used.
    Other methods are not precluded
Related to the CFFDNF system
  The low PSD EIRP/EIS test cases in known FF BP direction are not applicable to the black box approach
    This can be revised whenever empirical methods to determine the offset location are shown feasible
  CFFDNF + black&white box is applicable to low PSD EIRP/EIS test cases in known FF BP direction
    Whether a local search to determine the NF test direction and/or optimize EIRP/EIS is FFS.
    EIRP/EIS can be approximated in the NF (min. range lengths for PC1 and PC3 are FFS)
  TRP test cases at very close distances require offset compensation while range lengths beyond 32cm for PC3 do not necessarily require offset compensation.
Impact of local searches on test time to be investigated by next meeting

## Slide 3: High DL power / low UL power test cases (2)
Minimum range length definition
  Option 1: according to the effective radiating aperture concept
  Option 2: based on acceptable TRP MU impact
Further analysis of these options is encouraged by the next meeting
f [GHz] | Effective Aperture [cm] Deff | CFFDNF Derat Distance | CFFNF Radiative NF boundary
24.25 | 5.10 | 0.32 | 0.19
30 | 4.12 | 0.28 | 0.18
40 | 3.09 | 0.25 | 0.17
43.5 | 2.84 | 0.24 | 0.17
52.6 | 2.35 | 0.23 | 0.17
f [GHz] | Effective Aperture [cm] Deff |  | 
24.25 | 5.10 | 0.32 | 0.19
30 | 4.12 | 0.28 | 0.18
40 | 3.09 | 0.25 | 0.17
43.5 | 2.84 | 0.24 | 0.17
52.6 | 2.35 | 0.23 | 0.17
Test distance (cm) | Grid (degree) | With Correction |  | No Correction | 
 |  | Mean TRP Error [dB] | TRP Std. Dev. [dB] | Mean TRP Error [dB] | TRP Std. Dev. [dB]
20 | 5 | -0.01420 | 0.03623 | 0.39449 | 0.24368
 | 7.5 | -0.02402 | 0.12553 | 0.39474 | 0.24664
 | 10 | -0.02944 | 0.16512 | 0.39100 | 0.29085
32 | 5 | -0.02238 | 0.01213 | 0.14085 | 0.08250
 | 10 | -0.03522 | 0.03330 | 0.14109 | 0.08532
43 | 5 | -0.02409 | 0.01027 | 0.07626 | 0.04411
 | 10 | -0.03733 | 0.02504 | 0.07631 | 0.04444

## Slide 4: High DL power / low UL power test cases (3)
Summary of options to conclude the applicability of the DNF system:
  Option 4:
    Beam peak searches and spherical coverage test cases are not applicable regardless of black-box or black&white-box approach. Performing these tests with the NF measurement probe would require the extensive black&white-box approach which is not deemed a feasible enhancement of the methodology.
    The low UL power/high DL power EIRP/EIS test cases in the known FF BP direction as well as spherical coverage and beam peak search are not applicable to the black box approach.
    The applicability of the low UL power/high DL power EIRP/EIS test cases in the known BP direction and with the black&white-box approach is FFS.
  Option 5:
    Beam peak searches and spherical coverage test cases are not applicable to black-box. For black&white-box approach, performing these tests with DNF would require the antenna array panel offset to be declared. This could be seen complex in case of multi-panel UE (multi-panel per band)
    The low UL power/high DL power EIRP/EIS test cases in the known FF BP direction as well as spherical coverage and beam peak search are not applicable to the black box approach.
    The applicability of the low UL power/high DL power EIRP/EIS test cases in the known BP direction and with the black&white-box approach is FFS.
  Option 6:
    Capture DNF for Beam peak searches and spherical coverage test cases in TR, meanwhile such method is not RAN4 recommendation
Agreement:
  Adopt option 4 as RAN4 conclusion meanwhile capture DNF for Beam peak searches and spherical coverage test cases into TR

## Slide 5: Band n262 testability (1)
The QoQZ MUs at 49 GHz presented by one company are within the example MU value defined in RAN5
  Little to no increase in QoQZ MU is expected for 49 GHz
Make the following changes to the “Multiple antenna” MU element:
  MU element description
  The applicability
  Potentially the MU element sample value

## Slide 6: Band n262 testability (2)
All open issues identified in RAN4 #97 WF [R4-2017599] remain open
Companies are encouraged to contribute their views toward closing these issues in the next meeting

## Slide 7: References
T-doc number | Company | Title
R4-2100525 | Apple Inc. | TP to TR38.884 on High DL and Low UL power test cases
R4-2101485 | MVG Industries, Sony | Overview of the Impact of phase variation for Direct NF Method
R4-2102616 | Keysight Technologies | On Test methodology for high DL power and low UL power test cases
R4-2102620 | Rohde & Schwarz | NF based solutions and Enhancement of permitted methods
R4-2102619 | Keysight Technologies | On Testability for band n262
R4-2100530 | Apple Inc. | TP to TR38.884 on structure updates related to band n262