## Slide 1: Way Forward on NR-U PUCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, Jan. 25th – Feb. 5th, 2021
Agenda: 7.1.7.4.3
R4-2103989
Document for: Approval

## Slide 2: Background
R4-2103934, Email discussion summary for [98e][317] NR_unlic_Demod_BS
R4-2017467, Way Forward on NR-U PUCCH demodulation requirements, Ericsson

## Slide 3: General test configurations
PUCCH formats
  Define the performance requirements for Rel-16 PF 0/1/2/3 with interlace resource allocation
Number of interlaces
  1 interlace for PF 0/1/2/3
Antenna configuration
  1Tx2Rx
Bandwidth
  Define the NR-U PUCCH requirements with 20MHz bandwidth
Frequency hopping
  Not configure frequency hopping
SCS
  15 kHz and 30 kHz
Propagation conditions
  TDLA30-10 Low

## Slide 4: PUCCH format 0
Parameter | Test
Number of UCI information bits | 1
Number of symbol | 1
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Initial cyclic shift | 0
First symbol | 13
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Number of interlaces | 1
Interlace index | 0 Note1
Propagation conditions | TDLA30-10 Low
Test metric | SNR@Prob(ACK missed)≤10-2 SNR@Prob(DTX->ACK)≤10-2
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz if agreed and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Number of symbols
  Only test 1 OFDM symbol for PF0
Test metric
  only Rel-15 test metric
    SNR@Prob(ACK missed)≤10-2
    SNR@Prob(DTX->ACK)≤10-2

## Slide 5: PUCCH format 1
Parameter | Test
Number of information bits | 2
Number of symbols | 14
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Initial cyclic shift | 0
First symbol | 0
Index of orthogonal cover code (timeDomainOCC) | 0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Number of interlaces | 1
Interlace index | 0 Note1
Propagation conditions | TDLA30-10 Low
Test metric | SNR@Prob(ACK miss)≤10^(−2) SNR @Prob(PUCCH DTX→Ack bits) ≤ 10^(−2) SNR@Prob(NACK→ACK)≤10^(−3)
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz if agreed and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Test metric
  only Rel-15 test metric
    SNR@Prob(ACK miss)≤10^(−2)
    SNR @Prob(PUCCH DTX→Ack bits) ≤ 10^(−2)
    SNR@Prob(NACK→ACK)≤10^(−3)

## Slide 6: PUCCH format 2
Number of interlaces
  One interlace
Number of OFDM symbols
  One OFDM symbol
Information bits
  22 bits
OCC configuration
  Not configure
Parameter | Value
Modulation order | QSPK
Intra-slot frequency hopping | N/A
Number of symbols | 1
The number of UCI information bits | 22
First symbol | 13
DM-RS sequence generation | NID0=0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Number of interlaces | 1
Interlace index | 0 Note 1
Propagation conditions | TDLA30-10 Low
OCC-Length-r16 | Not configured
Test metric | 
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Parameter | Value
Modulation order | QSPK
Intra-slot frequency hopping | N/A
Number of symbols | 1
The number of UCI information bits | 22
First symbol | 13
DM-RS sequence generation | NID0=0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Number of interlaces | 1
Interlace index | 0 Note 1
Propagation conditions | TDLA30-10 Low
OCC-Length-r16 | Not configured
Test metric | 
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz and RBs 0,5,10,…,50 are allocated for 30kHz. | 

## Slide 7: PUCCH format 3
Number of interlaces
  One interlace
information bits
  4 bits
  FFS on 16 bits
Number of OFDM symbols
  4
  FFS on 14
OCC length
  Option 1: OCC length n2 and OCC index n0
  Not configure
Parameter | Test 1
Modulation order | QPSK
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Additional DM-RS configuration | No additional DM-RS
Number of symbols | 4
The number of UCI information bits | 4 bits
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Antenna configuration | 1T2R
Number of interlaces | 1
Interlace index | 0Note 1
Propagation conditions | TDLA30-10 Low
Index of OCC | Not configure
Length of OCC | Not configure
Cyclic shift index for DMRS | 0
Test metric | 
Note 1: RBs 0, 10, 20,…,90 are allocated for 15kHz and RBs 0,5,10,…,45 are allocated for 30kHz. Note 2: The UCI information does not contain CSI part 2. | 
Parameter | Test 1
Modulation order | QPSK
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Additional DM-RS configuration | No additional DM-RS
Number of symbols | 4
The number of UCI information bits | 4 bits
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Antenna configuration | 1T2R
Number of interlaces | 1
Interlace index | 0Note 1
Propagation conditions | TDLA30-10 Low
Index of OCC | Not configure
Length of OCC | Not configure
Cyclic shift index for DMRS | 0
Test metric | 
Note 1: RBs 0, 10, 20,…,90 are allocated for 15kHz and RBs 0,5,10,…,45 are allocated for 30kHz. Note 2: The UCI information does not contain CSI part 2. | 
Notes: GTW agreement
information bits
  4 bits
  FFS on 16 bits
Number of OFDM symbols
  4
  FFS on 14
OCC length
  Option 1: OCC length n2 and OCC index n0
  Option 2: Not configure
: