## Slide 1
WF on FR2 DL contiguous CA BW enhancement
and new CA bandwidth classes
3GPP TSG-RAN WG4 Meeting # 96-e R4-2103110
Electronic Meeting, 25th January – 5th February, 2021
Agenda Item: 11.3.1
Verizon

## Slide 2: Background New FR2 bandwidth classes
During 1st round of discussion in [138], following proposal was discussed based on [1].
  Issue 1-1-1: New FR2 bandwidth classes
  Proposals
    Option 1: Add 4 new CA BW classes to FBG2 and 8 new CE BW classes to FBG3
    Option 2: Do not add new CA BW classes
    Option 3: Add new CA BW classes but differently as in option 1.
Majority supported option 1 (5 companies) and one companies supported 4 new classes
  A common observation is that the naming convention for the new CA BW classes may need to be reconsidered
A WF is recommended for further discussion

## Slide 3: WF on New FR2 bandwidth classes
RAN4 considers that there is a need to add a new objective in scope of Rel-17 FR2 UE WID which is
  Introduce new CA BW classes and related Rx requirements to support of contiguous downlink aggregated channel BW up to 1600 MHz
Decision whether WID is updated is discussed in RAN#91e

## Slide 4: Reference
R4-2100264, Release 17 FR2 bandwidth class, Verizon
R4-2102986, Email discussion summary for [98e][138] [98e][138] FR_RF_FR2_req_enh2_Part_1, (Nokia)