## Slide 1: WF on simulation assumptions for system performance evaluation Moderator(China Unicom)
3GPP TSG-RAN WG4 Meeting #98-e R4-2103274
Electronic Meeting, Jan. 25– Feb. 05, 2021

## Slide 2: Dynamic system level simulation
Configuration parameters | Values
Scenario | Urban macro
ISD | 500 m
Duplexing | FDD
Carrier frequency | 1.8 GHz, 2.1GHz
Modulation | Up to 64QAM, 256QAM is optional
Numerology | 15 kHz
Simulation bandwidth | 40 MHz
Transmission scheme | SU-MIMO
Codebook | For 2Tx, codebook [1 1]T is used for transmit diversity
SU dimension | 1 layer
Antenna configuration at TRxP | 4Rx, (M,N,P,Mg, Ng) = (1,2,2,1,1; 1,2); 4Rx, (M, N, P, Mg, Ng) = (1, 4, 2, 1, 2) 32Rx, (M,N,P,Mg, Ng) = (8,8,2,1,1; 2,8)
Antenna configuration at UE | 1Tx, (M,N,P,Mg, Ng) = (1,1,1,1,1; 1,1), 2Tx, (M,N,P,Mg, Ng) = (1,1,2,1,1; 1,1)
UE maximal transmit power | For 1Tx, 23 dBm for each TXRU For 1Tx, 26 dBm for each TXRU (High power UE) For 2Tx, 23 dBm for each TXRU (High power UE)
Scheduling | PF
Receiver | MMSE-IRC
Channel estimation | Ideal
Power control parameter | P0=[-60~-76], alpha = [0.6, 0.8]
TRxP number per site | 3
TRxP number | 21
Channel model | UMa following TR 38.901
Electronic tilt | 102°
Traffic model | FTP3, packet size: 100k / 10k Byte, arrival rate: [1 packet / s, 1 packet/200ms]
Uplink duty cycle | 50%, 100%
Note: HPUE ratio 100% baseline, 50% and 25% are optional

## Slide 3: Monte Carlo simulation
Environment | ISD (KM) | ISD (miles)
Urban | .75 | .47
Suburban | 2.8 | 1.74
Rural | 6 | 3.73
Rural | 8 | 5
 | Base Station | UE
Carrier frequency | 2GHz | 
Channel bandwidth | 40MHz, 20 MHz, 10 MHz | 
UL duty cycle | 100% | 
Active UE number in UL | [3] | 
Inter-site distance | Use Table 2 | 
Cell layout | Wrap-around 19 tri-sector cells | 
Frequency reuse | 1x3x1 | 
Lognormal fading | 10 dB | 
Shadowing correlation | Between cells: 0.5, between sites: 1.0 | 
MCL (including antenna gain) | 70 dB (urban and suburban areas) 80 dB (rural area) | 
Antenna gain and horizontal antenna pattern | 17 dBi, = 65 degrees, Am = 20 dB | Omni-directional antenna with -3.5 dBi.
Noise figure | 5 dB | 9 dB
Transmit power | 46 dBm | 23 dBm
Antenna height | 45 m | 1.5 m
 | Base Station | HPUE
Carrier frequency | 2GHz | 
Channel bandwidth | 40MHz, 20 MHz, 10 MHz | 
UL duty cycle | [50%] | 
Active UE number in UL | [3] | 
HPUE ratio | 100% baseline, [50%, 25% optional] | 
Inter-site distance | Use Table 2 | 
Cell layout | Wrap-around 19 tri-sector cells | 
Frequency reuse | 1x3x1 | 
Lognormal fading | 10 dB | 
Shadowing correlation | Between cells: 0.5, between sites: 1.0 | 
MCL (including antenna gain) | 70 dB (urban and suburban areas) 80 dB (rural area) | 
Antenna gain and horizontal antenna pattern | 17 dBi, = 65 degrees, Am = 20 dB | Omni-directional antenna with -3.5 dBi.
Noise figure | 5 dB | 9 dB
Transmit power | 46 dBm | 26 dBm
Antenna height | 45 m | 1.5 m
(a) With 23 dBm UE
(b) With 26 dBm UE

## Slide 4: Way Forward
Companies are encouraged to bring simulation results for system gain [and UE Tx power CDF curve] based on assumptions from previous pages.
  26dBm MoP VS 23dBm MoP for FDD PC2 for n1 or n3
  26dBm MoP VS 23dBm MoP for TDD PC2 assuming the same frequency carrier with n1 or n3.
Other results are not precluded