## Slide 1: Way Forward on Test Cases for SCell Dormancy
Ericsson, ...
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, Jan 25 – Feb 5, 2021
R4-2103563
Document for: Approval

## Slide 2: Background Test Case list from RAN4#97e
# | Test case description | Sourcing company
TC1 | EN-DC, NR spCell in FR1, SCell FR1, DCI 2_6 within/after 3 OFDM symbols | Apple
TC2 | EN-DC, NR spCell in FR1, 2xSCell in FR1, DCI 0_1/1_1 within/after 3 OFDM symbols | MediaTek
TC3 | EN-DC, NR spCell in FR2, SCell in FR2, DCI 0_1/1_1 within/after 3 OFDM symbols | Huawei
TC4 | EN-DC, NR spCell in FR1, 2xSCell in FR2, DCI 2_6 within/after 3 OFDM symbols | Qualcomm
TC5 | SA, spCell in FR1, SCell FR1, DCI 2_6 within/after 3 OFDM symbols | NEC
TC6 | SA, spCell in FR1, 2xSCell in FR1, DCI 0_1/1_1 within/after 3 OFDM symbols | Ericsson
TC7 | SA, spCell in FR2, SCell in FR2, DCI 0_1/1_1 within/after 3 OFDM symbols | Nokia
TC8 | SA, spCell in FR1, 2xSCell in FR2, DCI 2_6 within/after 3 OFDM symbols | Ericsson

## Slide 3: Agreements in RAN4#98e (1/5)
Agreement:
  Add pre-defined CSI-RS configurations to TS 38.133 clause A.3.14 for periodic CSI-RS with 40ms periodicity.[Issue 3-1-1]
Agreement:
  Test the switching both from dormancy to non-dormancy and non-dormancy to dormancy.[Issue 3-1-3]

## Slide 4: Agreements in RAN4#98e (2/5)
Agreement:
  For test cases with DCI 2_6, set the gap ps-Offset between PDCCH WUS and next onDuration to the allowed SCell dormancy switching time given the UE’s reported capabilities.[Issue 3-1-5]
Agreement:
  RAN4 to establish a common test framework for SCell dormancy requirements in terms of test methods for requirement verification, e.g. # missing HARQ-ACK/NACKs within specific windows, etc.[Issue 3-1-6]

## Slide 5: Agreements in RAN4#98e (3/5) Alignment of TCs 1, 4, 5 and 8 (outside active time)
Agreement:
  T1: UE receives DCI 2_6 for switching SCell(s) from non-dormancy to dormancy. Testing of interruption length on other serving cell(s).
  T2: UE conducts CSI and RRM measurements on dormant SCell(s). Testing of interruption rate on other serving cell(s). Keep UE active by addressing UE on PDCCH in spCell to keep inactivity timer running long enough to acquire statistics on interruption rate.
  T3: UE conducts CSI and RRM measurements on dormant SCell(s). No scheduling on PDCCH in spCell, inactivity timer expires.
  T4: UE receives DCI 2_6 for switching SCell(s) from dormancy to non-dormancy. Testing of interruption length on other serving cell(s). Testing of dormancy switching delay time.
  ps-Offset between PDCCH WUS and next onDuration is configured to correspond to the allowed SCell dormancy switching time, and based on the UE’s reported capabilities
  CSI-RS: Specify CSI-RS for dormant BWP
  Triggering timing: ●within initial 3 OFDM symbols, ●after initial 3 OFDM symbols of a slot

## Slide 6: Agreements in RAN4#98e (4/5) Alignment of TCs 2, 3, 6 and 7 (inside active time)
  Agreement:
  T1: UE receives DCI 1_1/0_1 with dormancy indication switching SCell(s) from non-dormancy to dormancy. Testing interruption length on other serving cell(s).
  T2: UE conducts CSI and RRM measurements on dormant SCell(s). Testing of interruption rate on other serving cell(s). T2 shall be long enough to allow reliable statistics on interruption rate, measured as missed ACK/NACK rate.
  T3: UE receives DCI 1_1/0_1 with dormancy indication switching SCell(s) from dormancy to non-dormancy. Testing interruption length on other serving cell(s). Testing dormancy switching delay time.
  CSI-RS: Specify CSI-RS for dormant BWP
  Triggering timing: ●within initial 3 OFDM symbols, and ●after initial 3 OFDM symbols of a slot
  DCI format: ●DCI 1_1
  Scheduling option DCI 1_1: Scheduling and/or non-scheduling DCI is for further discussion. Assume scheduling DCI for now and update later if needed.

## Slide 7: For further discussion until RAN4#98-bis-e (5/5)
  Issue 3-1-2: Pre-defined Dormant BWP configuration
  Option 1: Add pre-defined Dormant DLBWP to TS 38.133 clause A.3.9.2 with same parameters as for DLBWP.1.1.
  Option 2: Dormant BWP can be specified in test case as any of the existing DLBWPs.
  Issue 3-1-4: Whether to specify scheduling or non-scheduling DCI in tests for triggering during active time with DCI format 1_1
  Option 1: Leave the choice of scheduling/non-scheduling DCI 1_1 to RAN5 or TE implementation
  Option 2: Scheduling DCI 1_1 is default for the test cases
  Option 3: Scheduling DCI 1_1 used from dormant to non-dormant BWP and non-scheduling DCI 1_1 used from non-dormant to dormant BWP

## Slide 8: For RAN4#98-bis-e
  Test cases endorsed in RAN4#98e will be collected in a Big Draft CR, which after e-mail endorsement will serve as baseline for future work.
  Companies are invited to, using the endorsed Big Draft CR as baseline,
  further work on improving and aligning test cases
  further provide views and proposals on Issue 3-1-2 and Issue 3-1-4