## Slide 1: 3GPP TSG-RAN WG4 Meeting #98-e Electronic Meeting, 25th Jan. - 5th Feb. 2021
Intel
WF on NR Positioning Performance Requirements
R4-2103586

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
Still open for discussion

## Slide 3: Measurement Accuracy Requirements for RSTD(1)
Antenna panel assumption:
  RAN4 not to define separate accuracy requirements for RSTD measured with same panel and with different panels and
  the same accuracy requirements will be defined, which are based on the earlier simulation results (which did not assume different panels, according to the agreed simulation assumptions)
  Possible margin for different group delay calibration error in different panels can be considered
Applicable accuracy requirement in case of any serving cell change: FFS
  Option 1: Applicable accuracy requirements are not impacted by HO.
  Option 3 : The UE shall continue and complete an RSTD measurement while meeting RSTD measurement accuracy requirements in clause 10.1.23 even when a serving cell change occurs during the measurement.
Applicable propagation channel for accuracy requirement: FFS
  Option 1 : No need to define the applicability for propagation channels in accuracy requirement.
  Option 2a : Captured in the specification the propagation channel models based on which the accuracy requirements are derived.
  Option 2b: RAN4 to consider defining PRS-RSTD and UE Rx-Tx measurement accuracy requirements only for AWGN
FFS on the group delay calibration margin.
  margin equals to zero if the reference and neighbouring resources are on the same frequency layer in FR1
  32Tc, reference resource and neighbour resource are on different PRS layer

## Slide 4: Measurement Accuracy Requirements for RSTD(2)
RSTD accuracy requirements are defined to cover all BW configurations
Different RSTD accuracy requirements depend on the following parameters
  PRS BW defined in number of PRBs
Companies are encouraged to bring PRS accuracy simulation results in RAN4 #99e for the identified set of parameters
  PRS BW defined in number of PRBs
  PRS SCS
  dl-PRS-ResourceRepetitionFactor
  dl-PRS-NumSymbols
  dl-PRS-CombSizeN
  Other parameters are FFS
  Note: the full set of parameters and values were included in R4-2104046 or its revision , which will be also used as the template used to collect the simulation results also.
In the next meeting, the exact accuracy requirements can be defined from the simulation results based on the parameter sets listed in R4-2104046 or its revision .
  The simulation results can still be updated in the next meeting
  Depending on the final required accuracy numbers, not all parameters from R4-2104046 need to be present in the final accuracy requirements

## Slide 5: Measurement Accuracy Requirements for PRS RSRP(1)
PRS-RSRP SINR side condition #1 is [-3] dB. Companies are encouraged to bring simulation results for -3dB and -6dB SINR conditions.
The full set of parameters and values used for PRS RSRP simulations were included in R4-21xxxxx.
In the next meeting, the exact accuracy requirements can be defined from the simulation results, based on the parameter sets listed in R4-2104046
  The simulation results can still be updated in the next meeting
  Depending on the final required accuracy numbers, not all parameters from R4-2104046 need to be present in the final accuracy requirements
RF calibration margin: FFS
  Option 1: The RF margin for PRS-RSRP accuracy is defined as
    2.5dB for FR1 absolute accuracy requirements
    4dB for FR2 absolute accuracy requirements
    0dB for FR1 relative accuracy requirements
    0dB for FR2 relative accuracy requirements, provided that two PRS-RSRP are measured with the same Rx beam

## Slide 6: Measurement Accuracy Requirements for UE Rx-Tx time difference(1)
SINR side conditions for #1 is [-3dB]
Applicability of accuracy requirements in the case of NTA_offset change : FFS
  Option 1: Clarify in section 10.1.25.2 in TS 38.133: “UE Rx-Tx time difference accuracy requirements shall not apply if NTA_offset defined in Table 7.1.2-2 in 38.133 changes during the UE Rx-Tx measurement period.”
  Option 2 :Capture in the specification that UE Rx-Tx accuracy requirements do not apply in case the UE UL timing changes during the measurement period
Applicability of accuracy requirements under TA adjustment : FFS
  Option 1 : UE Rx-Tx measurement accuracy requirements shall not apply if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment or based on network-configured TA
  Option 2:
    UE Rx-Tx measurement accuracy requirements shall not apply if the uplink transmission timing changes during the UE Rx-Tx measurement period due to network-configured TA command.
    UE Rx-Tx measurement accuracy requirements shall apply if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment
  Option 3: Capture in the specification that UE Rx-Tx accuracy requirements do not apply in case the UE UL timing changes during the measurement period

## Slide 7: Measurement Accuracy Requirements for UE Rx-Tx time difference(2)
Applicable propagation channel for accuracy requirement: Follow the same principle of RSTD accuracy requirements
Applicable accuracy requirement in case of other (non-HO) serving cell changes: FFS
  Option 1 :The UE shall continue and complete a UE Rx-Tx measurement while meeting UE Rx-Tx measurement accuracy requirements in clause 10.1.23, when a serving cell change (including SCell change, addition, release, activation, or deactivation, or PSCell change, addition, or release) occurs during the measurement, provided the cell change does not impact the configuration of the SRS used for the measurement
The full set of parameters and values used for UR Rx-Tx time difference simulation were included in R4-2104046 or its revision .
In the next meeting, the exact accuracy requirements can be defined from the simulation results based on the parameter sets listed in R4-2104046 or its revision
  The simulation results can still be updated in the next meeting
  Depending on the final required accuracy numbers, not all parameters from R4-2104046 need to be present in the final accuracy requirements

## Slide 8: Test case design principles(1)
Test cases for the different deployment scenarios
  Option 1: Only need to define the test cases for SA
  Option 2 : RAN4 will define NR positioning test cases for NR-DC, where PCell is in FR1, and PSCell is in FR2; otherwise define test cases for other deployments with both FR1 and FR2 (e.g., CA or SA with FR1 PCell and FR2 neighbors).
Test cases for the different SINR side condition for UE Rx-Tx time difference : FFS
  Option 1
    Both SINR side conditions for UE Rx-Tx are tested in the same test with two cells.
    For PRS-RSRP, there can be separate tests (e.g., Test 1, Test 2, …) inside the test case, one for each side condition.
  Option 2
    by multiple sub-tests in each TC, or by associating different cells with different Es/Iot in a single test
Test cases for serving carrier frequencies and non-serving carrier frequencies measurements : FFS
  Option 1: define test cases for the serving carrier frequencies and non-serving carrier frequencies. The agreed TC list in R4 #97e shall be updated.
Additional path reporting configuration in test cases :No additional path reporting is configured (additionalPaths is not included in the measurement request)
Additional test cases for RSTD :FFS
  Specify three RSTD measurement accuracy (sub-) tests: Absolute RSTD, Differential RSTD, Additional Path Report
Absolute measurement reporting in test cases: FFS
  Option 1 :Absolute measurement reporting is tested for all PRS measurements

## Slide 9: Test case design principles(2)
General PRS configuration for NR Positioning test case (e.g. PRS periodicity, combsize ,e.t.c) : FFS
SRS configuration for NR Positioning test case: FFS
Number of cells/TRPs for NR Positioning test case : FFS
Number of positioning frequency layers : FFS (depends also on whether serving and non-serving frequency measurements are tested)
Synchronous/Asynchronous cells : FFS
Muting pattern :FFS
Testing procedure: FFS

## Slide 10: Test case design principles(3)
Subsets of accuracy tests :FFS
  Option 1. Define two subtests per accuracy test cases corresponding to different combinations of {Es/Iot, PRS BW}.
  Option 2. In each test case, the NR measurements are tested for multiple measurement bandwidths, with at least:
    the smallest bandwidth,
    a bandwidth from the medium bandwidths range (e.g., >48 PRBs in FR1 or >32 PRBs in FR2),
    a bandwidth from the large bandwidths range (e.g., >132 PRBs in FR1 or >64 PRBs in FR2).
Joint configuration of PRS-RSRP with RSTD and UE Rx-Tx
  No: PRS-RSRP is configured together for DL-TDOA or multi-RTT (nr-RequestedMeasurements in the measurement request indicates no PRS-RSRP is requested together with RSTD or UE Rx-Tx).
Supported test configurations in FR1 and FR2 : FFS