## Slide 1: WF on R16 RRM enhancement part 3 – Multiple SCell activation, inter-frequency measurement without MG, FR2 inter-band CA, UE specific CBW change
Apple, …
R4-2103620
3GPP TSG-RAN4 Meeting #98-e
Online, 25 Jan. – 5 Feb., 2021
Agenda item: 7.13
Document for: Approval
Agreement in 1st round
Agreement in GTW (Jan. 29th)
Agreement in 2nd round

## Slide 2: Multiple SCell activation – core (1/2)
Issue 1-1-1: The RTD(reception timing difference) with contiguous FR1 known cell or active serving cell to the to-be-activated SCell
  Agreement: The RTD (reception timing difference) with contiguous FR1 known cell or active serving cell to the to-be-activated SCell shall be no larger than 260ns
Issue 1-1-2: The RPD(reception power difference) with contiguous FR1 known cell or active serving cell to the to-be-activated SCell.
  Agreement: The RPD(reception power difference) with contiguous FR1 known cell or active serving cell to the to-be-activated SCell shall be no larger than 6dB.
Issue 1-2-1: Extend the assumption in FR1 multiple SCells activation to single FR1 SCell activation
  Agreement: Extend the UE requirement (to skip cell detection for unknown FR1 SCell that is intra-band contiguous to active or known serving cell) to single SCell activation.
Issue 1-2-2: Requirement applicability on the other being-activated SCells during the FR1 multiple SCells activation
  Agreement: No requirement applies for a FR1 unknown SCells being activated, if no requirements apply for one or more of the FR1 unknown SCell(s) being activated with the same MAC CE

## Slide 3: Multiple SCell activation – core (2/2)
Issue 1-2-3: Condition of SMTC configuration to apply multiple SCell activation requirement
  FFS:
    Option 1 (Huawei, Apple, QC, MTK, NEC): Multiple SCell activation requirements apply provided that SMTC offset is same for all SCells activated by the same MAC CE.
    Option 1a: option 1 with clarification on per-FR MG capability and SCells’ condition in the same band
    Option 2 (Ericsson, Nokia): No need to have such restriction of SMTC offset as in option1.
Issue 1-2-4: Condition of SSB offset to apply SCell activation requirement without cell detection
  FFS:
    Option 1 (Huawei, Apple, Ericsson, MTK, NEC): For scenarios where UE is not assumed to perform cell detection on the target SCell, the SCell activation requirements apply provided that SSB offset is same on the target SCell and the active or known serving cell.
    Option 2: TBA
  Issue 1-2-5: Condition of ssb-PositionsInBurst to apply FR2 multiple SCell activation requirement
  Agreement: Multiple SCell activation requirements for FR2 unknown SCells apply provided that the parameter ssb-PositionsInBurst is same for the known serving cell(s) and the target SCell.

## Slide 4: FR2 inter-band CA - core
Issue 2-1-1: scheduling restriction during RLM
  Agreement: For RLM, there is no scheduling restriction if the UE is configured with different numerology between SSB on one FR2 band and data on the other FR2 band provided the UE is configured for IBM operation for the band pair.
  Issue 2-1-2: Removal the description for the case when no measurement restriction is allowed
  Agreement:
    Keep the descriptions on FR2 SSB BFD/CBD/L1-RSRP for the cases with “no measurement restriction” in the spec.

## Slide 5: TCs of inter-frequency measurement requirement without MG
Issue 4-1: Power imbalance condition for inter-frequency measurement requirement without MG
  Agreement: Do not define conditions

## Slide 6: TCs of inter-band CA requirement for FR2 UE measurement capability of independent Rx beam
Issue 6-1: AoA setup in TCs of inter-band CA requirement for FR2 UE measurement capability of independent Rx beam
  Agreement: AoA configuration for both Cell 1 and Cell 2 = Setup 3 (with rough beams) and FFS on the other parameter adjustment (e.g. Noc, Es, Es/Iot and etc) in the test cases (R4-2103628).

## Slide 7: Issue 7-1: removal of TCs for multiple SCell activation due to the testability of simultaneous FR1+FR2 links
Issue 7-1: removal of TCs for multiple SCell activation due to the testability of simultaneous FR1+FR2 links
  Agreement:
    Option 2b (Huawei, Apple, Ericsson, MTK, QC): Keep TC2 but remove the interruption test part for LTE and FR1 PSCell in TC2 and remove TC3 at this stage until the testability of simultaneous FR1+FR2 is clarified.