## Slide 1: WF on URLLC UE performance requirements with higher BLER
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #98-e
E-meeting, 25 January – 5 February 2021
Agenda Item: 7.8.1.2
R4-2103955

## Slide 2: FR1 High reliability (1)
      Background (Agreed parameters from #94e, #94e-Bis, #95e, #96e and #97e)
  SCS/CBW: ​
    FDD: 15 kHz/10 MHz​
    TDD: 30 kHz/40 MHz​
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.​
  PDSCH configuration:
    Mapping type A, symbol length 12, starting symbol 2.​
    Aggregation level: 2 for FDD and TDD
    Max number of HARQ transmissions: 4​
    FDD: No scheduling in slots 0 and 1 (or 19) within 20ms.
    TDD: No scheduling in D slots i, where mod(i, 10) = 0, and S slots
    HARQ process number: 4 for FDD and TDD
    MCS 19
  Antenna configuration: 2x2 and 2x4, ULA low​
  Propagation condition: TDLA30-10​
  Target BLER: 1%​ (BLER is calculated after all transmission​)
  BLER calculation method
    BLER = NpacketFail/NpacketTx, where NpacketFail is the number of packets with CRC fail after all transmissions (initial and retransmissions), NpacketTx is the total number of packets transmitted during the test.
  Target Confidence level: 99%​

## Slide 3: FR1 High reliability (2)
The number of slots between PDSCH and corresponding HARQ-ACK information for FDD
  The number of slots between final repetition PDSCH and corresponding HARQ-ACK information: 2
The number of slots between PDSCH and corresponding HARQ-ACK information for TDD
  6 if mod(i,10) = 2
  5 if mod(i,10) = 4
  3 if mod(i,10) = 6

## Slide 4: FR2 High reliability (1)
Background (Agreed parameters from #97e)
  SCS/BW: 120 kHz / 100 MHz
  TDD pattern: DDSU, S=11:3:0
  PDSCH configuration
    Frequency domain resource allocation: Full bandwidth
    Mapping Type A, Start symbol 1, Length 13
    PDSCH aggregation factor: n2
    Scheduling: No scheduling in D slot i, where mod(i,160) = 0 and mod(i, 160) = 1, and S slots
  DM-RS configuration: Type 1, Single-symbol DM-RS, 1 additional DM-RS
  PT-RS configuration: Frequency density 2, Time density 1, RE offset 2
  Overhead for TBS determination: 6
  HARQ process: 2
  Maximum number of HARQ re-transmission: 4
  Channel model: TDLA30-75
  Antenna configuration: 2x2, ULA low
  Test metric: 1% BLER

## Slide 5: FR2 High reliability (2)
MCS: MCS16 from Table 3

## Slide 6: Pre-emption indication (1)
      Background (Agreed parameters from #94e, 94e-bis, 95e and 96e)
  No URLLC PI performance requirements
  Time frequency set: 14x1
  Number of symbols to be pre-empted: 2
  Starting symbol to be pre-empted: 3
  Pre-emption scheduling: Fixed scheduling
  Test applicability for eMBB UE PI requirements: optional with UE capability signalling
  Antenna Configuration: 2x2 and 2x4, ULA low
  The assumption of UE behaviours for buffer flushing and decoding
    If UE cannot decode the PDCSH correctly, UE feeds back NACK to gNB. Then UE flushes the buffer and waits for the next re-transmission for LLR combing to decode the PDSCH.
  URLLC interference modelling
    SNR: Same as for eMBB transmission
    Structure: Some random data

## Slide 7: Pre-emption indication (2)
      Background (Agreed parameters from #94e, 94e-bis, 95e and 96e)
  Use the following parameters for eMBB PDSCH configuration
Parameter |  | Value
Duplex mode |  | FDD, TDD
Active DL BWP index |  | 1
PDSCH configuration | Mapping type | Type A
 | k0 | 0
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PDSCH aggregation factor | 1
 | PRB bundling type | Static
 | PRB bundling size | 2
 | Resource allocation type | Type 0
 | RBG size | Config2
 | VRB-to-PRB mapping type | Non-interleaved
 | VRB-to-PRB mapping interl bundle size | N/A
PDSCH DMRS configuration | DMRS Type | Type 1
 | Number of additional DMRS | 1
 | Maximum number of OFDM symbols for DL front loaded DMRS | 1
Number of HARQ Processes |  | FDD: 4, TDD: 8
Maximum HARQ transmission |  | 4
The number of slots between PDSCH and corresponding HARQ-ACK information and TDD pattern |  | FDD: 2 TDD: FR1.30-1
CBW/SCS |  | FDD: 10/15, TDD: 40/30
RB allocation |  | Full bandwidth
MIMO layer |  | Rank 1
Propagation condition |  | TDLA30-10

## Slide 8: Pre-emption indication (3)
      Pre-emption probability
  10% within 1 radio frame
      Pre-emption pattern for TDD
  [0 1 0 0 0 0 0 0 0 0, 0 0 1 0 0 0 0 0 0 0, 0 0 0 1 0 0 0 0 0 0, 0 0 0 0 1 0 0 0 0 0]
      eMBB MCS
  MCS 16 in Table 1
      Test metric
  70% of max T-put