## Slide 1: WF on Enabling US 3.45 – 3.55GHz in Band n77
Apple
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic Meeting, April 12th – 20th, 2021
R4-210xxxx

## Slide 2: Background
Band n77 operation in US was first introduced in Rel-16 specifications which is currently restricted to 3700 – 3980 MHz range.
FCC has recently released new rules for 5G operation in 3450 – 3550 MHz range which is also covered by Band n77.
In this meeting, the technical aspects were discussed to address the necessary requirements and specification modifications in order to enable the support of 3450 – 3550 MHz in Band n77 in US [1-5].
This WF captures the outcome of the first-round email discussions which will be based upon for the contributions in next meeting to conclude the support of US 3450 – 3550 MHz in Band n77.

## Slide 3: Tentative Agreements after 1st Round Discussions
No UE SEM modification is needed for adding 3.45 – 3.55 GHz in US Band n77.
No modification to UE coexistence bands is needed for adding 3.45 – 3.55 GHz in US Band n77.
Note 12 in Table 5.2-1 in TS 38.101-1 is modified to cover the support of 3.45 – 3.55GHz range. One of these notes is chosen in next meeting
  “In the USA the Band n77 usage is restricted to outside the Band n48 frequency range.”
  “In the USA this band is restricted to 3450 – 3550 MHz and 3700 – 3980 MHz.”
To include the support of US 3.45 – 3.55GHz range in Band n77 starting from Rel-16, the issue on how the network can distinguish devices supporting the new frequency or not within the same release needs to be resolved.
Changes (in emission limits) are needed in BS specifications to enable US 3.45 – 3.55 GHz in Band n77.

## Slide 4: Way Forward
Companies are encouraged to propose solution(s) on how the network can distinguish devices supporting the new frequency or not within the same release and the corresponding CRs with the necessary specification changes, including the proposed solution.
Companies are encouraged to assess the impact of the network not knowing if the UE will operate in 3.45-3.55 GHz or if it will not operate in 3.45-3.55 GHz.
UE and BS CRs will be treated together as a single package.
Aim to conclude the support of US 3.45 – 3.55GHz range in Band n77 in next RAN4 meeting.

## Slide 5: References
[1] R4-2107109 “Band n77 usage in the US for 3.45 to 3.55 GHz”, Apple
[2] R4-2107349 “Enabling US 3.45 – 3.55 GHz with Band n77”, Qualcomm Incorporated, AT&T
[3] R4-2107350 “Addition of new spectrum in Band n77 for US”, Qualcomm Incorporated, AT&T, Nokia
[4] R4-2104496 “Draft CR to TS 38.104: Additional of FCC emission limits on US 3.45-3.55 GHz band”, Nokia, Nokia Shanghai Bell
[5] R4-2104497 “CR to TS 38.141-1: Additional of FCC emission limits on US 3.45-3.55 GHz band”, Nokia, Nokia Shanghai Bell