## Slide 1: WF on PC2 n34 and n39
Moderator (CMCC)
3GPP TSG-RAN WG4 Meeting # 99-e R4-210xxxxx
Electronic Meeting, May. 19-27, 2021

## Slide 2
Issue 1-1-1: UE MOP and Tx power tolerance for n34/n39 of Power class 2
Proposals
  Option1:
    The MOP and Tolerance for single antenna port are to be specified as 26dBm ±2 dB for band n34/n39 of power class 2
    The MOP and Tolerance for UL MIMO are to be specified as 26dBm +2/-3 dB for band n34/n39 of power class 2
  Option2: The power tolerance for PC2 for n34 is +2/-3dB. Regardless of single antenna port or UL MIMO case.
  Option3: PC2 n34/n39 MOP lower tolerance should be +2/-2 dB.
WF:
  TBA

## Slide 3
Issue 2-1-3: MPR
Proposals
  Option1: No changes to 1Tx PC2 MPR general requirements.
  (The agreement captured in the WF R4-2105386 has been approved in RAN4#98-bis-e meeting)
  Option2: To comply with emission limits, add a new note which allows 2dB power backoff for outer allocations and 1dB for inner allocations in case of RBstart <= 4.32MHz and PC2, DFT-s-OFDM and CBW larger than 5MHz.
WF
  TBA

## Slide 4
Issue 2-1-2: A-MPR
Option1: No changes to PC2 A-MPR requirements for n39.
Option2: Re-use NS_50 PC3 A-MPR regions for PC2 A-MPR. For 40 MHz CIM3 A-MPR use values defined in A1 column of the PC3 A-MPR.
WF:TBA
Channel Bandwidth (MHz) | RBstart*12*SCS (MHz) | LCRB*12*SCS (MHz) | A-MPR, PC3 | A-MPR, PC2
25 MHz | ≤ LCRB*12*SCS - 5 | > 5 | A7 | A7
 | ≤ 20 | ≤ 1.44 | A8 | 
30 MHz | ≤ LCRB*12*SCS - 5 | > 5 | A7 | A7
 | ≤ 25 | ≤ 1.44 | A8 | A8
 |  | ≤ 3.6 | A9 | 
40 MHz | ≤ 4.32 | > 0 | A1 | A1
 | > 4.32, ≤ 10.44 | ≤ 10.8 | A3 | A3
 | > 4.32, ≤ 18 | > 10.8 | A2 | A2
 | > 18, ≤ 31.68 | > max (31.68 – RBstart*12*SCS, 0) | A6 | A6
 | > 31.68 | > 0 | A5 | A1
NOTE 1: The A-MPR values are specified in Table 6.2.3.19-2. |  |  |  | 
Table 1. A-MPR regions for NS_50, together with A-MPR for PC3 and PC2 (PC2 highlighted in yellow)
Modulation/Waveform |  | A1 (dB) | A2 (dB) | A3 (dB) | A5 (dB) | A6 (dB) | A7 (dB) | A8 (dB)
 |  | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner
DFT-s-OFDM | Pi/2 BPSK | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2 | ≤ 4 | ≤ 2
 | QPSK | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2 | ≤ 5 | ≤ 2
 | 16 QAM | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2 | ≤ 5 | ≤ 2.5
 | 64 QAM | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 |  | ≤ 5 | 
 | 256 QAM | ≤ 11 | ≤ 7 |  | ≤ 5 |  | ≤ 5 | 
CP-OFDM | QPSK | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 | ≤ 3.5 | ≤ 6.5 | 
 | 16 QAM | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 | ≤ 3.5 | ≤ 6.5 | 
 | 64 QAM | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 |  | ≤ 6.5 | 
 | 256 QAM | ≤ 12 | ≤ 8 |  |  |  | ≤ 6.5 | 
Table 2. A-MPR values for NS_50
Channel Bandwidth (MHz) | RBstart*12*SCS (MHz) | LCRB*12*SCS (MHz) | A-MPR
25 MHz | ≤ LCRB*12*SCS - 5 | > 5 | A7
 | ≤ 20 | ≤ 1.44 | A8
 | ≤ max(0, 6.48 - LCRB *12*SCS) | > 1.44, ≤ 5.0 | A6
30 MHz | ≤ LCRB*12*SCS - 5 | > 5 | A7
 | ≤ 25 | ≤ 1.44 | A8
 |  | ≤ 3.6 | A9
 | > LCRB *12*SCS – 5, ≤ 5.04 | > 3.6 | A6
40 MHz | ≤ 4.32 | > 0 | A1
 | > 4.32, ≤ 10.44 12.96 | ≤ 10.8 | A3
 | > 4.32, ≤ 18 | > 10.8 | A2
 | > 18, ≤ 31.68 | > max (31.68 – RBstart*12*SCS, 0) | A6
 | > 31.68 | > 0 | A5
NOTE 1: The A-MPR values are specified in Table 6.2.3.19-2. |  |  | 
Option3: Use allocations regions found in Table 1 and A-MPR proposed in Table 2 for 25MHz, 30MHz and 40MHz CBW NS_50. T Table1 PC2 A-MPR regions for NS_50 Table 2: PC2 A-MPR for NS_50
Modulation/Waveform |  | A1 (dB) | A2 (dB) | A3 (dB) | A5 (dB) | A6 (dB) | A7 (dB) | A8 (dB)
 |  | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner
DFT-s-OFDM | Pi/2 BPSK | ≤ 11 11.5 | ≤ 7 8.0 | ≤ 3 4.0 | ≤ 5 7.5 | ≤ 2 2.5 | ≤ 4 5 | ≤ 2 2.5
 | QPSK | ≤ 11 11.5 | ≤ 7 8.0 | ≤ 3 4.0 | ≤ 5 7.5 | ≤ 2 2.5 | ≤ 5 6 | ≤ 2 2.5
 | 16 QAM | ≤ 11 11.5 | ≤ 7 8.0 | ≤ 3 4.0 | ≤ 5 7.5 | ≤ 2 2.5 | ≤ 5 6 | ≤ 2.5 3.0
 | 64 QAM | ≤ 11 11.5 | ≤ 7 8.0 | ≤ 3 4.0 | ≤ 5 7.5 |  | ≤ 5 6 | 
 | 256 QAM | ≤ 11 11.5 | ≤ 7 8.0 |  | ≤ 5 7.5 |  | ≤ 5 6 | 
CP-OFDM | QPSK | ≤ 12 12.5 | ≤ 8 9.0 | ≤ 4.5 5.5 | ≤ 5 7.5 | ≤ 3.5 4.5 | ≤ 6.5 7.5 | 
 | 16 QAM | ≤ 12 12.5 | ≤ 8 9.0 | ≤ 4.5 5.5 | ≤ 5 7.5 | ≤ 3.5 4.5 | ≤ 6.5 7.5 | 
 | 64 QAM | ≤ 12 12.5 | ≤ 8 9.0 | ≤ 4.5 5.5 | ≤ 5 7.5 |  | ≤ 6.5 7.5 | 
 | 256 QAM | ≤ 12 12.5 | ≤ 8 9.0 |  | ≤ 5 7.5 |  | ≤ 6.5 7.5 |