## Slide 1: WF on FR2 interband UL CA
RAN4#99-e R4-21xxxxx
e-Meeting, May. 19-27, 2021
Samsung

## Slide 2: Max EIRP for IBM between different frequency group
Options
  Option 1: per UE (refer to R4-2109656)
  Option 2: per band with max EIRP limit of each band set to 43 dBm (PC3/PC4) and 55 dBm (PC1).
Agreement:
  Option 2: per band with max EIRP limit of each band set to 43 dBm (PC3/PC4) and 55 dBm (PC1).

## Slide 3: Min peak EIRP for CA_n257A_n259A based on IBM
Specify minimum peak EIRP requirements per band with relaxed requirement compared to single-CC, i.e., n257=22.4-X dBm, n259=18.7-Y dBm
  Options for values of X and Y, i.e. ΔTIB,P,n
    Option 1: X and Y shall depend on the activation status of the participating CA bands
    Option 2: ΔTIB,P,n shall be ΔRIB,P,n -1 dB
    Option 3: Consider “total UE power concept + relaxation due to inter-band CA operation (include MBR etc.)”
    Option 4: other
      4.1 X=Y=2.5dB
      4.2 equal to or less than 3dB + MBR
      4.3 take power consumption and thermal issues into consideration
  Agreement for values of X and Y, i.e. ΔTIB,P,n
    TBD

## Slide 4: Spherical coverage for CA_n257A_n259A based on IBM
Specify EIRP spherical coverage requirements per band with relaxed requirement compared to single-CC.
  At least following terms shall be quantified to obtain the individual n257 and n259 EIRP relaxations:
    MBR
    Degradation for multi-band to PA-PA interaction
    EIRP Common coverage relaxation
  Further study other relaxation terms:
    Power consumption consideration Total UE power concept

## Slide 5: Reference
R4-2107663 Email discussion summary for [99-e][137] NR_RF_FR2_req_enh2_Part_1, Moderator (Nokia)