## Slide 1: WF on UE PC2 SAR solutions and UE maximum power
China Telecom
R4-21xxxxx
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May. 19-27, 2021
Agenda: 8.35.1

## Slide 2: Background
The contributions submitted in RAN4 #99e meeting for SAR solutions and UE maximum power:
  R4-2108805, On UL Duty Cycle method for NR uplink inter band CA, Nokia, Nokia Shanghai Bell
  R4-2108806, On increasing UE maximum power high limit for NR uplink inter band CA, Nokia, Nokia Shanghai Bell
  R4-2109173, Discussion on increasing maximum output power for UE PC2 CA, Mediatek India Technology Pvt.
  R4-2109676, Discussion on SAR ratio in duty cycle solution, vivo
  R4-2109975, More on methods for faciliating SAR compliance for inter-band UL CA, Ericsson
  R4-2109976, Higher BC power class for UL CA, Ericsson
  R4-2110049, Further discussion on SAR schemes for UE power class 2 NR inter-band CA with 2UL, China Telecom
  R4-2110050, Further discussion on SAR schemes for UE power class 2 NR SUL configurations, China Telecom
  R4-2110192, Discussion on SAR issue for HP UE inter-band UL CA, Xiaomi
  R4-2110438, Further discussion on SAR solution for NR PC2 inter-band CA, ZTE Corporation
  R4-2110830, R17 Inter band CA HPUE SAR, OPPO
  R4-2110831, R17 power class report for NR in CA, OPPO
  R4-2111298, Discussion on New Power Limits for Inter-band CA or DC, Huawei,HiSilicon
  R4-2111501, Power class consideration for NR inter-band UL CA, Apple

## Slide 3: WF on SAR solutions
Duty Cycle based solutions
  Report the total duty cycle capability per band combination with SARratio factor consideration and not need to report SARratio
    Dutycycle threshold calculation procedure, which is to be specified in the spec.
      Option1: DutyNR, x *( PNR,x/ P26)*SARratioNR, x + DutyNR, y *(PNR, y/ P26)* SARratioNR, y ≤ Duty threshold
      where, SARratioNR, x = 50%/DutycycleNR, x ; SARratioNR, y = 50%/DutycycleNR, y
      Option2: DutyNR, x *( PNR,x/ P26) + DutyNR, y *(PNR, y/ P26) *SARratioNR ≤ Duty threshold
      Where, SARratioNR = DutycycleNR, x /DutycycleNR, y
      Agreement: Option 1
    Dutycycle capability reporting
      Option 1: Report only one total dutycycle capability independent of power class cases
      Option 2: Report total dutycycle capabilities based on power class cases
      Agreement: Option 1
“Blind scheme” solution can be discussed further

## Slide 4: WF on UE maximum power
How to increase UE maximum power high limit
  Option 1: Remove PPowerClass constraint from PCMAX_H
  Option 2: Replace PPowerClass with sum or modified sum in both PCMAX_H and PCMAX_L
  Option 2a: Define a new power class where the requirements are based on per-band power capability (no need to further define separate MSD requirements)
  Option 3: Define a new power class per band-combination
  Option 4: Consider power boosting approach
  Agreement: Down-select to Option 2 and Option 3

## Slide 5: WF on UE maximum power
WI scope for increasing UE maximum power high limit
  Option 1: Focus on increasing UE maximum power high limit for NR uplink inter band CA under this WI and revise the WID to accommodate this topic in the objective accordingly.
  Option 2: Discuss the topic in a dedicated SI in Rel-18.
  Agreement: