## Slide 1: WF on NR-U maintenance-related topics
Qualcomm Incorporated
R4-210xxxx
3GPP TSG-RAN WG4 #99-e
May 19th ‒ 27th, 2021
Electronic Meeting

## Slide 2: Intra-cell guardband for wideband operation
Agreement
  For DL
    UE requirements apply when zero-width guard bands are configured and all RB sets within the channel are scheduled and available for DL transmission at the gNB
  For UL
    RAN4 only defines UE RF requirements in Rel-16 for contiguous RB-sets in the UL
    Requirements apply with UL data scheduled over contiguous RB-sets with no guard bands between them, i.e. RBs between RB-sets are also scheduled for transmission
    Requirements apply with guard bands at the edges of the scheduled RB-sets
    FFS: Whether guard bands at the edges of the scheduled RB-sets can be referred to as intra-cell guard bands
    FFS: Whether intra-cell guard bands are assumed to be zero or non-zero.

## Slide 3: Other agreements
NOTE 14: This band is applicable in the USA only subject to FCC Report and Order FCC 20-51
  This note shall be modified to be more general since Band n96 is becoming available in other countries.
The NR-U Rx requirements for maximum input level and spurious emissions shall be added to the specifications.