## Slide 1: WF on transient position and related requirements in Rel-16
Agenda item: 6.2.1
Source: LG Electronics
3GPP TSG-RAN WG4 Meeting #99-e R4-2107746
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
In RAN4 #97-e meeting, RAN4 already agreed as follow in R4-2016806
  Due to large switching period defined in RRM spec, no need to consider the RF test for switching time requirement if defined
  Specific switching time 150us is captured in TR only
In RAN4#99-e meeting, RAN4 discussed the transient position for TDM operation between LTE V2X and NR V2X in ITS spectrum.
  In 1st Round, RAN4 agreed the principle as follow
    Agreement
    Based on RAN1 reply LS, RAN4 can agree that the switching position will be decided by comparison each LTE SL and NR SL packet priority when the priority is not same in ITS spectrum.
    When they have same priority between LTE SL and NR SL, it is up to UE implementation. But, it is still open issue how to apply the switching position.
RAN4 still discuss whether or not specify the On/Off time mask with switching time in TS38.101-3.

## Slide 3: WF: On/Off time mask in TS38.101-3
In 2nd round e-mail discussion, moderator proposed two options as follow
Issue 1-1-3: RAN4 specification perspective, is it beneficial to specify the On/Off time mask in TS38.101-3 for TDM operation in ITS spectrum?
  Option 1: In case of the priorities of LTE SL and NR SL are the same, this is up to UE implementation for the switching position. So, it is not needed to specify RF requirements. The RRM requirements in clause 12.9.1 in TS38.133 can be considered.
  Option 2: RAN4 specify the On/Off time mask in TS38.101-3.
WF: Option 1. The additional RF requirements is not needed.

## Slide 4: Reference
R4-2107634, “RAN4#99-e_summary_108_5G V2X maintenance,” Moderator (LG Electronics)
R4-2109044, “Discussion on time mask for NR V2X and LTE V2X switching in ITS band,” CATT
R4-2109688, “Discussion on the switching period position between LTE SL and NR SL,” vivo
R4-2109919, “Switching position for TDM operation between LTE V2X and NR V2X in ITS spectrum ,” LGE
R4-2110027, “on switching period,” Xiaomi
R4-2111437, “On SL switching period,” Huawei
R4-2109045, “CR for TS 38.101-3, Time mask for NR V2X and LTE V2X switching in ITS band,” CATT