## Slide 1: WF on operating scenarios for Uu and SL operating in the same licensed band
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, 19th - 27th May, 2021
Agenda item: 9.14.5
Document for: Approval
R4-21xxxxx
CATT, …

## Slide 2: Background
  The following issues are discussed for operating scenarios for Uu and SL operating in the same licensed band:
  Issue 1-1-1: Duplex mode
  Issue 1-2-1: Intra-band con-current V2X operation with adjacent carrier for TDD band
  Issue 1-2-2: Intra-band con-current V2X operation with adjacent carrier for FDD band
  Issue 1-2-3: Frequency separation for non-adjacent carriers
  Issue 1-3-1: Intra-band V2X operation with same carrier
  Issue 1-3-2: Switching period length
  Issue 1-3-3: Switching period position
  Issue 1-3-4: Scheduling restriction for switching
  Issue 1-3-5: Time mask for TDM with same carrier
  Issue 1-3-6: Time mask for TDM with different carriers

## Slide 3: Issue 1-1-1: Duplex mode
  Agreements:
  Do not use duplex mode to describe intra-band con-current V2X operation. Use “con-current SL transmission and Uu transmission operation” and “con-current reception of SL and Uu transmission operation” terminology to separate the discussion of FDM operation between Uu and SL operating in a licensed band.

## Slide 4: Issue 1-2-1: Intra-band con-current V2X operation with adjacent carrier for TDD band
  Agreements:
  Simultaneous NR UL Transmission and NR SL reception with adjacent carrier in TDD band are not allowed, and then RAN4 allow intra-band con-current SL operation with adjacent carrier for FDM operation in TDD band without in-device coexistence study.

## Slide 5: Issue 1-2-2: Intra-band con-current V2X operation with adjacent carrier for FDD band
  Agreements:
  Focus on intra-band con-current V2X operation with adjacent carrier for TDD band and deprioritize FDD band. FDD band can be studied once operator has request.

## Slide 6: Issue 1-2-3: Frequency separation for non-adjacent carriers
  Candidate options:
  Option 1: RAN4 discuss whether to introduce the concurrent reception of SL and Uu transmission operation in the licensed band.
  Option 2: No need to introduce the frequency separation for the case Uu and SL are in different channels for intra-band con-current operation.
  Recommended WF
  Further discuss whether to introduce con-current SL reception and Uu transmission operation with non-adjacent carrier.

## Slide 7: Issue 1-3-1: Intra-band V2X operation with same carrier
  Candidate options:
  Option 1: Prioritize the scenario for Uu and SL in the same carrier for intra-band V2X operation (TDM).
  Option 2: Prioritize the scenario for Uu and SL in the different carrier for intra-band V2X operation (TDM).
  Option 3: Prioritize the scenario for Uu and SL in both the same carrier and different carrier for intra-band V2X operation (TDM).
  Recommended WF
  Further discuss whether to decide prioritization on TDM with same carrier and different carrier or to consider both as 1st priority.

## Slide 8: 1-3-3: Switching period position
  Agreements:
  The priority rule, i.e. the switching period is located on the RAT that has a lower priority, is considered as a starting point.

## Slide 9: Issue 1-3-4: Scheduling restriction for switching
  Agreements:
  Leave scheduling restriction for switching to RRM session.

## Slide 10: Reference
[1] R4-2107669, Email discussion summary for [99-e][143] NRSL_enh_Part_2, Moderator (CATT), RAN4#99-e