## Slide 1: WF on MPR requirements for intra-band con-current V2X operation
Agenda item: 9.14.5
Source: LG Electronics
3GPP TSG-RAN WG4 Meeting #99-e R4-210xxxx
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
During RAN4#98bis-e & RAN4 #99-e meeting, only one company provided simulation results for MPR requirements for simultaneous NR Uu transmission and NR SL transmission in licensed NR band.
In 1st round discussion, RAN4 discussed the sub-topic 3-2 for MPR requirements for intra-band V2X con-current operation as follow.
  Sub-topic 3-2: MPR for intra-band V2X con-current operation
    Issue 3-2-1: Modulation order and RB allocation
    Issue 3-2-2: Ratio of total RB allocation over 1MHz
    Issue 3-2-3: MPR for 26dBm
    Issue 3-2-4: MPR for 23dBm
RAN4 still discuss how to define the MPR requirements for simultaneous NR Uu transmission and NR SL transmission in licensed NR band.

## Slide 3: WF: MPR requirements for intra-band con-current V2X operation
Issue 3-2-1: Modulation order and RB allocation
  Proposals
    Option 1: Define MPR for NR V2X intra-band con-current operation of SL PC5 and Uu taking configured Modulation Order and RB allocations into account.
WF: Option 1 is baseline to define MPR requirements. The MPR requirements can be updated, if other companies provide the MPR results in next RAN4 meeting.

## Slide 4: WF: MPR requirements for intra-band con-current V2X operation
Issue 3-2-3: MPR for PC2 UE
  Proposals
    Option 1: Specify MPR in Table 1 and 2 for NR V2X intra-band con-current operation for maximum total output power of 26dBm.
WF:
  Specify MPR requirements with Table 1 and Table 2 for PC2 intra-band con-current V2X UE
  The detail Non-contiguous Outer1 RB allocation and Outer2 RB allocation will be captured in TR.
Table 1. Contiguous RB allocation for Power Class 2
Table 2. Non-contiguous RB allocation for Power Class 2
Modulation |  | MPR for bandwidth class B(dB) | 
 |  | inner | Outer
CP-OFDM | QPSK | ≤ [1.5] | ≤ [3.5]
 | 16QAM | ≤ [2.0] | ≤ [3.5]
 | 64QAM | ≤ [3.0] | ≤ [3.5]
 | 256QAM | ≤ [5.0] | ≤ [5.0]
Modulation |  | MPR for bandwidth class B(dB) |  | 
 |  | inner | Outer1 | Outer2
CP-OFDM | QPSK | ≤ [2.0] | ≤ [4.0] | ≤ [6.0]
 | 16QAM | ≤ [2.5] | ≤ [4.0] | ≤ [6.0]
 | 64QAM | ≤ [3.5] | ≤ [4.5] | ≤ [6.0]
 | 256QAM | ≤ [4.5] | ≤ [5.0] | ≤ [6.0]

## Slide 5: WF: MPR requirements for intra-band con-current V2X operation
Issue 3-2-4: MPR for PC3 UE
  Proposals
    Option 1: Specify MPR in Table 3 and Table 4 for NR V2X intra-band con-current operation for maximum total output power of 23dBm.
WF:
  Specify MPR requirements with Table 3 and Table 4 for PC3 intra-band con-current V2X UE
  The detail Non-contiguous Outer1 RB allocation and Outer2 RB allocation will be captured in TR.
Modulation |  | MPR for bandwidth class B(dB) | 
 |  | inner | Outer
CP-OFDM | QPSK | ≤ [1.0] | ≤ [1.0]
 | 16QAM | ≤ [1.0] | ≤ [1.0]
 | 64QAM | ≤ [1.0] | ≤ [1.0]
 | 256QAM | ≤ [1.5] | ≤ [1.5]
Table 3. Contiguous RB allocation for Power Class 3
Modulation |  | MPR for bandwidth class B(dB) |  | 
 |  | inner | Outer1 | Outer2
CP-OFDM | QPSK | ≤ [1.0] | ≤ [1.5] | ≤ [3.0]
 | 16QAM | ≤ [1.0] | ≤ [1.5] | ≤ [3.0]
 | 64QAM | ≤ [1.0] | ≤ [1.5] | ≤ [3.0]
 | 256QAM | ≤ [1.5] | ≤ [2.0] | ≤ [3.0]
Table 4. Non-contiguous RB allocation for Power Class 3

## Slide 6: Reference
[1] R4-2107669, “RAN4#99-e_summary_143_NRSL_enh_Part2,” Moderator (CATT)
[2] R4-2109947, “RF requirements for partial used licensed band bewteen NR Uu and NR SL operation,” LGE
[3] R4-2109702, “MPR for NR V2X intra-band con-current operation with Uu,” LGE
[4] R4-2109950, “TP on RF requirements for intra-band con-current V2X operation in licensed band,” LGE