## Slide 1: WF on synchronization synchronous operation for Uu and SL operating in the same licensed band
Huawei, HiSilicon, [ ]
R4-21xxxxx
3GPP TSG-RAN WG4 #99-e
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
The following issues related to synchronous operation between Uu and SL in the licensed band have been discussed in RAN4#99-e meeting
  Issue 2-1-2: SL transmission timing
  Issue 2-3-1: LS on SL timing and sync reference source

## Slide 3: WF
2-1-2: SL transmission timing
Options
  Option 1: SL transmission timing to be aligned with UL timing of Uu.
  Option 2: For sidelink transmissions,
    SL transmission timing is aligned with Uplink timing when Uu and sidelink is TDMed coexistence in the same band, including TDM coexistence within the same carrier or different carriers. (NTA= 0)
    Otherwise, SL transmission timing is aligned with Downlink timing.
  Option 2a: For sidelink transmissions,
    SL transmission timing is aligned with Uplink timing when Uu and sidelink is TDMed/FDMed coexistence in the same band, including TDM coexistence within the same carrier or different carriers.
    Otherwise, SL transmission timing is aligned with Downlink timing.
  Option 3: Only allow Uu UL transmission prior to SL reception and transmission, i.e. configure SL Rx/Tx slots to be located in the back of Uu UL Tx slots.
  Option 4: Follow existing SL transmission timing aligned with DL timing of Uu.
WF
  Option 2/2a (Huawei, CATT, Ericsson, vivo)
  Option 4 : Any changes to SL timing is up to RAN1 (Qualcomm, LGE)

## Slide 4: WF
Issue 2-3-1: LS on SL timing
Options
  Option 1: Send LS to RAN1 if RAN4 have any agreement/divergence on timing and sync reference source of SL.
  Option 2: No need to send LS to RAN1. (Qualcomm, LGE)
  Option 3: Send LS to RAN1 asking the feasibility of the timing considering the RAN4 consensus. (Ericsson, CATT, Huawei, vivo)
Recommended WF
  According to the agreed WF in last meeting, send LS to RAN1 to check whether SL transmission timing option 2/2a are feasible from RAN1 perspective as there are divergent views in RAN4.

## Slide 5
Reference
[1] R4-21xxxxx, Email discussion summary for [99-e][143] NRSL_enh_Part_2, CATT