## Slide 1: WF on [145] NR_ext_to_71GHz Part1
Intel Corporation (Moderator)
3GPP TSG-RAN WG4#99-e Meeting R4-21xxxxx
Electronic Meeting, May 19 – 27, 2021

## Slide 2: FR definition in 60 GHz (1)
Issue: Plenary tasked each WG to discuss and recommend how to introduce FR definition in 60 GHz.
Options:
  Option 1: Introduce FR2-1 (24.25 – 52.6 GHz) and FR2-2 (52.6 – 71 GHz) (Apple, Intel, Huawei, Charter, LG)
    Within option 1, indicate on the preferred approach:
      “FR2-1 and FR2-2” (Apple, Intel), or
      “FR2.1 and FR2.2” (Huawei)
  Option 2: Introduce FR2-2 (52.6 – 71 GHz) in addition to FR2 (24.25 – 52.6 GHz) (Intel, ZTE, MediaTek, Qualcomm)
  Option 4: Ericsson, Charter, CMCC, Samsung, AT&T
    All UE RF/demod requirements defined as function of band, BW, PC or band combo within FR2;
    BS requirements can be updated to cater for an extension of FR2 to include 52.6 – 71 GHz;
    All RRM requirements for higher SCS applicable for 52.6 – 71 GHz can be defined as function of SCS within FR2;
  Option 5: Nokia, R&S, MediaTek
    Keep FR2 definition as it is
    Introduce FR2x (52.6 – 71 GHz) and FR2-comb (24.25 – 71 GHz)
Agreement: TBD

## Slide 3: FR definition in 60 GHz (2)
Issue: Compromised suggestion to describe the RAN4 status to RAN
Wording suggestion by Nokia
  RAN4 agrees FR3 is not defined and for BS operating in 52.6 – 71 GHz current terminology like BS type 2-O can be re-used
  RAN4 agrees separate FR2-based names are needed for 24.25 – 52.6 GHz and 52.6 – 71 GHz
  Multiple companies prefer to keep current FR2 definition and name as it is for 24.25 – 52.6 GHz
  Multiple companies prefer having an additional single label to address the full range of 24.25 – 71 GHz
  Multiple companies consider that RAN4 has means to define requirements as a function of bands, bandwidths, band combinations and SCS
Agreement: TBD

## Slide 4: Max CBW for 960 kHz (Issue 3.2.1-1)
Issue: Max CBW for 960 kHz SCS
Options:
  Option 1: 2000 MHz for both licensed and unlicensed bands (CATT, Apple, Qualcomm, CMCC, vivo, Samsung, Intel, ZTE, MTK, Xiaomi, Huawei)
  Option 2: 2160 MHz and 2000 MHz for both licensed and unlicensed (Qualcomm, Xiaomi, Nokia, Charter)
  Option 3: 2160 MHz for unlicensed and 2000 MHz for licensed (Apple, LGE, Charter, Sony)
  Option 4: Make a decision for unlicensed operation and FFS for licensed operation (Qualcomm)
  Option 5: 2160 MHz for both licensed and unlicensed bands (Ericsson, Sony)
Agreement: TBD

## Slide 5: Optionality of UE support of Max. CBW
It is proposed that UE support of the following max. CBW for each SCS is optional, in addition to the agreement that UE support of 480/960kHz SCS is optional:
  120kHz: 400MHz
  480kHz: 1600MHz
  960kHz: 2000MHz and/or 2160MHz
Options:
  Option 1: Yes
  Option 2: No
  Option 3: FFS
Agreement: TBD

## Slide 6: Channelization (Issue 3.2.2)
Issue: Channelization on 52.6 – 71 GHz whether it should be harmonized or separated between license and unlicensed bands.
Options:
  Option 1: Harmonize channelization between licensed and unlicensed bands (Nokia):
    Option 1A: Align with IEEE with fixed channelization (Qualcomm, Charter)
    Option 1B: Do not align with IEEE with fixed channelization (vivo, MTK)
    Option 1C: Do not align with IEEE and floating channelization (Ericsson, ZTE, Huawei)
    Option 1D: CATT, CMCC
      Option 1D-1: Do not align with IEEE with fixed channelization for licensed and no LBT unlicensed bands.
      Option 1D-2: Align with IEEE with fixed channelization for LBT unlicensed bands. Try to harmonize option 1D-2 with option 1D-1 as much as possible.
  Option 2: Separate channelization (Apple, Xiaomi)
    For licensed:
      Option 2A: NR based floating raster (No 802.11ad/ay alignment) (Apple, Xiaomi)
    For unlicensed:
      Option 2B: Align with 802.11ad/ay and no NR channel overlaps with two IEEE channels (Apple, Xiaomi)
Agreement: TBD

## Slide 7: SU for max CBW (Issue 3.2.3-1)
Issue: RAN1 asked SU for max channel bandwidth. While RAN4 needs more time to discuss, RAN1 needs input from RAN4.
Moderator suggestion:
  Option 1:
    For 120 kHz SCS: Keep the same max SU from FR2, i.e., 95 %
    For 480/960 kHz SCS: Provide the SU in range, i.e., [85 – 95] %
  Option 2:
    For 120/480/960 kHz SCS: Provide the SU in range, i.e., [85 – 95] %
Agreement: TBD

## Slide 8: Intra-band contiguous CA within 2/2.16 GHz
Issue: Whether CA is supported for intra-band contiguous within 2/2.16 GHz
Options:
  Option 1: N x 400 MHz, n = [2, 3, 4, 5] (Charter, MTK, CATT, CMCC, Nokia)
    Option 1-A: M x 100 MHz for 120 kHz SCS, M = TBD (Nokia)
  Others:
    Normal CA operation (Ericsson)
    100/200/400 MHz CC based CA (Huawei, Qualcomm)
Agreement: TBD

## Slide 9: CA equal to or larger than 2/2.16 GHz (Issue 3.2.4-2)
Issue: Whether CA is supported for larger than 2/2.16 GHz
Options:
  Option 1: Support CA ≥ 2/2.16 GHz (CMCC, vivo, Nokia, Huawei, Sony)
  Others:
    Normal CA operation (No sub-channelization) (Ericsson)
    No such wide CA capability for handheld UE; Need further discussion for CPE (Qualcomm)
Agreement: TBD

## Slide 10: Band number (Issue 2.2.1)
Issue: Whether 52.6 – 71 GHz range is to reuse FR2 range, i.e., 257 – 512, or a new range, i.e., 513 – 1024.
Agreement: Reuse the reserved band numbers in FR2 for 60 GHz band

## Slide 11: Regulatory for Unlicensed band (Issue 2.2.2-1)
Issue: Which regulatory requirements will be considered for unlicensed regulation requirements.
Agreement: Consider EN 302 567, EN 303 753, and TR 38.805 (FCC 47 CFR 15.255) for mobile application in unlicensed band.

## Slide 12: ITS band for unlicensed band (Issue 2.2.2-2)
Issue: Whether ITS band for unlicensed band
Agreement: No need to exclude ITS band for unlicensed band

## Slide 13: Intermediate CBWs between Max and Min CBWs (Issue 3.2.1-2)
Issue: Intermediate CBWs between max and min CBWs for each SCS
Agreement: Introduce integer multiples of the minimum CBW for each SCS:
  120 kHz SCS (Min. 100 MHz/Max. 400 MHz): 200 MHz
  480 kHz SCS (Min. 400 MHz/Max. 1600 MHz): 800, 1200 MHz
  960 kHz SCS (Min. 400 MHz/Max. TBD MHz): 800, 1200, 1600 MHz

## Slide 14: Operation Scenario in 60 GHz NR
Issue: Latest approved WID states that NR/NR-U operation in 52.6 – 71 GHz can be in standalone, aggregated via CA or DC with an anchor carrier. Given the unlicensed band in 60 GHz is newly defined, it is necessary to define and finish a single band requirement first.
Agreement: RAN4 aims to finish a single band requirement first

## Slide 15: OTA aspect in 60 GHz
Issue: Whether RAN4 needs to recommend RAN Plenary the need and urgency of studying the UE OTA test method for 52.6 – 71 GHz.
Agreement: Agree to recommend RAN Plenary the need and urgency of studying the UE OTA test method for 52.6 – 71 GHz

## Slide 16: References
R4-2107671, “Summary for [99-e][145] NR_ext_to_71GHz_Part_1,” Intel (moderator), RAN4 #99-e, May 2021