## Slide 1: WF on [145] NR_ext_to_71GHz Part1
Intel Corporation (Moderator)
3GPP TSG-RAN WG4#99-e Meeting R4-2107876
Electronic Meeting, May 19 – 27, 2021

## Slide 2: FR definition in 60 GHz (1)
Issue: Plenary tasked each WG to discuss and recommend how to introduce FR definition in 60 GHz.
Options:
  Option 1: Introduce FR2-1 (24.25 – 52.6 GHz) and FR2-2 (52.6 – 71 GHz) (Apple, Intel, Huawei, Charter, LG)
    Use the unique term FR2 to cover FR2-1 and FR2-2
    Within option 1, indicate on the preferred approach:
      “FR2-1 and FR2-2” (Apple, Intel), or
      “FR2.1 and FR2.2” (Huawei)
  Option 2: Introduce FR2-2 (52.6 – 71 GHz) in addition to FR2 (24.25 – 52.6 GHz) (Intel, ZTE, MediaTek, Qualcomm)
  Option 4: Ericsson, Charter, CMCC, Samsung, AT&T
    All UE RF/demod requirements defined as function of band, BW, PC or band combo within FR2;
    BS requirements can be updated to cater for an extension of FR2 to include 52.6 – 71 GHz;
    All RRM requirements for higher SCS applicable for 52.6 – 71 GHz can be defined as function of SCS within FR2;
  Option 5: Nokia, R&S, MediaTek
    Keep FR2 definition as it is
    Introduce FR2x (52.6 – 71 GHz) and FR2-comb (24.25 – 71 GHz)
Agreement: RAN4 should further discuss the issue based on concepts of Option 1, Option 2/5 and Option 4.
Notes: Ericsson: Keep option 4. Keep option 1 which may introduce the sub-range.
Charter： One option is to extend FR2 and the other is keep FR2 as it is and define the

## Slide 3: FR definition in 60 GHz (2)
Issue: Compromised suggestion by Nokia to describe the RAN4 status to RAN
Wording suggestion
  RAN4 agrees FR3 is not defined and for BS operating in 52.6 – 71 GHz current terminology like BS type 2-O can be re-used
  RAN4 agrees separate FR2-based names are needed for 24.25 – 52.6 GHz and 52.6 – 71 GHz
  Multiple companies prefer to keep current FR2 definition and name as it is for 24.25 – 52.6 GHz
  Multiple companies prefer having an additional single label to address the full range of 24.25 – 71 GHz
  Multiple companies consider that RAN4 has means to define requirements as a function of bands, bandwidths, band combinations and SCS
Agreement:
  RAN4 agrees FR3 is not be introduced in any RAN4 specifications for the frequency range 52.6 – 71 GHz.“
Notes: Huawei: We need discuss the details for those bullets. There are aspects which contradict with each other, especially for the last three. We need some detailed discussion.
Ericsson:
Charter: one important aspect to extend FR2 to 71GHz, there are additional NR-U bands in FR2. That would be benefit from extending FR2 to 71Ghz. We have favor to extend FR2.
AT&T: support keeping FR2 definition to apply the entire range. Minimize the spec effort. 38.101-2 and corresponding BS spec we can reuse them. We should keep FR2 for the full range.
Apple: perhaps we agree on second bullets. We need differentiate two frequency and we should include pros and cons from each option.
Nokia: We need discussion on exact label of FR2 should be used.
Ericsson: support AT&T comment. For second bullet, there are various aspects. Huawei suggested to extend the current range and on top of it introduce the sub-range. We do not really see the need to introduce the sub-band.
Huawei: to Nokia on the sub-bullet #2, this is general covering both Option 1~5. We do not excluding using the existing FR2. To Ericsson, we can already see there is strong preference from companies to have some … sub-band will not trigger the discussion of requirements. To apple, I am fine to extend LS to capture pros and cons for options to considered.
AT&T: second bullet causes confusion. We would like to highlight FR2 as it exists. The whole should be kept as FR2.
Apple: it is not good to leave all the work to RAN. We should make better decisions in RAN4 first and then provide options to RAN. We should provide some analysis that RAN4 did to RAN. We can leave options on the table with pros and cons.
Charter: we agree AT&T
Mediatek: we have concern on extending FR2 to beyond 52.6GHz. Whether the same requirement will be applied.
Apple: we provide the solution to differentiate the existing FR2 and new FR2 based band.
Nokia: support Apple. Some differentiation of signaling.
Ericsson: we agree that some requirements may be different. Signaling is RAN2 issue.
Huawei: RAN2 side does not really care and handle. On requirements, we have FR2 requirements which depend on frequency range. We support Apple comment and need send feedback to RAN. We would like to reduce the option numbers.
Samsung: prefer to keep bullet #1 only.

## Slide 4: Max CBW for 960 kHz (Issue 3.2.1-1)
Issue: Max CBW for 960 kHz SCS
Options:
  Option 1: 2000 MHz for both licensed and unlicensed bands (CATT, Apple, Qualcomm, CMCC, vivo, Samsung, Intel, ZTE, MTK, Xiaomi, Huawei)
  Option 2: 2160 MHz and 2000 MHz for both licensed and unlicensed (Qualcomm, Xiaomi, Nokia, Charter)
  Option 3: 2160 MHz for unlicensed and 2000 MHz for licensed (Apple, LGE, Charter, Sony)
  Option 4: Make a decision for unlicensed operation and FFS for licensed operation (Qualcomm)
  Option 5: 2160 MHz for both licensed and unlicensed bands (Ericsson, Sony)
Agreement:
Use Option 1 as starting point
  Further check if there is any issue to use 2000MHz Max CBW to cover unlicensed band.
  If there is issue identified, RAN4 should consider Option 3 and Option 5.
  There is no mandating to following IEEE channelization and there is no alignment requirement following EU C1
Further analyze the max CBW taking the following aspects into account
  The agreed Max CBW needs cover IEEE band
  Reduce the complexity for implementation to support both licensed and unlicensed bands
Notes: Nokia: if going with Option 1, we will lose IEEE.
Charter: we should align with unlicensed.
CATT: we observe some problem for 2160.
ZTE：even if not align with iEEE, there would be no problem.
CMCC: there is no differentiation for licensed and unlicensed bands. In total there is 4GHz bandwidth. 2000 makes more sense.
Apple: we should differentiate between licensed and unlicensed band. Option 3 could work. For licensed band and licsned band, we always have different sets of bandwidth supported.
Samsung: we should align licensed and unlicensed.

## Slide 5: Optionality of UE support of Max. CBW
It is proposed that UE support of the following max. CBW for each SCS is optional, in addition to the agreement that UE support of 480/960kHz SCS is optional:
  120kHz: 400MHz
  480kHz: 1600MHz
  960kHz: 2000MHz and/or 2160MHz
Options:
  Option 1: Yes
  Option 2: No
  Option 3: FFS
Agreement: TBD

## Slide 6: Channelization (Issue 3.2.2)
Issue: Channelization on 52.6 – 71 GHz whether it should be harmonized or separated between license and unlicensed bands.
Options:
  Option 1: Harmonize channelization between licensed and unlicensed bands (Nokia):
    Option 1A: Align with IEEE with fixed channelization (Qualcomm, Charter)
    Option 1B: Do not align with IEEE with fixed channelization (vivo, MTK)
    Option 1C: Do not align with IEEE and floating channelization (Ericsson, ZTE, Huawei)
    Option 1D: CATT, CMCC
      Option 1D-1: Do not align with IEEE with fixed channelization for licensed and no LBT unlicensed bands.
      Option 1D-2: Align with IEEE with fixed channelization for LBT unlicensed bands. Try to harmonize option 1D-2 with option 1D-1 as much as possible.
  Option 2: Separate channelization (Apple, Xiaomi)
    For licensed:
      Option 2A: NR based floating raster (No 802.11ad/ay alignment) (Apple, Xiaomi)
    For unlicensed:
      Option 2B: Align with 802.11ad/ay and no NR channel overlaps with two IEEE channels (Apple, Xiaomi)
Agreement: TBD

## Slide 7: SU for max CBW (Issue 3.2.3-1)
Issue: RAN1 asked SU for max channel bandwidth. While RAN4 needs more time to discuss, RAN1 needs input from RAN4.
Moderator suggestion:
  Option 1:
    For 120 kHz SCS: Keep the same max SU from FR2, i.e., 95 %
    For 480/960 kHz SCS: Provide the SU in range, i.e., [85 – 95] %
  Option 2:
    For 120/480/960 kHz SCS: Provide the SU in range, i.e., [85 – 95] %
Agreement: TBD

## Slide 8: Intra-band contiguous CA within 2/2.16 GHz
Issue: Whether CA is supported for intra-band contiguous within 2/2.16 GHz
Options:
  Option 1: N x 400 MHz, n = [2, 3, 4, 5] (Charter, MTK, CATT, CMCC, Nokia)
    Option 1-A: M x 100 MHz for 120 kHz SCS, M = TBD (Nokia)
  Others:
    Normal CA operation (Ericsson)
    100/200/400 MHz CC based CA (Huawei, Qualcomm)
Agreement: TBD

## Slide 9: CA equal to or larger than 2/2.16 GHz (Issue 3.2.4-2)
Issue: Whether CA is supported for larger than 2/2.16 GHz
Options:
  Option 1: Support CA ≥ 2/2.16 GHz (CMCC, vivo, Nokia, Huawei, Sony)
  Others:
    Normal CA operation (No sub-channelization) (Ericsson)
    No such wide CA capability for handheld UE; Need further discussion for CPE (Qualcomm)
Agreement: TBD

## Slide 10: Intermediate CBWs between Max and Min CBWs (Issue 3.2.1-2)
Issue: Intermediate CBWs between max and min CBWs for each SCS
Moderator proposal: Introduce integer multiples of the minimum CBW for each SCS:
  120 kHz SCS (Min. 100 MHz/Max. 400 MHz): 200 MHz
  480 kHz SCS (Min. 400 MHz/Max. 1600 MHz): 800, 1200 MHz
  960 kHz SCS (Min. 400 MHz/Max. TBD MHz): 800, 1200, 1600 MHz
Agreement: TBD
  One company gave a comment on implementation perspective (e.g., poor FFT effiency) on 1200 MHz for 480 kHz SCS

## Slide 11: Operation Scenario in 60 GHz NR
Issue: Latest approved WID states that NR/NR-U operation in 52.6 – 71 GHz can be in standalone, aggregated via CA or DC with an anchor carrier. Given the unlicensed band in 60 GHz is newly defined, it is necessary to define and finish a single band requirement first.
Agreement: RAN4 aims to finish a single band requirement first. CA/DC can be discussed in parallel.

## Slide 12: Band number (Issue 2.2.1)
Issue: Whether 52.6 – 71 GHz range is to reuse FR2 range, i.e., 257 – 512, or a new range, i.e., 513 – 1024.
Agreement: Reuse the reserved band numbers in FR2 for 60 GHz band

## Slide 13: Regulatory for Unlicensed band (Issue 2.2.2-1)
Issue: Which regulatory requirements will be considered for unlicensed regulation requirements.
Agreement: Consider EN 302 567, EN 303 753, and TR 38.805 (FCC 47 CFR 15.255) for mobile application in unlicensed band.

## Slide 14: ITS band for unlicensed band (Issue 2.2.2-2)
Issue: Whether ITS band for unlicensed band
Agreement: No need to exclude ITS band for unlicensed band

## Slide 15: OTA aspect in 60 GHz
Issue: Whether RAN4 needs to recommend RAN Plenary the need and urgency of studying the UE OTA test method for 52.6 – 71 GHz.
Agreement: Agree to recommend RAN Plenary the need and urgency of studying the UE OTA test method for 52.6 – 71 GHz

## Slide 16: References
R4-2107671, “Summary for [99-e][145] NR_ext_to_71GHz_Part_1,” Intel (moderator), RAN4 #99-e, May 2021