## Slide 1: WF on LTE RRM maintenance all agreements in RAN4#99-e in email thread: [99-e][203] LTE_RRM_maintenance
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #99-e R4-2108215
Electronic Meeting: 19th – 27th May 2021
Agenda Items: 4.2.3, 5.2.2.3, 5.2.1

## Slide 2: RSS based RSRQ measurement Rel-16 eMTC
RAN4 discussed whether to introduce RSS based RSRQ measurement for release 16 eMTC under TEI. Based on the discussions, following options were identified:
  Option 1: RSS based RSRQ shall not be introduced under TEI work for release 16 eMTC.
  Option 2: Adjust applicability requirements in TS 36.133 to enable reuse of existing CRS based RSRQ measurements in case of RSS based RSRP measurement configuration.
  Option 3: Wait for RAN1 conclusion on whether to introduce RSS based RSRQ under TEI work for release 16 eMTC.

## Slide 3: LTE DAPS handover in Even further mobility enhancement
RAN4 discussed further clarification on DL-to-Ul and UL-to-DL switching time as follows:
  Prior to random access procedure autonomous interruption is done in communication towards the target cell as necessary to enable the UE to have sufficient switching time, and after the random access procedure autonomous interruption is done in communication towards source cell as necessary to allow the UE to have sufficient switching time.
Based on the discussions, it was identified that a similar issue is being discussed for NR DAPS handover and it was agreed to reuse the behaviour from that discussions to LTE DAP handover.