## Slide 1: WF on Mandatory Gaps Remaining Issues
Ericsson, Mediatek Inc., Qualcomm
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021
Agenda item: 5.1.3.1
Document for: Approval
R4-210xxxx

## Slide 2: Background
RAN2 has defined the following capabilities for NR only mandatory gaps.
  TS38.306
  TS36.306
supportedGapPattern-NRonly Indicates measurement gap pattern(s) optionally supported by the UE for NR SA and NR-DC when the frequencies to be measured within this measurement gap are all NR frequencies. The leading / leftmost bit (bit 0) corresponds to the gap pattern 2, the next bit corresponds to the gap pattern 3 and so on. The UE shall set the bits corresponding to the measurement gap pattern 2, 3 and 11 to 1. | UE | FD | No | No
supportedGapPattern-NRonly-NEDC Indicates whether the UE supports gap patterns 2, 3 and 11 in NE-DC when the frequencies to be measured within this measurement gap are all NR frequencies. | UE | No | No | No
4.3.6.44 measGapPatterns-NRonly-r16 This field indicates whether the UE supports gap patterns 2, 3 and 11 in LTE standalone when the frequencies to be measured within this measurement gap are all NR frequencies. 4.3.6.45 measGapPatterns-NRonly-ENDC-r16 This field indicates whether the UE supports gap patterns 2, 3 and 11 in (NG)EN-DC when the frequencies to be measured within this measurement gap are all NR frequencies.

## Slide 3: Background
In current RAN2 signaling design,
  the UE will report supportedGapPattern-NRonly bitmap to indicate which gap patterns are supported for NR-only measurements in NR-SA and NR-DC, but
  the UE can only report 1 bit signalling measGapPatterns-NRonly-r16, measGapPatterns-NRonly-ENDC-r16, supportedGapPattern-NRonly-NEDC to indicate gap patterns #2, #3 and #11 in LTE SA, EN-DC and NE-DC.
The UE has different capability signalings for support of NR-only gap patterns in different CA/DC modes.
  Thus, the UE may have to report supporting different NR-only gap patterns in different CA/DC modes while in fact it supports the same gap patterns in these CA/DC modes.

## Slide 4: Open Issues
Whether UE should have the same capability signaling for support of gap patterns for NR-only measurements in different CA/DC mode?
Option 1: Yes
Option 2: No
Does RAN4 need to request the signalling change for NR-only measurements in different CA/DC mode?
Option 1: Keep current 1 bit signalling for LTE SA, EN-DC and NE-DC
Option 2: Change the 1 bit signalling to bitmap for LTE SA, EN-DC and NE-DC