## Slide 1: WF on NR-U RRM Core Requirements all agreements in RAN4#99-e in email thread: [99-e][209] NR_unlic_RRM_1
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #99-e R4-2108253
Electronic Meeting, 19th – 27th May 2021
Agenda Items: 6.1.5

## Slide 2
Agreements from the 1st GTW session
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Availability of SSB occasions for CBD
For CBD, the UE, which is configured in DRX, is not required to determine the availability of SSB occasions more frequent than:
  Once per Max(25ms, P* TSSB) if TDRX ≤ 320ms
  Once per P* TDRX if TDRX > 320ms.

## Slide 4: Availability of SSB occasions for RLM/BFD/L1-RSRP
FFS: whether to consider P factor for RLM/BFD/L1-RSRP

## Slide 5: Interruptions during SCell activation for intra-band CA
Additional relaxations apply for the following conditions
  The scheduled SSB index is the last one in the SSB burst and
  SMTC duration configured by the network includes up-to two candidate positions for the SSB index
  CCA failure happens on both candidate positions
Candidate relaxations:
  Option 1: Extend the length of interruption window
  Option 2: Allow a certain performance degradation
  Option 3: Allow multiple interruptions due to RF tuning
Note: the agreement applies at least for unknown SCell activation case

## Slide 6: Interruptions during SCell activation for inter-band CA with target Cell unknown
Proposals 1: More than one interruptions are allowed on the victim inter-band CCs.
  1a: For inter-band CA where victims on inter-band CCs and intra-band CCs interruptions and target SCell is unknown, more than one interruptions are allowed.
  1b (ZTE Corporation, Ericsson): For scenarios with victims on inter-band CCs and intra-band CCs: more than one interruption can be allowed.
Proposal 2: A single interruption is allowed on the victim inter-band CCs
  2a: A single interruption applies to any victim cell outside the band with the (unknown) SCell being activated, irrespective of whether any intra-band victim cell is present or not and. No further clarification is needed in the spec text.
    No need to consider RF retuning due to DL CCA failures in SCell activation/deactivation requirements.
  2b: A single interruption applies to any victim cell outside the band with the SCell being activated
Proposal 3: Single interruption on the victim inter-band CCs, but allow a certain performance degradation on the active serving cell in the same band with being-activated unknown Scell.

## Slide 7: Interruptions during SCell activation for inter-band CA with target Cell known
Proposal 1: More than one interruptions are allowed on the victim inter-band CCs.
  1a: For inter-band CA where victims on inter-band CCs and intra-band CCs interruptions and when target SCell is known with measurement cycle larger greater than 160 ms, more than one interruptions are allowed.
  1b: For scenarios with victims on inter-band CCs and intra-band CCs: more than one interruption can be allowed.
Proposal 2:
  2a: A single interruption applies to any victim cell outside the band with the (known) SCell being activated, irrespective of whether any intra-band victim cell is present or not and. No further clarification is needed in the spec text.
    No need to consider RF retuning due to DL CCA failures in SCell activation/deactivation requirements.
  2b: A single interruption applies to any victim cell outside the band with the SCell being activated

## Slide 8: Timing: Definition of the reference cell which is not available, with respect to DRX and MGs
In the requirements of clause 7.1.2, the term reference cell on a carrier frequency subject to CCA is not available at the UE refers to when at least one SSB is configured by gNB, but the first two successive candidate SSB positions for the same SSB index within the discovery burst transmission window are not available during at least one discovery burst transmission window, at the UE due to DL CCA failures at gNB during the last X ms; otherwise the reference cell on the carrier frequency subject to CCA is considered as available at the UE.
  X = 1280ms.