## Slide 1: WF on NR-U RRM Core Requirements all agreements in RAN4#99-e in email thread: [99-e][209] NR_unlic_RRM_1
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #99-e R4-2108253
Electronic Meeting, 19th – 27th May 2021
Agenda Items: 6.1.5

## Slide 2
Agreements from the 1st GTW session
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Availability of SSB occasions for CBD
For CBD, the UE, which is configured in DRX, is not required to determine the availability of SSB occasions more frequent than:
  Once per Max(25ms, P* TSSB) if TDRX ≤ 320ms
  Once per P* TDRX if TDRX > 320ms.

## Slide 4: Availability of SSB occasions for RLM/BFD/L1-RSRP
FFS: whether to consider P factor for RLM/BFD/L1-RSRP

## Slide 5: Interruptions requirements during SCell activation
For intra-band and inter-band CA allow single interruption on the victim CCs, but allow performance degradation on the active serving cell in the same band with being-activated unknown SCell and when L3,1 > 0

## Slide 6: Interruptions during SCell activation for inter-band CA with target Cell known
A single interruption applies to any victim cell outside the band with the SCell being activated

## Slide 7: Timing: Definition of the reference cell which is not available, with respect to DRX and MGs
In the requirements of clause 7.1.2, the term reference cell on a carrier frequency subject to CCA is not available at the UE refers to when at least one SSB is configured by gNB, but the first two successive candidate SSB positions for the same SSB index within the discovery burst transmission window are not available during at least one discovery burst transmission window, at the UE due to DL CCA failures at gNB during the last X ms; otherwise the reference cell on the carrier frequency subject to CCA is considered as available at the UE.
  X = 1280ms.